## Slide 1
MRPC飞行时间探测器研制进展
Wang Yi
Department of Engineering Physics, Tsinghua University
yiwang@mail.tsinghua.edu.cn

## Slide 2
Abstract:
  Introduction of PID and MRPC
  Three generation of MRPC-TOF
  STAR-TOF
  CBM-TOF
  SoLID-TOF
Conclusion

## Slide 3
3
Particle identification
Velocity
- Flight time：
- Cherenkov velocity：
- TRD：
dE/dx
Energy -Calorimeter
Detection system of physics experiments
Particle identification by：

## Slide 4
Typical TOF detector
Fast scintillator + PMT (SiPM)
Cherenkov scintillator + MCP
MRPC
MRPC has the advantage of good timing resolution, high detection efficiency and relatively low cost, and is widely used to construct TOF system in modern high energy nuclear physics experiments.

## Slide 5
Drift chamber
Parallel plate
RPC
MRPC
Evolution of timing gas detector

## Slide 6
Application in nuclear physics experiments
Application in industry（Muon tomography)
Application in medicine（TOF-PET）
Standard parameters:
Resistivity of glass: ~1012 Ω.cm
Working gas: 90%Freon+5%iso-butane+5% SF6
Time resolution <100ps
Efficiency >95%
Charge: a few PC
Dark current: a few nA
Noise ~1Hz/cm2
Rate <100 Hz/cm2
Large area, low cost
Read out
Read out
Insulator
Carbon
Insulator
Resistive
plate
MRPC application：
MRPC structure
MRPC introduction

## Slide 7
MRPC performance
Efficiency：
efficiency of single gap：
Weighting field
threshold
Efficiency of N gaps：
Time resolution：

## Slide 8
8
8
MRPC工作气体的选择
1）高电负性 （吸附系数>10-5）
2）在高电场下不易击穿
标准工作气体: C2H2F4 (90%) i-C4H10 (5%) SF6 (5%)
-C2H2F4 (tetrafluorethane): 主要工作气体，电负性
-i-C4H10 (iso-butane): 吸收光子，减少流光
-SF6(sulfur hexafluoride): SF6具备超强的吸附电子能力。吸附电子变成负离子，很容易与正离子结合，活动性变差。
元素的电负性表

## Slide 9
The voltage drop in the gas gap:
Two main ways to improve rate capability:
Reducing bulky resistivity of electrode glass (CBM)
Reducing the avalanche charge (ATLAS)
Other methods:
Reducing the thickness of glass
Warming the detector
The smaller the voltage drop, the higher efficiency and higher rate capability!
How to increase rate of MRPC

## Slide 10
Typical MRPC TOF
RHIC-STAR TOF
Float glass
FAIR-CBM TOF
High rate- low resistive glass
JLab-SoLID TOF
High rate and 20ps resolution

## Slide 11
RHIC-STAR

## Slide 12
STAR-TOF MRPC
12
Long side view

## Slide 13
Glass: ～4×1012.cm
Carbon tape: 500k /
Gas gap: 6×0.22mm
Working gas: 95% F134a+5% iso-butane
Time resolution: 70ps
Efficiency >90%
Rates capability: <100Hz/cm2 !
3cm
6cm
Readout pad
STAR MRPC performance
604个MRPC时间分辨统计图

## Slide 14
14
14
MRPC mass production

## Slide 15
Only TPC:
/k ~0.7 GeV/c,
(,k)/p ~1.1 GeV/c
TOF
e
π
K
p
Only TOF:
 /k ~1.6 GeV/c,
(,k)/p ~ 3.0 GeV/c
TPC
PID of STAR-TOF

## Slide 16
TOF
QGP
Physics results
Nature 473 (2011) 353

## Slide 17
17
SIS100/300
SIS18
HESR
CR
Compressed Baryonic Matter
Super Fragment-Separator:
Nuclear Structure and Astrophysics
Anti-Proton Physics
p-Linac
100 m
FAIR phase 1
FAIR phase 2
Atomic, Plasma, Applied Physics
1012/s; 1.5 GeV/u; 238U28+
1010/s 238U92+ up to 11 (35) GeV/u
3x1013/s 30 (90) GeV protons
radioactive beams up to 1.5 - 2 GeV/u;
1011 antiprotons 1.5 - 15 GeV/c
Primary Beams
Secondary Beams
FAIR – Conceptual View

## Slide 18
18
18
Dipol
magnet
The Compressed Baryonic Matter Experiment
Ring Imaging
Cherenkov
Detector
Transition
Radiation
Detectors
Resistive
Plate
Chambers
(TOF)
Electro-
magnetic
Calorimeter
Silicon
Tracking
Stations
Tracking
Detector
Muon
detection
System
Projectile
Spectator
Detector
(Calorimeter)
Vertex
Detector

## Slide 19
19
19
The structure of CBM-TOF wall
CBM-ToF Requirements
Full system time resolution sT ~ 80 ps
Efficiency > 95 %
Rate capability  30 kHz/cm2
Polar angular range 2.5°– 25°
Occupancy < 5 %
Low power electronics
(~100.000 channels)
Free streaming data acquisition
Au+Au, Center, 10AGeV
Simulated with CBM ROOT

## Slide 20
20
MRPC
2
3
Optic (~50m)
CBM CLK (40MHz)
ToF CLK (160MHz)
MRPC
MRPC
MRPC
ToF SYNC Signal
Counting-Room
CAVE
Example for 192 Channel
Electronics & Readout chain
PADI8
GET4

## Slide 21
21
Development of low resistive glass
Performance of the glass
Glass mass production
Yield >100m2/month
Aging test with X-ray source
Online test system. The efficiency and time resolution can be obtained by cosmic ray while irradiated by X-rays. 0.1C/cm2 charge is accumulated in 35 days.

## Slide 22
Rate: 70kHz/cm2
Time resolution: 40 ps
Rate capability of high rate MRPC
Even though the rate is 70kHz/cm2, the efficiency is still higher than 90% and the time resolution is about 80ps.
Test results at Nuclotron, Dubna，2013

## Slide 23
Prototype design for CBM-TOF
Strip-MRPC
Inner zone-MRPC

## Slide 24
24
24
Glass: low resistive glass
0.7mm thick, 27cm x 25cm
Strip: 27cm x 0.7cm, 0.3cm interval, 24 strips
Gas gap: 8 x 0.25mm, two stacks
Gas box: 600mm x 500mm x 72mm
Design of strip-MRPC for high rate region
Differential strip: 7mm wide+3mm interval
h
w
t
ground
Feed trough: Micro-strip, 50Ω

## Slide 25
Quality assurance of each type of materials and the assembling procedure is recorded.
Detailed information can be found by scanning the QR code on it.
A website is developed to record all the QR information of each produced counter: http://hepd.ep.tsinghua.edu.cn/CBM_TOF/
CBM-TOF MRPC的批量生产

## Slide 26
MRPC setup in the gas box.
PADI 10
PADI power cable
PADI power interface
PADI output
Interface board
HV connector
MRPC3a - 000
MRPC3a - 002
MRPC3a - 003
Layout of cosmic test system

## Slide 27
Noise rate around 1 Hz/cm2
Dut | Ref | BRef/ Sel2 | Eff | Time Resolution/ps | Clustersize Dut | Clustersize Ref | Event number | Calibration mode
009 | 010 | 011 | 0.984 | 92.3 | 1.8 | 1.8 | 6052 | 701001702
009 | 011 | 010 | 0.964 | 89.4 | 1.8 | 1.7 | 6280 | 701002701
010 | 009 | 011 | 0.989 | 100.2 | 1.7 | 1.8 | 3125 | 701701002
010 | 011 | 009 | 0.99 | 99.2 | 1.7 | 1.7 | 4671 | 701702700
011 | 009 | 010 | 0.973 | 91.8 | 1.7 | 1.8 | 5384 | 702701001
011 | 010 | 009 | 0.984 | 95 | 1.7 | 1.7 | 6121 | 702701700

## Slide 28
28
Overview of SoLID
Full exploitation of JLab 12 GeV Upgrade
 A Large Acceptance Detector AND Can Handle High Luminosity (1037-1039)
Take advantage of latest development in detectors , data acquisitions and simulations
Reach ultimate precision for SIDIS (TMDs), PVDIS in high-x region and threshold J/y
5 highly rated experiments approved (+3)
Three SIDIS experiments, one PVDIS, one J/y production (+ three run group experiments)
Strong collaboration (250+ collaborators from 70+ institutes, 13 countries)
Significant international contributions (Chinese collaboration)
Solenoidal Large Intensity Device

## Slide 29
The MRPC is developed for the TOF of SoLID
Main Requirements for TOF:
  /k separation up to 7GeV/c
  Time resolution < 20ps
  Rate capability > 10kHz/cm²
MRPC1
MRPC2
MRPC3
100cm
16cmm
28cm
SoLID-TOF structure
SoLID-TOF super module
SoLID-TOF structure

## Slide 30
30
Two technologies

## Slide 31
应用神经网络方法改进时间分辨

## Slide 32
  Next to do: Development of high rate and high
  time resolution TOF
  Simulation to get : Width of gas gap time resolution
  Development of high rate 15ps resolution MRPC
  Development of 15ps jitter SCA, fast amplifier and TDC
  Impedance match
  Study “ecological” gas mixture for high rate MRPC
Next to do…

## Slide 33
http://fismat.ibero.mx/rpc2018/home
Welcome to RPC2018

## Slide 34
Conclusions
Time of flight system (TOF) based on MRPC technology is widely used and played an important role in modern high energy nuclear physics experiments.
With the increase of accelerator energy and luminosity, many experiments have increasingly demand on the TOF for particle identification to have high resolution TOF under high data rate environment.
New technology such as New material (low resistive glass), New electronics (switched capacitor array (SCA) and precision TDC ) will be used in TOF system.
New gas mixture (ECO-gas ) will also be a big issue in the future!

## Slide 35
Thanks for your attention!