## Slide 1: Manufacture and performance of three 200×200mm² thermal-bonding Micromegas prototypes
Zhiyong Zhang（张志永）, Liang Guan（管亮）, Xiaolian Wang（汪晓莲）, Tianchi Zhao（赵天池）
核探测与核电子学国家重点实验室
中国科学技术大学近代物理系
E-mail: zhzhy@mail.ustc.edu.cn
2014/07/19-07/20

## Slide 2: Outline
Basic principle
Manufacture
Test system
Performance
Summary

## Slide 3
• Basic principle
Y. Giomatnris, et al., MICROMEGAS: a high-granularity position-sensitive gaseous detector for high particle-flux environments, 1996 Nuclear Instruments and Methods in Physics Research A 376 29-35.
Y. Giomatnris, Development and prospects of the new gaseous detector “Micromegas”, 1998 Nuclear Instruments and Methods in Physics Research A 419 239-250
Stainless steel
mesh

## Slide 4
• Manufacture
MicroMesh: 350 LPI woven stainless steel mesh pitch/wire diameter 75/24 μm
tough polyester films with a permanent, dry (hot-melt type) adhesive on both sides
Double avalanche gaps are achieved on both side of the readout PCB.
Compressed air
Stretched mesh
Hot plane
Spacers
Readout PCB
The readout PCB with a Germanium plated layer (0.1-0.5μm thickness, ~2MΩ/口)
Thermal-bonding film spacers and frame are placed on the PCB.
Germanium Plated PCB
» Structure
» Materials
The intrinsic volume resistivity of Ge (house temperature):59ohm.cm

## Slide 5
 | Mm01 | Mm02 | Mm_Ge
Active area (mm²) | 200×200 | 200×200 | 200×200
Number of spacers | 173 | 200 | ~200
Dimension of spacers (mm) | 4 | 3 | 3
Spacer area (%) | 5.43 | 3.53 | 3.85/3.34
Tension of mesh (N/cm) | 19/20 | 19.5/19.5 | 19/20
Bonding time | 70/70 | 69/69 | 65/65
Temperature (up) (oC) | 116/118 | 116/115 | 120/117
Temperature (down) (oC) | 138/132 | 130/130 | 144/139
Pressure (kg) | 125/110 | 124/120 | 119/127
» Bonding condition

## Slide 6
HV test in clean room
After bonding
» Fabrication

## Slide 7
Gas system
DAQ system
NIM crate and HV, logic plug-in board
Mobile scanning platform , x-ray gun, shielding box et.al..
• Test system

## Slide 8
• Setup
Gas Mixture: Ar+CO2(93:7);
Flowing gas mode;
Scanning with a ⁵⁵Fe source and a Cu-target x-ray gun;

## Slide 9
Gas Mixture: Ar+CO2(93:7);
Kalpha: 5.9keV; Kbeta: 6.5keV;
Fitted by triple gauss function + linear noise;
• Performance
» Spectrum of ⁵⁵Fe source (Mm01)

## Slide 10
» Absolute gain (left)
» Energy resolution versus gas gain (⁵⁵Fe source 5.9keV x-rays) (right)

## Slide 11
20cm×20cm active area
⁵⁵Fe source Scan direction:
The gas gain is mainly depend on the avalanche gap，which is determined by the flatness of hot plate, heating time, and pressure etc.
» Gain non-uniformity

## Slide 12
20cm×20cm active area
Cu Kalpha x-rays source scanning (perpendicular to the strips):
Fine scan the active area with a Cu-target x-ray gun in a ~15mm range, about ± 5% non-uniformity is obtained, which will affect less for the spatial resolution, since the cluster size of avalanches is smaller than 1 mm.
» fine scan (Mm02)

## Slide 13
  Signals from preamplifier are digitized and recorded through Digital Oscilloscope for offline analysis
  Pulse shapes are fitted (range: 2~3*rise time) with sigmoid function:
  Signal Amplitude and Rise time are extracted from the fitted function.
  Rise time:
» Pulse analysis
Risetime:110ns

## Slide 14
Cu X-rays tube(8KeV)
source
150-5000μm
100-5000μm
» Rate capability study
collimator
Micromegas
The Germanium layer is around
connected to the ground.

## Slide 15
» Rate capability
T. Alexopoulos, et.al., A spark-resistant bulk-micromegas chamber for high-rate applications, 2011 Nuclear Instruments and Methods in Physics Research A 640 110–118.
The gain versus x-rays rate with different surface resistivity.

## Slide 16
» Stability
Source: 5.9keV x-rays
Operated at a gain of ~9300;
Radiation rate:150Hz

## Slide 17
• Summary
◊ The thermal-bonding method had been developed to manufacture the Micromegas, the manufacture and performance are presented.
◊ High gain and good energy resolution are obtained with the 200×200 mm² prototypes.
◊The rate capability and stability are also studied, further improvements need to be carried out.
Further plan：
■ Try to improve the uniformity efficiency and rate capability of resistant anode chamber.
■ Develop the new structures like PIM, Backplane.
■ Setup a telescope for cosmic test of BGO ECAL of DAMPE, if it is needed.
Thank you!