## Slide 1: Introduction to VMM
Feng Li
State Key Laboratory of Particle Detection and Electronics
Depart of Modern Physics, University of Science & Technology of China
Acknowledgment
Gianluigi De Geronimo
DG Circuits Consulting, Stony Brook University, University of Michigan
Shanghai, CHEP2018

## Slide 2
VMM ASIC family
VMM: ASIC family for ATLAS Muon Spectrometer upgrade (Micromegas and Thin Gap Chamber)
VMM1
AR
  VMM1
  VMM2
  VMM3

## Slide 3
VMM1
An ASIC for Micropattern Detectors

## Slide 4
or
real time address (ART)
peak
time
addr
Architecture of VMM1
direct timing (ToT or TtP)
timing
mux
mux
amplitude
mux
mux
address
logic
CA
shaper
64 channels
dual polarity, adj. gain (0.5, 1, 3, 9 mV/fC) (0.11 to 2 pC), adj. peaktime (25-200 ns)
discriminator with sub-hysteresis and neighboring (channel and chip)
address of first event in real time at dedicated output (ART)
direct timing outputs: time-over-threshold or time-to-peak
peak detector, time detector <1 ns
multiplexing with sparse readout and smart token passing (channel and chip)
threshold and pulse generators, analog monitors, channel mask, temperature sensor, 600mV BGR, 600mV LVDS
power 4.5 mW/ch, size 6 x 8.4 mm², process IBM CMOS 130nm 1.2V
logic
neighbor
CA

## Slide 5
Architecture of VMM2

## Slide 6
Packaging of VMM2
custom BGA package
21 x 21 mm², 400-pin, 1 mm pitch

## Slide 7
Architecture of VMM3

## Slide 9
Packaging of VMM3

## Slide 10
Attenuation Networks (π-Networks)
VDDP
VDDP
PAD
RP2
RP1
CP
RP1  300 kΩ, RP2  300 kΩ
CP  CPAD/2 or 100pF 10V
Attenuation 1/3, can be adjusted
No attenuation → only RP1=100k
VMM3
VDDP
VDDP
STRIP
RS2
RS1
CS
RS1  300 kΩ, RS2  300 kΩ
CS > 100pF 10V
Small attenuation, or none
Beware of inter-strip coupling
No attenuation → only RS1=100k
VMM3
  G. De Geronimo
bias
bias
attenuation CP/(CP+CPAD)
WIRES
(ac-coupled)
RW2
RW1
Cw
RW1  1 MΩ, RW2  300 kΩ
CWG  1nF 10V, CW  200pF 10V
Attenuation 1/6, can be adjusted
CWG keeps wire impedance low
Controlled termination possible
No attenuation → only RW1=300k
VMM3
CWG
grounding
(& termination)
VMM3

## Slide 11: Problem on VMM3
Higher gain, higher baseline
Oscillation observed, probably caused by the π-Networks of FEB channels and the POWER Vddad of VMM3.

## Slide 12: Thanks!

## Slide 13: Path Towards VMM
mixed-signal
2-phase readout
peak and timing
neighboring
sub-hysteresis
few timing outputs
VMM1
2011-12
50 mm²
500k FETs
(8k/ch.)
mixed signal
continuous fully-digital readout
current-output peak detector
increased range of gains
three ADCs per channel
FIFOs, serialized data with DDR
serialized ART with DDR
additional timing modes
64 timing outputs
ITAR
additional functions and fixes
VMM2
2013-14
115 mm²
5M FETs
(80k/ch.)
mixed signal + digital
continuous simultaneous readout
SEU-tolerant logic
deeply revised front-end for TGC
(2nF, 50pC, fast recovery, ...)
L0 handling digital core
SLVS and new config. interface
new reset control and fast reset
timing at threshold
timing ramp optimization
pulser range extension
ART synchronization
32-channel skip
additional functions and fixes
VMM3
2015-16
130 mm²
10M FETs
(160k/ch.)