## Slide 1: Scintillator ECAL Digitization update
2024/04/15
Jiaxuan Wang

## Slide 2: Digitization
Energy Deposition E_Dep
SiPM response N_PE
SiPM saturation correction N_PE_Saturation
ADC calibrated ADC
ADC ADC under HL mode
Energy reconstruction
  0.5 MIP cut
  Dead channel cut
  50MeV && 100 hits cut

## Slide 3: Digitization p.e
Energy deposited in scintillator
Photon emission :
  Of Poisson distribution
PDE :
SiPM saturation :
  Exponential formula
Input : MC truth hit energy
Output: photoelectron number
Process:
  MIP energy : 0.305 MeV
  SiPM gain (ADC/p.e.) and MIP spectrum MPV (ADC/MIP)
  Poisson smear
Input : photoelectron number
Output: photoelectron number(after saturation correction)
Process:
  SiPM type 10um-10000 15um-4489

## Slide 4: Digitization
Input : photoelectron number(after saturation correction)
Output: calibrated ADC value
Process:
  SiPM gain (ADC/p.e.)
  Gaussian smear
    ADC = p.e. * gain
Input : calibrated ADC value
Output: ADC high low gain ADC
Process:
  Gaussian smear :
    Mean : calibrated ADC / Hl-ratio + pedestal mean
    Sigma : pedestal sigma
  High-low switch point
    High gain saturation: high adc > switch point , let highadc =4000
    Low gain saturation : low adc > 3000, let lowadc = 3000
Calibrated ADC : p.e. * gain
  Gain error : fit error
  Single photoelectron spectrum Width : statistical error
ADC converted into high-low gain mode
ADC saturation

## Slide 5: Comparison
Data with low hitNo but high deposited energy according to energy reconstruction
  0.5MIP cut
  Dead channel cut
  50MeV and 100hits cut for 40GeV e- cut
Red: data
Blue: MC_truth
Green: MC_digi
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 6: Layer energy deposition
Data with high energy
Red: data
Blue: MC_truth
Green: MC_digi
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 7: Layer energy deposition
First 16 layers
Layer 14 show different behavior
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 8: Layer energy deposition
Layer No.16-29
Layer 16 show different behavior
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 9: HitNo2Energy
Red: data
Green: MC_digi

## Slide 10: Summary
Basic MC digitization process has been finished
MC digitization has little influence
Still need to improve
  SiPM gain
  Single photoelectron peak width
  Noise model
  Layer 14 && Layer 16 check

## Slide 11: BACKUP

## Slide 12: ADC saturation

## Slide 13: ADC saturation

## Slide 14: SiPM saturation

## Slide 15: SiPM saturation