## Slide 1: Scintillator ECAL Digitization update
2024/04/29
Jiaxuan Wang

## Slide 2: Digitization
Overview
Beam size
  From layer9 layer10
Format
  Same with test beam data
E_Dep
N_photon
N_p.e.
ADC
Photon smear
SiPM
Model
ADC
Convert

## Slide 3: Digitization Step 1
Workflow
  Input : MC truth hit energy
  Output : N_photon
Process
  N_photon
    MIP_E : 0.305 MeV
    SiPM gain (ADC/p.e.)
    MIP MPV (ADC/MIP)
    PDE
  Non-uniformity of light output
    ~4.2%
  Poisson Smear

## Slide 4: Digitization Step 2
Workflow
  Input : N_photon
  Output : N_p.e.
Process
  Pixel placement : 10um-100*100, 15um-67*67
  PDE : 10um-10% 15um-25%
  Crosstalk : 10um-10% 15um-15%
  Avalanche

## Slide 5: Digitization Step 3
Workflow
  Input : N_p.e.
  Output : High-low gain mode ADC
Process
  ADC && gaussian smear
    ADC Mean = N_p.e.* SiPM Gain
    ADC Sigma = 3 * sqrt(N_p.e.)?
  High-low gain mode ADC
  Pedestal fluctuation
  High-low gain saturation
    High gain saturation: high adc > switch point , let high adc =4000
    Low gain saturation : low adc > 3000, let low adc = 3000

## Slide 6: Energy reconstruction
Data sets
  Data : ~100000 40GeV e-
  MC : 100000 40GeV e-/pi-(97.5:2.5)
Restrictions
  Hit cut
    0.8 MIP cut
    Dead channels cut
  Event cut
    50MeV && 100 hits cut

## Slide 7: Comparison
Data: low hitNo but high deposited energy
Digitization:
Red: data
Blue: MC_truth
Green: MC_digi
Red: data
Blue: MC_truth
Green: MC_digi

## Slide 8: Layer energy deposition
First 16 layers

## Slide 9: Layer hitNo
First 16 layers

## Slide 10: Summary && Plan
Summary
  Discrepancy between Data and MC
Plan
  Adjust crosstalk
  Detector material PCB
  SiPM gain error
  …

## Slide 11: BACKUP