## Slide 1
Super Tau-Charm Facility
Conceptual Design of the STCF Detector Superconducting Solenoid Magnet
Presenter: Zhang Xiao Tao
Date: 21st Nov 2024

## Slide 2: Contents of STCF Detector Superconducting Solenoid Magnet
Draft timeline of Detector Superconducting Solenoid Magnet Design
Physical Requirements and Magnetic Field Design
Research and Development of Superconducting Coil
Research and Development of Cryostat
Research and Development of Quench Protection Circuit
Summary and Future Work
Detector Superconducting Solenoid Magnet

## Slide 3: 1. Draft timeline of Detector Superconducting Magnet Design
  CY
  CY
Phase II
Phase II
Today
  STCF Detector Mechanical Design Seminar
  Prepare the project proposal_ Solenoid
  Zhang Xiaotao/LP
  Prepare the STCF DSSM TDR
  DSSM
  Project pre research_ Cable joint and mapping device
  Prepare the STCF Cryogenics TDR
  DSSM
  Zhang Guoqing/ZXT
  Project pre research_ Superconducting Cable
  Zhang Xiaotao/LP
  DSSM
  Lesson learn the relevant chapters of BES III, STCF CDR, CMS TDR.
  Project pre research_ Suspension
Prepare the report for the FTCF workshop in November
  Zhang Xiaotao
Optimization yoke poletip
  Project pre research_ Quench protection and detection circuit
  He Chongchao
  Zhang Xiaotao
  Prepare the project proposal _ Cryogenics
Phase I
  Zhang Xiaotao
  Study of coil cooling
  Chen Zibo
  Liu Ping/ZXT
Detector Superconducting Solenoid Magnet team aligned @Aug.30th.2024
  DSSM

## Slide 4: 2. Physical Requirements and Magnetic Field Design - Comparison of Main Parameters of Superconducting Magnets for ATLAS, CMS, BES III, and STCF Detectors
Detector Superconducting Solenoid Magnet
Name | Parameters | ATLAS | CMS | BESIII | STCF
Cryostat | Inner radius /m | 1.15 | 2.97 | 1.38 | 1.45
 | Outer radius /m | 1.35 | 3.80 | 1.70 | 1.85
 | Length /m | 2.40 | 13.00 | 3.91 | 4.76
Superconducting coil | Nominal diameter/m | 2.46 | 4 layers | 2.95 | 3.10
 | Length /m | 5.30 | 12.48 | 3.52 | 4.00
Conductor size/mm*mm |  | 4.25*30 | 22.3*72 | 3.7*20 | 4.67*15
Electrical performance | Central magnetic field strength /T | 2.00 | 4.00 | 1.00 | 1.00
 | Nominal current /A | 7600 | 19500 | 3150 | 3820
 | Inductance /H | 1.35 | 14.15 | 2.10 | 1.69
 | Energy storage /MJ | 39.00 | 2700.00 | 9.50 | 12.30
 | Cold mass/t | 5.70 | 234.00 | 3.60 | 4.80

## Slide 5: 2. Physical Requirements and Magnetic Field Design - Physical modeling and boundary conditions
Physical Requirements:
  Design value of the central magnetic field : 1.0 T
  Uniformity in the tracking volume ≤ 2%
  Magnetic field measurement accuracy ≤ 0.3%
  Axial leakage magnetic flux ≤ 50Gs@5.1m
Boundary Condition
  End Yoke plates layer: 40, 40, 40, 45, 45, 60, 60, 60, 80, 80, 150 mm respectively
  Barrel Yoke layer: 40, 40, 45, 45, 60, 60, 60, 80, 80, 150 mm respectively
  Yoke octagon innner diameter: 3700 mm
  Yoke total length: 7000 mm
Detector Superconducting Solenoid Magnet
Main parameters of the STCF detector superconducting magnet

## Slide 6: 2. Physical Requirements and Magnetic Field Design - Yoke prototype
Detector Superconducting Solenoid Magnet
Main parameters of the STCF detector
STCF superconducting magnet flux distribution

## Slide 7: 2. Physical Requirements and Magnetic Field Design - Electromagnetic field finite element simulation results (Further optimization required)
Detector Superconducting Solenoid Magnet
STCF detector superconducting magnetic field distribution at tracking area
Distribution of magnetic field along the centerline
The uniformity and magnetic field distribution need further optimization to meet the requirements

## Slide 8: 3. Research and Development of Superconducting Coil - Superconductor, layout structure and parameters of superconducting coil
Detector Superconducting Solenoid Magnet
Conductor paraments | 
rated current | 3820 A
critical current at 4.2 k & 2 T | ≥15000 A
condutor length | 9.15 km
cable dimension | 4.67 mm *15 mm
Rutherford cable paraments | 
number of strands | 16
cable transposition pitch | 100±5 mm
Cu : NbTi | ~1:1
NbTi filament diameter | 30±5 μm
numbe of filaments | ≥600
n value@2T | ≥35
aluminum stabilizer paraments | 
RRR@0t,4.2K | ≥500
Yield strength@4.2k | ≥60MPa
Crosssection ratio of aluminum | >80%
Conceptual structure layout of the solenoid
Cross-sectional view of the superconductor for the STCF detector magnet
Conductor paraments
5083 Aluminum Support Cylinder
1000 RRR Aluminum Strip
He cooling pipe
Superconductor cable

## Slide 9: 4. Research and Development of Cryostat - FEA simulation of preliminary design cryostat
Detector Superconducting Solenoid Magnet
Buckling analysisl（2D 1/2 Model）
Cryostat dimension
Name | Parameter
Inner radius | 1.49m
Outer radius | 1.88m
Length | 4.76m
Inner cylinder thickness | 6mm
Outer cylinder thickness | 16mm
End plate thickness | 32mm
Conclusion: By simulating the buckling analysis of a cryostat using two FEA softwares, the selected dimensions can fully meet the design requirements.

## Slide 10: 4. Research and Development of Cryostat - STCF detector cryogenics sketch map and heat load estimation
Detector Superconducting Solenoid Magnet
Items of Heat Load | 77 K | 4.5 K
Caused by the support rods in cryostat | 26.527 W | 1.038 W
Caused by the radiation in cryostat | 73.801 W | 3.236 W
Caused by the current leads | —— | 7.920 W + 0.421 g/s
Caused by the radiation in chimney & SP | 10.025 W | 0.407 W
Caused by the support rods in chimney & SP | 3.900 W | 0.022 W
Caused by the bayonet and valves in SP | 46.000 W | 13.000 W
Caused by the measuring wires | 5.311 W | 0.831 W
Total | 165.5 W | 26.46 W + 0.421g/s
Adopted heat load（×1.5） | 248 W | 39.7 W + 0.63 g/s
Heat load estimation
STCF detector cryogenics sketch map
Preliminary plan: The 4.5K cold mass is cooled using thermosiphon liquid helium, while the 77K shield is cooled using forced flow liquid nitrogen.

## Slide 11: 5. Research and Development of Quench Protection Circuit - Multi-sectioned quench process circuit(Further discussion)
Schematic of multi-sectioned quench process circuit
Conclusion: The external resistance of quench is inversely proportional to the current decay time and inversely proportional to the induced potential.
1- Power supply; 2-Cold resistor; 3-Cold diode; 4- Coil; 5-Hoop cylinder

## Slide 12: 6. Summary and Future Work - Future work plan
Research and development of superconductor
FEA simulation of two different cooling methods (forced cooling and thermosiphon)
Optimization of the yoke poletip, including the field shape of the magnetic field uniformity in the tracking volume area
Thermal leakage analysis of suspension
Design and numerical calculation of quenching protection circuit

## Slide 13
Thank you for your attention

## Slide 14: Backup information

## Slide 15: Backup information

## Slide 16: Backup information