## Slide 1
The RF Techniques of STCF
Yelong Wei
on behalf of Ring RF system
2024.11.20

## Slide 2: Outline
2 Technique Route
1 Background & Introduction
3 TM020-mode Cavity Design
4 Summary

## Slide 3: STCF Ring RF System
One of the most serious issue is that large beam currents to excite fast-growing longitudinal coupled-bunch instabilities (CBI) caused by the accelerating mode of detuned RF cavities which is needed to compensate for the reactive component of beam-loading.
The other issue is to minimize the cavity higher-order mode (HOM) impedances which drive strong longitudinal and transverse CBI and bring the induced HOM power.
RF system
RF Cavities
RF Power Source
Low-level RF System
Super Tau-Charm Facility Ring RF system

## Slide 4: STCF Collider Ring
 | Values |  |  | 
Beam Energy [GeV] | 1.0 | 1.5 | 2.0 | 3.5
Circumference [m] | 865.398 |  |  | 
Revolution frequency [kHz] | 346.42 |  |  | 
RF Frequency [MHz] | 499.7 |  |  | 
Harmonic Number | 1442 |  |  | 
Number of Bunches | 692 |  |  | 
Beam Current [A] | 1.5 | 2 | 1.7 | 2
Momentum Compaction Factor | 13.04×10-4 | 13.65×10-4 | 13.86×10-4 | 14.14×10-4
Energy Loss per Turn [keV] | 105.9 | 265.9 | 541 | 1477
Beam SR Power [kW] | 159 | 452 | 1082 | 2954
RF Voltage [MV] | 1 | 2 | 3 | 6
Synchronous phase [°] | 174 | 172 | 170 | 166
Considering damping ring has a low beam current, so the RF system can be developed for both damping and collider ring.
Key parameters for RF systems：
Frequency: 499.7 MHz ；
Single collider ring provides a voltage of 6 MV and a beam power of 3 MW

## Slide 5: Outline
2 Technique Route
1 Background & Introduction
3 TM020-mode Cavity Design
4 Summary

## Slide 6: Superconducting VS Normal-conducting
 | Superconducting cavity [SC] | Normal-conducting cavity [NC]
HOM damping | Simple | Complicated
Accelerating Voltage | High（~2.0MV） | Low（~0.5MV）
Module Length | Long（3-3.5 meter） | Short（~0.5 meter）
Robust | Complicated for Commissioning | Easy for Commissioning
Maintenance | Cryogenic system requires special attention | Easy
Economic | High construction budget | Low construction budget
3.5m
0.5m
[1]T. Huang, W. Pan, G. Wang，et al., The development of the 499.8MHz superconducting cavity system for BEPCII. Nucl. Instrum.Methods Phys. Res. Sect. A 1013, 165649 (2021).
[2]E. Weihreter, F. Marhauser, HOM damped cavities for high brilliance synchrotron light sources, in: Brilliant Light in Life and Material Sciences, Springer, Dordrecht, 2007, pp. 413–42

## Slide 7: RF Systems for Different Colliders
Colliders | Cavity Types | 
PEP-II | NC（20 NC for electron ring, 6 NC for positron ring） | Closed-off at 1998
BEPCII | SC（1 SC for each ring） | Commissioning
SuperKEKB | SC+NC（8 NC and 8 SC for electron ring，32 NC for positron ring） | Commissioning
BINP-SCTF | NC（3 NC for each ring） | Under Design
NC is more advantageous in terms of easy maintenance, running robust, low construction budget.

## Slide 8: STCF Ring RF System
 | KEKB SC | BEPCII SC | ARES NC(KEKB) | TM020 NC | PEP-II NC | BESSY-II NC
Beam power [kW] | 3000 | 3000 | 3000 | 3000 | 3000 | 3000
Voltage [kV] | 6000 | 6000 | 6000 | 6000 | 6000 | 6000
Number of cavities | 10 | 20 | 10 | 12 | 15 | 30
Voltage per cavity [kV] | 600 | 300 | 600 | 500 | 400 | 200
Shunt impedance per cavity –circuit Ω | 46.5E9 | 46.5E9 | 8.625E5 | 2.85E6 | 3.5E6 | 3.4E6
Unloaded quality factor | 1E9 | 1E9 | 1.15E5 | 6.0E4 | 3E4 | 2.96E4
Power poss per cavity [kW] | 0.00387 | 0.00097 | 209 | 44 | 23 | 6
Beam power per cavity [kW] | 300 | 150 | 300 | 250 | 200 | 100
Input power per cavity [kW] | 300 | 150 | 509 | 294 | 223 | 106
Detuning frequency per cavity [kHz] | 75 | 150 | 12 | 92 | 283 | 557
SC is disadvantageous due to relative lower accelerating voltage required
NC RF systems are chosen as a candidate for our STCF collider rings。

## Slide 9: Different NC Cavities Worldwide
 | f0 [MHz] | Ra [MΩ] | R/Q [Ω] | Q0 | Voltage per cavity [kV] | Input power per cavity
KEK-PF | 509 | 7.68 | 174.5 | 44,000 | ＜500 | ＜ 150 kW
KEK-ARES | 509 | 1.725 | 15 | 115000 | < 850 | 750 kW = 150 kW+600 kW
PEP-II | 476 | 7.6 | 234.6 | 32,400 | ＜850 | 320 kW = 70 kW+250 kW
BESSY-II | 500 | 6.8 | 229.7 | 29,600 | ＜500 | ＜ 150 kW
KEK-RIKEN TM020 | 509 | 6.8 | 113 | 60,000 | ＜800 | > 200 kW
KEK-PF does not heavily damping HOMs
BESSY-II and PEP-II strongly damping HOMs，but with complicated mechanical design
ARES comprises of storage, coupling and accelerating cavities，but with complicated mechanical design
TM020 are advantageous in terms of compact and simple HOM damping
TM020 has a low R/Q，which is beneficial for suppressing CBI caused by accelerating mode

## Slide 10: TM020-mode NC Cavity from KEK and RIKEN
RF Parameters | 
Working mode | TM020
Working frequency | 509 MHz
Unloaded quality factor | 60000
Shunt impedance | 6.8 MΩ
Voltage per cavity | 825 kV
Power per cavity | 100 kW（no beam） 210 kW（400 mA）
RF Parameters | 
Working mode | TM020
Working frequency | 509 MHz
 | 60000
 | 6.8 MΩ
Voltage per cavity | 825 kV
Power per cavity | 100 kW（no beam） 210 kW（400 mA）

## Slide 11: Technique Route Selected for STCF
 | KEKB SC | BEPCII SC | ARES NC(KEKB设计) | TM020 NC | PEP-II NC | BESSY-II NC
Beam power [kW] | 3000 | 3000 | 3000 | 3000 | 3000 | 3000
Voltage [kV] | 6000 | 6000 | 6000 | 6000 | 6000 | 6000
Number of cavities | 10 | 20 | 10 | 12 | 15 | 30
Voltage per cavity [kV] | 600 | 300 | 600 | 500 | 400 | 200
Shunt impedance per cavity –circuit Ω | 46.5E9 | 46.5E9 | 8.625E5 | 2.85E6 | 3.5E6 | 3.4E6
Unloaded quality factor | 1E9 | 1E9 | 1.15E5 | 6.0E4 | 3E4 | 2.96E4
Power poss per cavity [kW] | 0.00387 | 0.00097 | 209 | 44 | 23 | 6
Beam power per cavity [kW] | 300 | 150 | 300 | 250 | 200 | 100
Input power per cavity [kW] | 300 | 150 | 509 | 294 | 223 | 106
Detuning frequency per cavity [kHz] | 75 | 150 | 12 | 92 | 283 | 557

## Slide 12: Outline
2 Technique Route
1 Background & Introduction
3 TM020-mode Cavity Design
4 Summary

## Slide 13: Cavity Geometry
Location d

## Slide 14: Optimized TM020-mode cavity
RF parameters | 
Working mode | TM020
Frequency [MHz] | 499.7
R/Q [Ω] | 109
Unloaded quality factor | 61500
 | 3.79
[mA/V] | 3.17
RF parameters | 
Working mode | TM020
Frequency [MHz] | 499.7
R/Q [Ω] | 109
Unloaded quality factor | 61500
 | 3.79
 | 3.17
Magnetic fields
Electric fields

## Slide 15: HOM damping-Transverse modes
Simulated dampers
Realistic dampers

## Slide 16: HOM damping-Longitudinal modes
Simulated dampers
Realistic dampers
Mode | Frequency(GHz) | Rz(Ω)
TM021 | 0.76637 | 344.36
TM031 | 0.98353 | 581.11
TM033 | 1.88010 | 406.97

## Slide 17: Thermal Analysis for Cavity
Cooling system
Including pumping vacuum
  Pumping vacuum has little effect
  50 kW power dissipation on the cavity surface
  Max stress：Coupling port，65.885 MPa
  Max deformation：Equator outer，0.10285mm
  Frequency shift：-100.8KHz
Temperature
Deformation
Stress

## Slide 18: Input Power Coupler
Design Target
  499.7 MHz TM020-mode cavity
  Waveguide-type input coupler，online tuning。
Working frequency | 499.7 MHz
Type | Waveguide type
Power capacity | CW 200 kW
Design coupling factor | 1.0
Coupling factor | 1~8
Coupling type | Magnetic Coupling
Vacuum leakage rate | <1e-10 mbar·l/s
Ultimate vacuum | <5e-7 Pa
Mode | Frequency | Q0
TM020 | 499.70 MHz | 61500
Electric fields
On-axis electric fields

## Slide 19: Two types of input coupler
Coupler types
  Coaxial type：
    Complicated
    Fixed coupling factor, have large reflections for different beam currents
  Waveguide type：
    Simple geometry
    Variable online tuning for different beam currents
    High construction budget。
  After comparisons, we choose waveguide type input coupler

## Slide 20: RF Design
Coupling port
  Increasing the fillets to minimize the magnetic fields
  Tuning range：Tuner insertion depth 3~63mm→0.9975~8
  Frequency shift：-0.1564MHz
  58kW→748kV
Coupling port
垂直耦合口方向Electric fields distribution
Coupling factor as a function of insertion depth of Tuner

## Slide 21: MP for Coupling Port
  MP for coupling port only：
    No oscillating，the number of particles decreases with time
  For an input power：0~200kW，No MP occur
Particles distribution at 10kW@40ns
Input power （kW）
SEY
At 200kW，the number of paticles decreases with time

## Slide 22: Bending Waveguide RF Design
Bending waveguide
  90° bending waveguide for connection between port and
  ceramic windows
    S11：499.7MHz@-94.656dB
    Low electromagnetic fields，low BDR
EM fields
Optimized S11
Mechanical modelling

## Slide 23: RF Design for Ceramic Window
Ceramic Window
  99.5% Ceramic Window：aluminium oxide
    Low loss tangent，low temperature，low BDR
    No difficulty in welding，there are some existing experience
  S11：499.7MHz@-66.921dB
  WR1800 waveguide
Ceramic window geometry
Electric fields
Magnetic fields
Optimized S11

## Slide 24: MP for Ceramic Window
  MP is a key issue for ceramic window。
  At an input power of 0~200kW，SEY<1，No MP occur
Electric Fields at 230kW
At 230kW, the number of particles decreases with time
Input power （kW）
SEY
SEY
Input power of 230kW

## Slide 25: RF Design for Stepped Waveguides
WR1800 to HFWR1800 converter
  Stepped waveguides：
    Material：Aluminum alloy
    Bandwidths：S11：499.7MHz@-71.638dB, -30dB@38.61MHz
    Input power = 200kW，Emax<0.1 MV/m, much lower than breakdown
Modelling and electric fields
Optimized S11

## Slide 26
Final Input coupler connected with WR1800 waveguides

## Slide 27: Thermal Analysis for Coupling Port
Coupling Port
  Conditions：Using Four-way water cooling surrounds the coupling port
  Position at Short edge for coupling port，Max Temperature： 39.9℃
  Max thermal stress：12MPa
  Max thermal deformation ：0.0181mm
CW 200kW thermal distribution
Deformation
Stress
Each cooling has a flow velocity 10L/min，pressure ≥0.4MPa

## Slide 28: Thermal Analysis for Waveguides
Bending and Stepped waveguides
  No wind required
  Stepped waveguide：CW 200kW，Max Tem 10.48℃
  Bending waveguide：
    Deformation results from the pumping vacuum
    Deformation positions at waveguide wide edge
    Finally we choose a waveguide with a thickness of 15mm*10mm
    Max deformation 0.2mm，Max stress 71.22MPa，meet the requirements
CW 200kW temperature
机械及抽真空时，弯波导变形及应力随波导宽边厚度变化
应力
变形
CW 200kW Temperature
CW 200 kW deformation
CW 200kW stress

## Slide 29: Thermal Analysis for Ceramic Window
Ceramic purity
  Cooling enough：
    97% max Temperature: 76.28℃，99.5% max temperature: 47.348℃
  After comparisons, 99.5% Ceramic is chosen for our window
97%（Left）及99.5%（Right）Volume Loss
99.5% thermal
97% thermal

## Slide 30
Thermal analysis
  Cooling system: 6 L/min surrounding the ceramic window
    Max deformation: 0.019175mm
    Max stress: 41.593Mpa
Deformation and stress
Stress for copper and ceramic window
Modelling
Meet the requirements

## Slide 31: Mechanical Design for Whole Module
2491.5mm
2946mm
739mm

## Slide 32: Summary & Outlook
We have chosen a NC 499.7MHz TM020-mode cavity with strong HOM damping for our STCF collider rings; further optimizations are required on heavily damping to meet the requirement of 2 A, 3.5 GeV.
RF design and preliminary mechanical design on this TM020-mode cavity have been completed；
The fabrication is planned to be completed by the end of 2025.