## Slide 1: Implementation of MicroTCA Based Low-level RF Systems
2024.09.18

## Slide 2
CONTENT
1
Introduction
2
3
4
MTCA.4 LLRF
System Hardware
FPGA Framework & Software Implementation
Summary

## Slide 3: LLRF Introduction
01

## Slide 4: LLRF System
Basic requirements:
Cavity Field Control (RF loops)
Cavity Resonance Control (frequency loops)
Additional requirements:
High speed data acquisition
Built-in system diagnosis
Automation commission
Exception handling procedures
Low Level Radio Frequency
Regulates the amplitude and the phase of the accelerating voltage inside a RF cavity is essential to ensure the stable operation of charged particle accelerator

## Slide 5: Digital LLRF System Types
LLRF Testing at the FNAL CMTS
“Pizza box”
19-inch modules
Individually developed and built hardware
Crate-based systems
Of-the-shelf components
Highly modularity and scalability
MicroTCA LLRF at the XFEL

## Slide 6: Motivation for MicroTCA.4
Limitations of VME/CPCI/PXI:
Low bus bandwidth
Lack of support for serial fabrics
Insufficient intelligent control support
Evolved from ATCA/MTCA
Modern, high-speed data transfer
Redundant fans/power supply
Intelligent platform management
Excellent signal quality
Internal clock & trigger distribution
Requirements in the High-Energy Physics
High data rate
Scalable modular system
Shelf management and monitoring
Redundancy
Hot swap capability

## Slide 7: MTCA.4 LLRF System Hardware
03

## Slide 8: MTCA.4 LLRF: Overview
Power Supply
MicroTCA Carrier Hub
Processor
Board
AMC
Boards
RTM
Boards
Redundant
PSU & MCH
RF interface, I/O extension
In-house development or COTS
ADC, DAC, FPGA
Mostly COTS

## Slide 9: Chassis selection
1U Chassis
• Integrated eMCH
• 2-slot Double Mid-Size AMC w/ RTM
• 2-slot Single Mid-Size AMC
• Integrated PSU
3U Chassis
• 4-slot Double Mid-Size AMC w/ RTM
• 1-slot Double Mid-size AMC
• 1-slot Double Full-size MCH
• 2 Double Full-size PM
9U Chassis
• 12-slot Double Mid-Size AMC
slots w/ RTM
• 2-slot Double Full-size MCH w/ RTM
• 4 Double Full-size PM
2U Chassis
• 5-slot Double Mid-Size AMC w/ RTM
• 1-slot Double Full-size AMC
• 1-slot Double Full-size MCH w/ RTM
• 1 Double Full-size PM

## Slide 10: Backplane Connections
MLVDS
Shared between all slots
Triggers, interlocks, clocks, ...
Usually one transmitter and multiple receivers
Example: interlock and trigger interconnect between digitizer, EVR or interlock board
mTCA-EVR-300U
SIS8300L2
DAMC2
Timing
Trigger
MPS Interlock

## Slide 11: Backplane Connections
Processing Board
Digitizer
FMC Carrier
Data
Processing
Cavity
Tunning
Point-to-point links
Direct communication between boards, used for data aggregation
Protocol selection up to application: Aurora, 8b/10b, (10)G Ethernet
Example: Data exchange between master-slave digitizer for multi-cavity LLRF control, superconducting cavity with resonance controller

## Slide 12: Backplane Connections
Gigabit Ethernet
1000BASE-KX
TX and RX diff pair at 1.25 Gbps
Examples: Ethernet interface of Zynq-based boards, UDP transceiver on FPGA
PCI Express
Gen 3 (8 GT/s), x4 (x8 in special crates) choice for many apps
Native support for PCI Express 5.0 in the future
Other protocols available (SRIO, 10/40Gb Ethernet )
PCIe Switch
ETH Switch

## Slide 13: Computing Module
PCIe interface card
NAT-PHYS80 MCH
optical uplink
PCIe interface card for operation in PCs / servers
Optical PCIe Gen3 x8/x16 uplink
Obtaining higher computing and storage performance at a lower cost
CPU module inside of crate
Processor performance limited by 80 W per slot power limit
Easy to operate and maintain

## Slide 14: AMC & RTM Selection
Many AMCs and RTMs available on the market, LLRF system needs to make appropriate choices based on the system architecture and operating frequency band

## Slide 15: Direct Sampling Schemes with RTM
Direct Sampling RTM
DC to 400 MHz DS front-end
Latest generation of RF sampling ADCs digitize signals at frequency up to several GHz, which makes it possible to sample RF signal directly
Direct-sampling architecture provides flexibility and simplification for LLRF
AMC Digitizer
10 channel 125MHz/16Bit digitizer

## Slide 16: Direct Sampling Schemes with AMC Carrier
FMC Card
Carrier AMC
Dual HPC FMC Carrier
High frequency analog signal transfer over Zone3 can leads to crosstalk between the differential channels
Get rid of Zone 3 analog bandwidth limitations using carrier + FMC
Many COTS components for GSPS ADC and DAC

## Slide 17: Other Direct Sampling Schemes
High sampling rate digitizer using single-ended analog RTM connection (Class RF1.0)
Zynq RF-SoC digitizer: highly integrated, more flexible, lower latency
MMC-TRX02-B RF-SoC
12bit, Sampling: 4GSPS, Bandwidth: 4GHz, Channels: 8ch
AMC576 RF-SoC
16 ADC (12-bit @ 2 GSPS) and 16 DAC (14-bit @ 6.4 GSPS)
DAMC-DS812ZUP
8 channels, 800 MSPS, 12 bit digitizer

## Slide 18: Down-conversion Schemes
RTM Front-end
500MHz to 6GHz Down/VM converter
LO & Clock
Generator
For L, S, C band LLRF, RF signal is typically down-converted in RTM front-end
For higher frequency (X-band) LLRF, conversion between X, S or C out of crate may required
AMC Digitizer
10 channel 125MHz/16Bit digitizer

## Slide 19: Down-conversion Schemes with RF Backplane
DRTM-LOG1300
eRTM-508MHz
Candox Systems, Inc.
RF backplane introduced in MicroTCA 4.1
Extra slots for RF/clock signal generation and distribution modules, Supports up to 3 extended RTMs (RTMs without AMC)
Up to 2 power supply RTMs with low-noise, separated, analog, bipolar power distribution
RF signal distribution over backplane, eliminates RF coaxial cable, more compact system, improves reliability

## Slide 20: Cavity Tuning
Piezo RTM
DRTM-PZT4
2 independent channels operation(0 to +200V)
Operation as an actuator or a sensor
Motor control

## Slide 21: FPGA Framework and Software Implementation
03

## Slide 22: FPGA Framework
BSP
PCIe、DMA、DDR, configuration of peripherals on the board (clocks, I/O buffers, ADCs, DACs, etc.)
APP
User specific algorithms（LLRF control , DAQ logic, etc. ）
DAQ Requirements:
Multi-channel
Pulse/continuous mode
Cross clock domain
Timestamp
Down sampling
Configurable data width
Interrupt
…

## Slide 23: Typical PCIe block design
Xilinx XDMA is provided as an option to transfer data between the FPGA and the instance's CPU memory
Open-source driver
Easy to install and use, and does not require driver development expertise to use
Support multiple channels per FPGA for high performance
DAQ Stream Input
DMA (S2MM)
MIG
XDMA
Register Access

## Slide 24: XDMA Device Driver
Official Driver:
https://github.com/Xilinx/dma_ip_drivers
Driver Customization:
Board startup configuration support
Crate slot mapping
Driver installation script
Udev rules and dkms support for the Xilinx XDMA driver，example：
https://github.com/MicroTCA-Tech-Lab/xdma-metapackage
User space character device structure :
C2H: AXI4 port (DMA from device)
H2C: AXI4 port (DMA to device)
Register: AXI4-Lite port

## Slide 25: Typical processing system block design
PS
AXI DMA
Interrupt Controller
DAQ Stream Input
Register Access
Typically involves integrating a Processing System IP with DMA, peripherals, memory, or programmable logic in a block design environment
Capable of implementing an embedded EPICS IOC for control and data access via Ethernet

## Slide 26: User Space Driver
Linux kernel driver for the general purpose DMA
Xilinx provides "DMA proxy" kernel driver
https://www.xilinx.com/video/soc/linux-dma-from-user-space.html
https://github.com/Xilinx-Wiki-Projects/software-prototypes/tree/master/linux-user-space-dma
The drivers use the Linux DMA Engine subsystem and provide the ability for user to write their own Linux driver which uses the Xilinx driver in kernel space through the DMA Engine subsystem
Other open source driver:
A zero-copy, high-bandwidth Linux driver and user space interface library for Xilinx's AXI DMA and VDMA IP blocks:
https://github.com/bperez77/xilinx_axidma
Linux Driver for the Zynq FPGA DMA engine
https://github.com/bmartini/zynq-xdma

## Slide 27: User Space Driver
User space application/driver through the UIO framework
Add the UIO driver to the kernel
Setup IP core in the device tree to use the UIO driver
Develop API to access IP cores via UIO device
Add access to memory:
  reserved memory region in device tree
  u-dma-buf kernel driver: https://github.com/ikwzm/udmabuf
Control AXI DMA engine read from/write to memory space
Example: libudmaio from MTCA Tech Lab
https://github.com/MicroTCA-Tech-Lab/libudmaio
Simplify the use of the Xilinx AXI DMA controller when used in S2MM (Stream to Memory-Mapped) mode
Over PCIe with xdma driver
From ARM over the Userspace I/O
Register Interface
DMA Controller
S2MM for example
Clear IRQs (S2MM_DMASR)
Set config (S2MM_DMACR)
Set Dst mem address (S2MM_DA)
Set length (S2MM_LENGTH)

## Slide 28: EPICS Integration
Build EPICS application
Develop device support using XDMA API or user space API
  Board initialization / configuration
  Wrapper for register r/w and DMA r/w
Re-write db record (ai/ao, li/lo, waveform, interrupt…) using device support
Develop complete EPICS IOC and OPI

## Slide 29: Summary
04

## Slide 30: Summary
MicroTCA is widely used in accelerators because it offers high performance, modular design, cost-effectiveness and reliability. It also provides quick deployment and is supported by a wide community
A relatively standardized MicroTCA.4 LLRF architecture has now been formed. Simplify system development, enables hardware reusability, reduces redundant development, and reduce costs
Xilinx provides a variety of mature IP cores, along with numerous open-source drivers and software, making high-speed data transmission very easy.

## Slide 31: Thank you for your attention!