## Slide 1
Simulation Study of Imaging Widgets with CSNS Muon Beam
Hu Jifeng (胡继峰)
South China Normal University
CSNS

## Slide 2: 物质尺度与观测装置
北京正负电子对撞机
CERN大型强子对撞机
European XFEL
上海同步辐射光源
天眼
哈勃望远镜
这里仅以部分大型装置为例
上海光源

## Slide 3: Muon as a natural probe
A fundamental particle, a lepton of the 2nd generation, 200 times heavier than electron.
Discovered in 1936 by Carl D.Anderson and Seth Neddermeyer. Twenty years later, muography was developed.
Science: an important probe in searching for new physics beyond the standard model
Technology: a novel probe to imaging objects of high density since its strong penetration power, as a distinctive method compared to other radiography: xCT, MRI, pCT, PET ...
Standard Model - Wikipedia

## Slide 4: Muon passing through matter
https://pdg.lbl.gov/
pair production, bremsstrahlung, and photonuclear interaction.
ionization energy loss
Critical energy determines how muons lose their energy in matter by what kinds of interaction.
Unlike cosmic rays, at CSNS the momentum of muon+ beam is small, thus ionization energy loss dominates.
critical energy
CSNS

## Slide 5: Imaging with cosmic muons (muography)
https://cds.cern.ch/images/CMS-PHO-GEN-2017-008-1
Primary cosmic rays 99% are hydrogen and helium nuclei from the sun.
Sea-level cosmic rays. At sea level most of the surviving rays are muons (μ) since their long lifetime (τ=2.2μs).
Advantages: rich production in nature, low cost, suitable for large volumes where physical access is not possible, such as ancient buildings, volcanoes , nuclear reactors, or deep underground (water).
At Earth’s surface, muon rate ~ 10000 per square meter per minute!
Decay length @ vacuum
Progress in muon tomography/EPS-2017
Notes: 添加右侧2图的引用

## Slide 6: From cosmic muons to beam muons
https://cds.cern.ch/images/CMS-PHO-GEN-2017-008-1
Advantages: rich production in nature, low cost, suitable for large volumes where physical access is not possible, such as ancient buildings, volcanoes , nuclear reactors, or deep underground (water).
simulation
Advantages: fast, real-time, and high precision imaging, and so on.
Lot of developments recent years by many research groups.
Nuclear Inst. and Methods in Physics Research, A 1015 (2021) 165768
Notes: Nuclear Inst. and Methods in Physics Research, A 1015 (2021) 165768

## Slide 7: Imaging widgets with CSNS μ+ beam
We would like to answer the following questions:
  what kinds of objects (shape, material) are applicable ? ranges of density and thickness.
  requirements on detector performance ? (position, momentum and energy resolutions)
  technical solutions for a μCT prototype construction. (gas-based, silicon, scintillator, crystal ...)
Notes: 需要重新梳理文字

## Slide 8: Simulation setup
Back Detector
Tracker
Range detector
Timing detector
Purpose:
Outgoing position (xf)
Outgoing energy (Ef)
A run consists of 107 events, a collection of (xi, pi, xf, pf) records for next analysis. Either parallel beam or cone beam is fine.
Y-Z view
Distance detector to source 40 cm
Distance target to source 20 cm
8x8 cm2
target
Cu
Ca
Muon beam
parallel
8x8 cm2
107 muons
Front Tracker
Tracker
Purpose:
Ingoing position (xi)
Ingoing energy (Ei)
Notes: 几何信息需要添加
μ 子探测技术方案(闪烁体探测器、核乳胶探测器、气体 探测器、切伦科夫探测器等)

## Slide 9: Muon scattering tomography
Energy loss
matter density and thickness following Bethe equation.
𝐸𝐿≅𝐸_𝑓−𝐸_𝑖∝𝜌ℎ, matter density and thickness following Bethe equation.
A better decoding can be achieved with normalized EL .
Energy loss
https://pdg.lbl.gov/
Ei
Ef
θ0
pi
pf
Scattering angle
, radiation length which links to matter density and thickness.
𝑆𝐴∝1/√(𝑋_0 ), radiation length which links to matter density and thickness.
Scattering angle
Notes: 检查pdg 关于 x0的表达

## Slide 10: dE/dx validation through air
30 MeV
40 MeV
50 MeV
4 MeV
10 MeV
20 MeV
Well agreements within kinetic energy range of CSNS beam
CSNS
30 MeV
40 MeV
50 MeV
4 MeV
10 MeV
20 MeV
80 MeV
200 MeV
Sampling 8 kinetic energies within air.

## Slide 11: Penetration power (Flux Efficiency)
107 events, continuous energy spectrum ranging from 30 MeV to 60 MeV

## Slide 12: Flux image with mu+ beam (Muograph)
Beam parameters |  | Beam parameters | 
Kinetic energy | 4 MeV, 50 MeV | Energy spread | ~2 keV
Integrated flux | 107 mu+ (100~1000 s) | Coverage area | 8x8 cm2
Direction | Z | Emittance diversity | degree level
Air background
Air background
cm
cm

## Slide 13: Flux image with 8 kinetic energies

## Slide 14: Flux image (low-energy-loss pass filter)
ΔE < 1.5 MeV

## Slide 15: Ionization energy loss spectrum
Two bumps reveal two different thickness in the coin.
Normalized energy loss with air
Energy loss

## Slide 16: MST Image using the EL method

## Slide 17: MST Image using the SA method

## Slide 18: MST images (ideal cases)

## Slide 19: Comparison to X Image (copper coin)

## Slide 20: Comparison to X Image (gold coin)
Xray 120 keV
does NOT work
Muon+ 30-60 MeV
muography
Muon+ 30-60 MeV
MST

## Slide 21: Comparison to X Image (chin)

## Slide 22: From 2D to 3D (parallel beam scan)
107 μ
1010 X

## Slide 23: Projections and Density Spectrums

## Slide 24: Reconstruction versus Original Phantom
xCT
μCT
The 82th slice reconstructed among 308 slices.
More quantitative measurements are under goging.

## Slide 25: Summary and Outlook
We currently investigate some widgets, for example, a copper coin and a chin. We notice that, these results are obtained at an ideal case.
MST require a high performance spectrometer, tracker and range detectors are minimum.
Compared to XCT, 3D reconstruction needs be improved.
In future
  Investigate more uncertainties.
Thanks for your attention!

## Slide 26: Developments in past decades
Early attempt: 1956, rock density with Geiger counter, without imaging (Australian)
First muograph: 1970, imaging Pyramid of Khafre (American)
Development: 2007, imaging active volcano (Japan)
Volcano
https://doi.org/10.1098/rspa.2021.0320
Pyramid
Nature, 552, 386 (2017).

## Slide 27: Recent years
Shipment
Phys. Rev. RESEARCH 2, 023017 (2020)
Deep underground
Nuclear fuel
Nuclear Instruments and Methods in Physics Research Section A, Volume 878 (2018)
Recorder Vol. 43, Issue No. 05 (2018)
Huge Building