## Slide 1: VLAST-P on-orbit calibration plan
2025/01/15
Speaker : Jiaxuan Wang

## Slide 2: Motivation
VLAST-P launch mission -> on-orbit calibration accuracy
Space cosmic ray main component is proton -> muon-like proton for calibration
Geomagnetic cutoff -> asymmetry proton spectrum

## Slide 3: What is Geomagnetic Cutoff?
Earth's magnetic field's ability to block or filter charged particles
  Magnetic latitude
  Particle energy and type
  Solar activities
Magnetic rigidity = momentum/charge
  Ability of a particle to overcome the influence of the magnetic field
  Cutoff rigidity: the minimum magnetic rigidity to penetrate the Earth's magnetic field.

## Slide 4: East-west Asymmetry
Spectrum discrepancy between from east and west
General equation for the motion of charged particles
Geomagnetic cutoff rigidities determined from the IGRF models

## Slide 5: Fermi on-orbit calibration
Overview

## Slide 6: Fermi on-orbit calibration
Pedestal
Individual crystal energy scales

## Slide 7: Fermi on-orbit calibration
Light asymmetry
  Heavy nuclei event
  12 evenly spaced bin
  on the ground with sea-level cosmic muons, on orbit with GCRs.

## Slide 8: Fermi on-orbit calibration
LAC Threshold (Log-Accept)
  Typical Setting: ~2 MeV, roughly 10 times the electronic noise level.
  Purpose: Discriminates very low-energy deposits (a few MeV) from noise.
  Calibration and Stability: sets one crystal end to maximum threshold, the other end to the nominal threshold, and looks at the trigger rate (logical OR). A step-function fit then yields the actual threshold in MeV.
FLE / FHE Thresholds (Fast Low Energy / Fast High Energy)
  Typical Values: ~100 MeV for FLE and ~1000 MeV for FHE.
  Purpose: Provide quick triggering for moderate (FLE) and high (FHE) energy events
  On-Orbit Calibration: Performed by dedicating runs to background events or using injected charge; the efficiency vs. deposited energy curve is fitted to extract each threshold.
ULD (Upper Level Discriminator)
  Puropose: ensure signals do not saturate the ADC in three energy ranges (LEX8, LEX1, and HEX8)
  Ground DAC calibration: ~5% below ADC saturation; On-orbit: slightly modified

## Slide 9: DAMPE on-orbit calibration

## Slide 10: VLAST-P on-orbit calibration
All detectors
About ECAL