## Slide 1: VLAST-P ECAL on-orbit MIP calibration
2025/03/18
Speaker : Jiaxuan Wang

## Slide 2: Motivation
Geomagnetic cutoff -> On-orbit calibration with different proton spectrum
IGRF13 geomagnetic field update -> Backtracing Json library

## Slide 3: Geomagnetic cutoff MC analysis
Proton properties
  Rigidity: sampled from AMS-02 proton flux
  Direction: sampled from 4
Time-reversal approach
  Difficult to evolve forward
  Backtracing Json library
    Spiral grid method: theta, arc
    Json library indicate whether allowed directly

## Slide 4: Proton spectrum
Proton spectrum from east and west
  Particle selection: along Y axis with 60 degrees cone angle
  Block selection: Particle Earth block and geomagnetic cutoff
Red: from east
Blue: from west

## Slide 5: ECAL geometry
Apply proton spectrum to VLAST-P ECAL standalone geometry
Particle incident direction
EAST
WEST

## Slide 6: MIP result
MIP comparison from east and west

## Slide 7: Proton Calibration
A geomagnetic cutoff rigidity is associated with each solid angle bin
Sample generate
  sphere center: in the prototype
  sphere radius: 1m
Bias sample: acd hit

## Slide 8: MIP selection
Restriction added to extract MIP-like proton
  Logic trigger
  Hit ECAL unit No

## Slide 9: MIP selection
Restriction added to extract MIP-like proton
  Logic trigger
  Hit ECAL unit No
  Proton direction(Truth level)
 | After cut | All | Eff | Total eff
Trigger | 3819981 | 10000000 | 38.2% | 38.20%
HitNo | 91638 | 381991 | 2.4% | 0.92%
Angle(T) | 21711 | 91638 | 23.69% | 0.22%

## Slide 10: MIP selection
The surrounding ECAL cell with more noise as particle could only penetrate one single ECAL crystal with a quite large incident angle

## Slide 11: Tracker message
VLAST-P tracker
  Six layers: Si strips with orthogonal in two adjacent layers
  ~ 3 sets of coordinates
  Track finding and track fitting
GenFit Toolkit
  An experiment-independent framework for track reconstruction
  Basic step:
    Initialize GENFIT environment: magnetic field and material effect
    Create the track and Add hits as measurements
    Fit the track with Kalman Fitter

## Slide 12: MIP selection
Restriction added to extract MIP-like proton
  Logic trigger
  Hit ECAL unit No
  GenFit fitted state momentum
 | After cut | All | Eff | Total eff
Trigger | 3819981 | 10000000 | 38.2% | 38.20%
HitNo | 91638 | 381991 | 2.4% | 0.92%
Angle(T) | 20930 | 91638 | 22.8% | 0.21%

## Slide 13: MIP MPV comparison
Comparison

## Slide 14: Summary and next step
East-west effect influence the proton MIP MPV
MIP proton selection
  Truth level info(incident direction) could help with the noise issue
  By exploiting GenFit toolkit, the noise issue could also be depressed
GenFit optimization or other alternative method

## Slide 15: Backup
File path: /home/wangzhen/mnt2/VLASTP/vcalo/run/OOC/result/ooc.root

## Slide 16: Lat and lon

## Slide 17: Pos and vel

## Slide 18: Pos and vel