## Slide 1: Micromegas development and production at JINR
D.Dedovich
Joint Institute for Nuclear Research, Dubna
INSTR 2026, October 12-16, 2026, Hefei, China

## Slide 2: Micromegas production at JINR
Site development starts from production of MM for ATLAS upgrade
34 world-largest MM chamber – 3.1m2 each were produced for ATLAS new small wheel. Chambers of similar size were also produced by Saclay group
Dubna and Saclay chambers prepared for installation

## Slide 3: Micromegas production site at JINR Current status
2 clean room
Granite table 3.2x2.6 m2 with 3D scanner
2 precise vacuum table
Mesh stretcher
lithographic equipment, maximum board size is 90x55 cm2
We cant produce PCB and order it from commercial manufacturer

## Slide 4: NICA/SPD Micromegas Central Tracker
Micromegas Central Tracker - simple&chip tracking detector, designed to improve performance of main tracker at phase 1 of experiment. Will be replaced by silicon vertex detector later
The innermost part of tracking system
3 layers of cylindrical micromegas chamber
Key requirements:
  Resolution : <150µ
  Double track resolution ~ 1mm
  Minimal amount of material

## Slide 5: SPD Micromegas Central tracker
800
Straw tracker inner space R=280 mm
MicroMegas tracker
Dead region
Beam pipe R=34 mm
MicroMegas tracker:
3 Layers R=50-61 mm
4 half-cylindrical micromegas chambers in each layer
3mm drift gap, 120-150μ gain gap
Interaction region

## Slide 6: MCT@SPD : realistic prototype
Resistive MM, Rin=50mm
Active area length: 200mm
0.6 mm strip pitch
Anode plane: 0.3 mm PI flex PCB
Cathode: plane 0.2 mm PI flex PCB
5 mm dead areas near the edges
Cathode conductive surface& shielding is done by vacuum coating
Material budget
  Active area: per layer
  3 mm from edge : per layer

## Slide 7: Cylindrical Micromegas: production cycle
Formation of the Micromegas structure (anode PCB, pillars, micromesh) using bulk technology, like for the plane chambers.
Bending on template
Gluing of force elements and cathode plane == shape fixation
Formation of the Micromegas structure (anode PCB, pillars, micromesh) using bulk technology, like for the flat chambers.
Bending on template
Gluing of the force elements and cathode plane == shape fixation
Cutting off extra materials

## Slide 8: Cylindrical Micromegas: test results
Gas gain was routinely reached, planned working gain is
Gain is very uniform over active area
Detector quality matches that of the flat prototypes. Bending does not result in the appearance of additional defects.
Gain vs voltage
Ar(93)-CO2(7)
Gain uniformity check

## Slide 9: Cylindrical MM : pillar structure
Small bending radius require ~1mm pillar pitch => large dead area, low efficiency?
Possible solution: рerhaps very small pillars (comparable in size to the transverse diffusion length) will not significantly affect efficiency and accuracy?
Direct comparison was done at T9 beam at CERN:
Two very similar chambers were tested
  1st MM chamber with standard pillars: ⌀ 0.7mm, pitch 6mm
  2d MM chamber with additional small pillars : ⌀ 0.25mm, pitch 1mm
  Both chambers have ½ of area 0.45mm strip pitch, and ½ of area 0.7 mm pitch
“standard pillars”
“SPD pillars”

## Slide 10: Pillar structure test results:
Large number of small pillars don’t cause crucial degradation of micromegas efficiency and resolution
Resolution vs voltage scan
Efficiency vs voltage scan

## Slide 11: Gas mixture for operation in magnetic field
In crossed electric and magnetic fields, electrons drift at an angle to the direction of the electric field, known as the Lorentz angle.
For the formation of the detector signal, the track appears "effectively inclined," coordinate accuracy degrades and occupancy increases
We need:
  Space resolution better then 150 μ
  Double hit resolution about 1.5 mm
  Good amplitude to operate in triggerless mode

## Slide 12: MM operation in magnetic field : ways to keep resolution
“Standard” mixtures (Ar-CO2-iC4H10, Ar-iC4H10) at optimal drift field + μ-TPC reconstruction
  Lorentz angle > 40o Charge divided between ~ 10 strips, high ocupancy, bad double hit resolution
Find a combination of mixture and drift field with Lorentz angle < 10o
AR-CO2 gas mixtures with high CO2 fraction (specifically Ar-CO2 30%-70%) looks OK:
  reasonable max. achievable gas gain
  Lorentz angle bellow 10o for B=1T
  Expected resolution is about 100µ B=1T for 0.4mm pitch and B=1Т (Garfield simulation, charge weighting)

## Slide 13: Gas mixture test in magnetic field: results
H4 beam & Goliath magnet, BMAX=1.35T
Two very similar chambers, APV25/SRS readout, Ar-CO2 (30%-70%) gas mixture
Small beam divergence(neglected)
Charge weighting for cluster coords reconstruction
chamber1
chamber2
Two chamber residual
B=0.92T
Pitch 0.45
Efficiency vs B
Resolution vs B
Pitch =0.7mm
Edrift=2kV/cm
Pitch =0.7mm
Edrift=2kV/cm
Better then in was expected!

## Slide 14: Development of low-material MM for AMBER small angle tracker
Requirements:
  Active area : 30x30 cm2 (preferably up to 40x40)
  Resolution :
  Material budget: per plane
  Easy-to-reproduce technology

## Slide 15: Low-material MM
2-side, “floating mesh”
Active area 10.2x10 cm2, easy to scale, limited by PCB size
2x256 strips, 0.4 mm pitch
for 2 plane
Resolution: (beam test results)
Efficiency (beam test results)

## Slide 16: Low-material MM prototype
Readout panel:
Sandwich 50μ flex PCB – 3mm Rohacell foam – 50μ flex PCB
withstands heating up to 130o and etching
Guard ring & pillars were produced after sandwich gluing
Mesh frame+mesh
Cathode – 25µ rigid-flex pcb
Outer wall – 25µ rigid-flex pcb.
Copper layer produced by vacuum coating for min material

## Slide 17: Low-material MM: readout panel
Sandwich 50μ flex PCB – 3mm Rohacell foam – 50μ flex PCB
Pillars cant be formed on raw readout PCB as polymerization of photoresist cause shrinking of thing (50μ) PCB
After gluing readout panel MUST withstand heating and etching (use suitable materials and glue)

## Slide 18: Low-material MM prototype Gas gain and uniformity
Gain vs voltage
Gain uniformity

## Slide 19: Low-material MM prototype Beam test result
Efficiency vs voltage
2D Efficiency map
Side1&side 2 residual
Pillars takes 4.9% of active area =>efficiency is near the limit
APV25/SRS readout, 2fQ thresold

## Slide 20
 | material | X0 (g/cm²) | Density (g/cm3) | Thikness, µ | Fill Factor | X0 (cm) | x/X0
shielding | Copper | 12,86 | 8,96 | 18 | 0,080 | 1,435 | 1,00E-04
Cover | Kapton | 40,58 | 1,42 | 25 | 1 | 28,577 | 8,75E-05
Cathod | Kapton | 40,58 | 1,42 | 50 | 1 | 28,577 | 1,75E-04
copper/cathode | Copper | 12,86 | 8,96 | 18 | 0,100 | 1,435 | 1,25E-04
mesh 63/18 | Inox | 14 | 7,93 | 25 | 0,448 | 1,765 | 6,34E-04
PCB | Kapton | 40,58 | 1,42 | 50 | 1 | 28,577 | 1,75E-04
PCB | Copper | 12,86 | 8,96 | 18 | 0,625 | 1,435 | 7,84E-04
core | Glue | 43,25 | 1,33 | 50 | 1 | 32,519 | 1,54E-04
 | rohacel |  |  | 3000 | 1 |  | 4,19E-04
 | Glue | 43,25 | 1,33 | 50 | 1 | 32,519 | 1,54E-04
PCB | Copper | 12,86 | 8,96 | 18 | 0,625 | 1,435 | 7,84E-04
PCB | Kapton | 40,58 | 1,42 | 50 | 1 | 28,577 | 1,75E-04
mesh 63/18 | Inox | 14 | 7,93 | 25 | 0,448 | 1,765 | 6,34E-04
copper/cathode | copper | 12,86 | 8,96 | 18 | 0,100 | 1,435 | 1,25E-04
Cathode | Kapton | 40,58 | 1,42 | 50 | 1 | 28,577 | 1,75E-04
Cover | Kapton | 40,58 | 1,42 | 25 | 1 | 28,577 | 8,75E-05
Shielding | Copper | 12,86 | 8,96 | 18 | 0,080 | 1,435 | 1,00E-04
 |  |  |  |  |  |  | 4,89E-03

## Slide 21
Thanks