## Slide 1: Progress and status of HIAF project
On behalf of the HIAF Project Team
Jiancheng Yang
Institute of Modern Physics (IMP) , Chinese Academy of Sciences (CAS)
Oct 15, HeFei, China
The International Conference on Instrumentation for Colliding Beam Physics
( INSTR 2026 )

## Slide 2
Project overview
Challenges, innovations, and breakthroughs
Construction, commissioning, and performance
Summary and perspectives
Outline

## Slide 3
Nuclear physics frontier:
Explore the limit of nuclear existence
Study exotic nuclear structure
Understand the origin of the elements
Study the properties of High Energy and Density Matter
Accelerators and use of high intensity heavy-ion beams will be key to solving those questions
FRIB
FAIR
NICA
RIBF
SPIRAL2
Project overview

## Slide 4
High-Intensity Heavy-Ion Accelerator Facility- HIAF
The major national science and technology infrastructure under construction with the support of both central and local governments
The project was proposed and constructed by IMP, CAS
The total budget is 3.0 billion CNY
High-Intensity Heavy Ion Accelerator Facility - HIAF

## Slide 5
BRing
iLinac:
Superconducting linac
Length:100 m/300 m
Energy: 17-22 MeV/u(U35+-46+)
SRing:
Spectrometer ring
Circumference: 277 m
Rigidity: 13-15 Tm
L: 180m, Bρ: 25 Tm
Fast cycle ring
Circumference: 569 m
Rigidity: 34 Tm
HFRS: Radioactive beam line
SECR:
Superconducting ECR source
1
2
3
4
5
6
Low energy nuclear structure terminal
High energy experimental terminal
High energy fragment separator HFRS
High precision spectrometer ring SRing
Electron ion recombination terminal
Radioactive ion beam physics terminal
Experimental terminals
The whole layout: accelerator components and experimental terminals
Project overview

## Slide 6
BRing
iLinac:
Superconducting linac
SRing:
Spectrometer ring
Circumference: 277m
Rigidity: 2-15 Tm
Fast cycle ring
Circumference: 590 m
Rigidity: 34 Tm
HFRS: Radioactive beam line
Low energy nuclear structure and irradiation terminal
High energy experiment station
Radioactive beams physics station
High precision
spectrometer ring
e-ion recombination
spectroscopy
2
3
4
5
6
1
Digital-twin-based engineering information modeling (BIM) of HIAF facility
SECR:
Superconducting
ECR source
Hyper nuclei physics
Phase diagram of strongly interacting matter
Project overview

## Slide 7
Beam commissioning
Equipment operation
Civil construction began
First key equipment
Key prototype
Equipment bidding
Testing
Auxiliary system
Installation
Offline commissioning
Batch processing
Achieve design parameters
@2025.11
2019
2020
2021
2022
2023
2024
2025
Time schedule
7-year construction period since 2019
Project overview
The key milestones and timelines

## Slide 8
Project overview
Challenges, innovations, and breakthroughs
Construction, commissioning, and performance
Summary and perspectives
Outline
Notes: That's the project overview. Now, let's look at the project challenges, innovations and breakthroughs.
In my talk, firstly I will give a general introduction of the HIAF project, today my talk will mainly focused on the challenges, and a series of innovations and breakthroughs addressing these challenges.
, as well as engineering construction and performance of facility. Finally is summary and future perspectives.
Then is the next step plan and future perspectives and

## Slide 9
 | SECR | iLinac | BRing | HFRS | SRing
Length / circumference (m) | --- | 114 | 569 | 192 | 277
Final energy of U (MeV/u) | 0.014 (U35+) | 17 (U35+) | 835 (U35+) | 800 (U92+) | 1100 (U92+)
Magnetic rigidity(Tm) | --- | --- | 34 | 25 | 15
Beam intensity of U | 1.7 emA (U35+) | 1.0 emA (U35+) | 21011ppp (U35+) 61011pps (U35+) | ------- | (0.5-1) 1012ppp (U92+)
Operation mode | DC | CW or pulse | fast ramping (12T/s, 3Hz) | Momentum-resolution 1100 | DC, deceleration
Emittance or Acceptance (H/V, ·mm·mrad, dp/p) |  | 5 / 5 | 200/100, 0.5% | 30mrad(H)/15 mrad(V), 2% | 40/40, 1.5% (normal mode)
High current low energy CW and high intensity high energy pulse beam
Features:
High intensity ion beam

## Slide 10
Key challenges
Institute | Machine | Planned | Achieved | Ion
BNL | AGS Booster |  | 5×109 | Au32+
CERN | LEIR |  | 9×108 | Pb54+
JINR | NICA Booster | 4×109 | / | Au32+
GSI | SIS18 | 1.0×1011 | ~ 4×1010 | U28+
FAIR | SIS100 | 4.0×1011 | / | U28+
IMP | HIAF-BRing | >1.0×1011 | / | U35+
IMP | HIAF-SRing | >5.0×1015 | / | U92+
IMP | HIRFL-CSR | 1.0×109 | 1.0×108 | U74+
Challenge-1:
Beam dynamics
Nonlinear effects
Space charge effects
Collective effects
Dynamic vacuum
Beam intensity
Beam quality
leads to
limits
World's most intense pulsed heavy-ion beams
Challenge-2
Technology aspect
Beam production
Low energy manipulation
Fast ramping acceleration

## Slide 11
How to achieve the unprecedented heavy ion intensity
BRing
iLinac
SECR
SRing
1~21011 ppp U35+
1 emA U35+
>1.7 emA U35+
~11012 ppp U92+
The Front-End
4th generation ECR
Injector
SRF Linac
Accumulation
Novel Dual-plane painting injection
Stacking
Innovative stripping stacking longitudinally
Acceleration
The highest ramping rate 24 T/s
AI-driven control software platform
Commissioning
Digital twin engineering construction
Construction

## Slide 12
Breakthrough-1:
Variation＜2%
Bi31+:
the peak current of pulse beam reached 1emA
HIAF goal
Innovative afterglow operation
Bi35+:
beam current is about 350 eμA , the new record of Bi ion.
HCI production
The world's first fourth-generation superconducting ECR ion source
Features：
45/28 GHz Operation
High Power quasi-optical microwave injection
Micro-channel plasma chamber

## Slide 13
0.8 MeV/u CW RFQ
CW, 1.0 emA U
QWR 007
HWR 015
Average Epk = 33.8 MV/m；20.7% > designed
Breakthrough-2:
SRF linac injector
Pulsed, 1.7 emA U
mA level highly charged heavy ion beam

## Slide 14
Conventional multi-turn injection
Dual planes painting injection
Novel dual planes painting injection
Both the horizontal and vertical painting simultaneous using the tilted E-Septum
2.0 1011 with two planes painting, nearly 10 times over the conventional multi-turn injection
Breakthrough-3:
New beam accumulation scheme

## Slide 15
High-ramping-rate beam acceleration
Why? High intensity ion beam effects dominated beam loss
Beam should be launched to the high energy as quickly as possible
Breakthrough-4:
Space
charge
Dynamic
vacuum
Collective
instability
Fast ramping rate mode
Challenges for fast ramping acceleration
RF system
Power supply
Vacuum chamber

## Slide 16
Fast ramping rate full energy storage PS
Power requirement (MVA) | Conventional | Energy storage
Bendng magnet | 180 | 15
Quadruple magnet | 50 | 6
Total of BRing | 250 | 41
Total of HIAF | 297 | 88
100Gs→<±1Gs
Dynamic magnet field correction
Excellent performance, and power consumption is reduced to 10% of traditional
Ramping rate > 40000A/s,
Tracking error< ±9.6 e-5
A full energy storage system including 350 power converters has been built
Energy from capacitor tank to magnet load
Energy from magnet load to capacitor tank
Innovative topology：
( variable forward excitation, full energy storage, PWM rectification technology )

## Slide 17
Magnetic alloy core loaded RF
Facilities | Voltage (kV) | Length (m) | Gradient(kV/m)
JPARC-RCS | 41 | 1.78 | 23
JPARC-MR | 46.7 | 1.78 | 26.2
SIS18 | 50 | 2 | 25
HIAF-BRing | 70 | 2 | 35
MA loaded RF system in the tunnel
Total RF voltage: 350kV
Breakthrough in MA Loaded Cavity
95×65×25mm
18um ribbon
18um ribbon
14um ribbon
460×230×25mm
780×360×35mm
World-leading level
Over ten years exploration
Ranks among the best in the world

## Slide 18
Thin-walled vacuum chamber
Thin-wall chambers: Keep eddy currents at a tolerable level
Stainless steel-0.3mm
Rib-15mm,one side
Novel scheme of IMP
Reinforcing ribs
HIMAC - Japan
GSI - Germany
3D-printed CT4 titanium alloy cage
Thin-wall chamber supported by cage
Cage: 4 mm one side
Stainless steel-0.3mm
Static vacuum
pressure
4.7×10-12
mbar
Dynamic vacuum level of high intensity
1×10-11 ~
5×10-12 mbar
This is the highest vacuum level ever reported for synchrotron facilities

## Slide 19
Breakthrough-4:
0.1
1
100
10
Ramp rate of the magnetic field （T/s）
HIMM, China
HIMAC, Japan
HIRFL-CSR, China
HIT, Germany
SIS12, Germany
HIAF，China
0. 5 T/s
1. 5 T/s
1 T/s
2 T/s
8~10 T/s
24 T/s
The non-resonant acceleration rate reaches 24 T/s, three times the fastest rate reported internationally.
Reducing high-intensity-dominated beam loss from 13% to 3%
High-ramping-rate beam acceleration

## Slide 20
Project overview
Challenges, innovations, and breakthroughs
Construction, commissioning, and performance
Summary and perspectives
Outline

## Slide 21
The standardized design of non-standard equipment is rapidly iterated
Three-dimensional virtual visualization of assembly optimization processes
Digital-driven modular prefabrication boosts efficiency
Full-chain data sharing for dynamic decision-making
Through a End-to-End Digital closed loop
Digital-twin-driven construction
Create new models for engineering construction
Design
Manufacturing
Installation
Management
High intensity Heavy ion accelerator -HIAF
Digital Twin collaborative platform
Digital Twins for high-quality and efficient construction of large scale scientific project
Engineering Construction

## Slide 22
Engineering Construction
Occupies 80 acres, total construction area 58,000 m2,
Testing&Assembly hall
SRing building
Cryo center
BRing building
Linac building
Central control building
Civil construction
10 above-ground building and a 2-kilometer-long underground tunnel at a depth of 13 meters

## Slide 23
The period for a 2-kilometer beam line has been shortened from 2-3 years to 8 months
iLinac
RFQ
BRing Injection Line
BRing
HiRIBL (HFRS)
SRing
Ion Sources
Tunnel installation
Full Digital Instruction
Engineering Construction

## Slide 24
AI-driven beam control platform
A new full-stack intelligent software system for communication, control, storage, and analysis
International
CV-Link
Increase the transmission rate by five times
Dynamic control performance is enhanced by 20 times
3s
67s
Big data access speed is 10 times faster
Internationally pioneering
high-speed communication protocol CV-Link
Innovative
big data access and analytics LA-DB
High reliability distributed intelligent control system LACCS
The entire chain guarantees the security of data for the accelerator's large scientific facility and core research experiments, with high performance
Machine Commissioning

## Slide 25
HIAF implementation: integration 141 beam dynamics, 3,559 large-scale devices, and 230,000 control variables for joint commissioning
It delivers real-time data processing, automatic control, and AI-based debugging - for large-scale accelerators.
Full cover of all accelerator nodes
Implantation of beam dynamic operation
Machine Commissioning

## Slide 26
Heavy-ion Accelerator Fires Up
Bring Beam
Science, 6 NOVEMBER 2025, P.559
The full commissioning, spanning a 2-kilometer-long beamline, was completed in only 16 hours — a new record for large-scale scientific facilities
The successful commissioning of HIAF was promptly reported in Science
Machine Commissioning

## Slide 27
HIAF束流指标
Increased
by a factor of 8
Increased
by a factor of 3
Increased
by a factor of 3
Xe
Bi
O
Excellent performance
New records for heavy ion beam intensity

## Slide 28
World first: nuclear mass precision improved from 10⁻⁷ to 10⁻⁸
In two-TOF mode:
HIAF-Spectrometer Ring
(SRing)
γt = 1.43 (IMS mode)
②
①
Excellent performance

## Slide 29
First Scientific Achievement
High precision spectrometer ring SRing
The new nuclide ¹⁵³Hf was discovered.
Approximately 35 new nuclear masses were simultaneously determined in 12h
World's first discovery of a new nuclide via a storage ring —
conventionally discovered with gas-filled recoil or radioactive beam separators

## Slide 30
First Scientific Achievement
Low energy nuclear structure terminal
242Fm@HIAF Half life: 4.17μs
Response < 1.0 s
Precise determination of the half-life of the extremely short-lived nuclide 242Fm: 4.17 μs, clarifying the inconsistency in the international 242Fm half-life data
Nuclear Physics A 255 (1975) 509
Eur. Phys. J. A 37, 177-183(2008)
241Fm@Dubna
Half life: 800μs
GSI
Half life：N/A
Response 100 s
Response 20 s

## Slide 31
First Scientific Achievement
200Pb Decay γ
200Pb identification
108Sn
105Cd
High energy fragment separator HFRS
First identification of neighboring nuclides of 200Pb, produced by 209Bi fragmentation
Offering key data for heavy-nucleus cross-section predictions.

## Slide 32
Project overview
Challenges and innovations
Engineering construction and performance
Summary and perspectives
Outline

## Slide 33
Beam dynamics study and machine performance improvement
Reliable and high efficiency operation for users
New techniques implementation for higher intensity
Ongoing efforts are focused on
HIAF intensity goal
Intensity goal with stripping stacking
Intensity world records
Summary and perspective
HIAF has successfully achieved its design goals — and established world-leading capabilities in high-intensity heavy-ion beams
Notes: Now ongoing efforts are focused on ………,
In particular, in the next step we will implement a unique longitudinal stripping stacking scheme, which will increase the beam intensity by a factor of several.
as well as new techniques implementation for higher intensity, there are
The next ion scheduled for commissioning is uranium ion, here is the specified design intensity for Uranium beam.

## Slide 34
①
③
④
②
⑥
BRing
SECR
iLinac
⑤
SRing
HFRS
⑨
⑦
⑧
(3)
(2)
(1)
Ions | Energy (GeV/u) | Intensity (ppp)
p | 9.3 | 1.01013
18O6+ | 4.3 | 6.01011
78Kr19+ | 1.7 | 4.01011
238U35+ | 0.85 | 2.01011
(1) Hyper nuclear physics
(2) Phase diagram of strongly interacting matter
(3) Irradiation research
Summary and perspective
High energy hall: polarized proton beam

## Slide 35
China advanced NUclear physics research Facility
ISOL
Scientific motivation:
The limit of existence of nuclides
Nuclear matter phase structure
Strong-field QED effect
Spin decomposition and origin of mass
High-energy-density physics
New physics beyond SM
Driven by the high power proton beam from CiADS Linac, producing high intensity neutron-rich nuclides and be post-accelerated by HIAF-U.
EicC
Consists of p-Ring, e-Ring and beam injectors, realizes dual-polarized high intensity electron ion collision, with full energy beam injection and rapid replacement based on e-injector and BRing-S.
HIAF-U
Upgrade HIAF with 200MeV/u iLinac, superconducting synchrotron BRing-S and the merging ring MRing, providing high-intensity, high-quality ion beams from proton to uranium.
CNUF-An upgrade project for the HIAF and CiADS
Sub-critical lead-bismuth eutectic (LBE) fast reactor
Notes: For future, an upgrade project CNUF is proposed based on HIAF, CNUF is abbreviation of China advanced nuclear physics research facility. The gray areas and lines show the facilities are under construction, the orange shows the update programs. It is consisted of ISOL、HIAF-U and EicC.

## Slide 36
CNUF-An upgrade project for the HIAF and CiADS
EicC: Dual-polarized high-luminosity electron-ion collider in the sea quark energy region.
Spin decomposition & nucleon mass origin
Mode: rapid replacement head-on collision
Integrated Lumi.=150-200 fb-1
U.S.EIC 10×100 GeV2
EicC 5×25 GeV2
JLab 12 GeV
Electron: 5 GeV, 4.5×1013 ppp, 80% polarization
Proton: 25GeV, 4×1014 ppp, 70% polarization
Ion: d (polarized), 3He (polarized) to Uranium
p-Ring: 86.5Tm, 500MHz RF
e-Ring: 16.7Tm, 500MHz RF
EicC at a sweet spot to systematically study the behavior of sea quarks.
EIC-US is a higher energy machine with an emphasis on low and moderate-x region for gluon.
Combining the measurements at both colliders will provide systematically controlled physics interpretation
Ecm=15-20 GeV, Lumi=(5-6) ×1033 cm-2s-1
Notes: The third is the EicC, EicC is Dual-polarized high luminosity electron-ion collider, the design center of mass energy is 15-20 GeV, the peak luminosity is about (5-6) ×1033 cm-2s-1. We hope the integrated luminosity can reach 150-200fb-1. Compare with EIC of US,

## Slide 37
HIAF in the early morning light, is only at the dawn of what it can achieve!
Thanks for your attention!
So we welcome researchers from the global scientific community — to explore the possibilities with us.

## Slide 38
HIAF and CiADS
CiADS
China Initiative Accelerator Driven System
HIAF
High-Intensity Heavy Ion Accelerator Facility
Superconducting proton linear accelerator
High power lead-bismuth eutectic (LBE) spallation target
Sub-critical lead-bismuth eutectic (LBE) fast reactor
Notes: Besides the HIAF, there is another facility CiADS in the same campus. CiADS is China Initiactive Accelerator Driven System. It consists of

## Slide 39
ISOL ( Isotope Separation On-Line ):
MW-class high-power proton beam to produce high-intensity neutron-rich nuclides and surface muon
Exploring the limit of existence of nuclides
Mode: ISOL + iLinac + BRing-N
Neutron-rich nuclides generation online (~1016 fis./s)
Post-acceleration by iLinac and Bring-N (>100 MeV/u)
Generate extremely neutron-rich secondary beams
Muon research and μSR application
Mode: CiADS + high power target
High intensity surface muon (~1012 μ/s)
Muon moderation and μSR
Future muon factory and collider
 | FRIB | PSI | ESS | CiADS
BEAM | H to U | p | p | p
Mode | CW | CW | CW | CW
Energy (GeV) | >0.2 | 0.59 | 2.5 | 0.5
Current (mA) | - | 2.44 | 2 | 5
Power (MW) | 0.4 | 1.44 | 5.0 | 2.5
CNUF-An upgrade project for the HIAF and CiADS
Notes: Isol will be constructed based on the MW-class high-power proton beam of CiADS. You can find in this table, CiADs can provide 2.5MW proton to produce high-intensity neutron-rich nuclides and surface muon.
Muon Spin Rotation/Relaxation/Resonance，利用缪子自旋特性在原子尺度上研究物质结构的方法统称。

## Slide 40
CNUF-An upgrade project for the HIAF and CiADS
Nuclear matter, hypernuclei and η/μ research
Mode: BRing-S (fast/slow ext. p-U) + fixed target
High-intensity high-power beam
Nuclear matter phase transition research
Hypernuclei, η/μ physics, Λ polarization
Strong-field QED effect experiment
Mode: MRing&SRing merging collision
Ecm=4-10 MeV/u, Lumi.>4×1026 cm-2s-1
Super strong e-field exceed Schwinger limit for low-background e-p pairs generation
MRing
SRing
Muon research
iLinac up to 200MeV/u
ISOL
High-energy-density physics
Ion-ion merging
BRing-N/S
Nuclear matter Hypernuclei Research
High-energy-density physics
Mode: BRing-N/S&MRing + beam manipulation
2MJ, ns-scale short bunches
Multimodal fixed target experiments
HEDM in strong shock wave region to create extreme matter states
HIAF-U: Multi-functional high-intensity accelerator facility from p to U
Facility | Beam (GeV/u) |  | Intensity (ppp)
FAIR | 2.7 | 238U28+ | 5×1011
NICA | 4.5 | 197Au32+ | 4×109
FNAL | 8.0 | p | 6.8×1013
HIAF | 0.8 | 238U28+ | 5×1011
 | 1.1 | 238U92+ | 1×1012
HIAF-U | 3.0 | 238U35+ | 2×1012
 | 9.1 | 238U92+ | 3×1012
 | 25 | p | 4×1014
HIAF & HIAF-U
BRing-N: 34Tm, 569m, 3Hz
SRing: 17(25)Tm, 270.5m, accumulation/compression
BRing-S: 86Tm, 3Hz, superconducting
MRing: 45Tm, superconducting, beam merging
Notes: HIAF-U is proposed on the HIAF, For HIAF-U, iLinac energy will update to 200MeV, a superconducting synchrotron with rigidity of 86 Tm and a superconducting storage ring for beam merging will be constructed. With these update programs both beam intensity and energy will increase significantly. HIAF-U will focus on