## Slide 1: Beam Facilities at China Spallation Neutron Source
Ruirui Fan
Institute of High Energy Physics, CAS

## Slide 2: 中国散裂中子源
China Spallation Neutron Source

## Slide 3: China Spallation Neutron Source
bird view of campus
Hefei
Dongguan

## Slide 4: CSNS campus
Before ground breaking, May 9, 2009
Aug. 28, 2017
Aug. 2024
Proposed at year of 2000
Budget: about 2.2 B CNY
Construction started at Sep. 2011, and finished at Mar. 2018
User program started in Oct. 2018
Beam power increased from 20kW to 185kW
Operation with long user hours and high availability
11 neutron instruments and in user program
Notes: This page shows the evolution of the CSNS campus in Dongguan. We have three key time nodes: the original site photo on May 9, 2009 before ground breaking; the completion status on August 28, 2017; and the latest campus view in August 2024. CSNS was first proposed in 2000, with a total budget of about 2.2 billion Chinese Yuan. Construction started in September 2011 and was completed in March 2018. The formal user program launched in October 2018. Up to now, the beam power has been raised from 20 kW to 185 kW, maintaining long user operation hours and ultra-high availability, with 11 neutron instruments officially open to users.

## Slide 5: CSNS Facility
DTL
RFQ
Ion Source
1.6 GeV RCS
Target
0.05 MeV
3 MeV
80 MeV
LEBT
MEBT
LRBT
RTBT
Beam Power on target [kW] | 100
Proton energy [GeV] | 1.6
Average beam current [uA] | 62.5
Pulse repetition rate [Hz] | 25
Linac energy [MeV] | 80
Linac type | NC
Linac RF frequency [MHz] | 324
Macropulse duty factor | 1.05
RCS circumference [m] | 228
RCS harmonic number | 2
Notes: This is the overall accelerator layout of CSNS, including ion source, RFQ, DTL, LEBT, MEBT, LRBT, RCS and tungsten target station. The core design parameters are clearly listed here: target beam power 100 kW, proton energy 1.6 GeV, average beam current 62.5 microamps, repetition rate 25 Hz, linac energy 80 MeV, and RCS circumference 228 meters. We also display the macro-pulse, mini-pulse and micro-pulse time structure formed by the ion source, LEBT chopper and RFQ system respectively.

## Slide 6
Powder Diffractometer | General Purpose Powder Diffractometer (GPPD)
 | Multi Physics Instrument (MPI)
 | High-resolution Powder Diffractometer (TREND)
 | High pressure diffractometer (HP)
Large Scale | Small Angle Neutron Scattering instrument (SANS)
 | Very Small Angle Neutron Scattering (VSANS)
 | Multi-Purpose Reflectometer (MR)
 | Liquid Neutron Reflectometer (LNR)
Industry Application | Engineering Material Diffractometer (EMD)
 | Energy Resolved Neutron Imaging (ERNI)
 | Atmosphere Neutron Irradiation (ANIS)
Direct Geometry Spectrometer | High energy inelastic spectrometer (HD)
 | Cold Neutron Inelastic Spectrometer (CNIS)
 | Polarized Chopper Spectrometer (PACS)
Indirect Geometry Spectrometer | Molecular Vibration Spectrometer (IMVS)
 | Neutron Backscattering Spectrometer (NUBS)
Single Crystal | Elastic Diffuse Scattering Spectrometer (EDS)
 | Single Crystal Neutron Diffractometer (SCND)
Nuclear physics & technique | Back-streaming white neutrons (Back-n)
 | Neutron Technology Develop Station (NTDS)
 | Neutron Physics & Application Instrument (NPAI)
 | High-energy Proton Experimental Station（HPES）
 | Muon station（MELODY）
CSNS Instrument Suite
Notes: After CSNS-II completion, the facility will own a complete instrument suite covering powder diffraction, small angle scattering, reflectometer, inelastic spectrometer, single crystal diffraction, nuclear physics and muon/proton experimental stations. Each type has multiple specialized instruments, forming a full-coverage neutron research platform for multidisciplinary demands.

## Slide 7
The User Program
https://user.csns.ihep.ac.cn (in both Chinese and English）
Registration user: 10,000+
A total of over 2,500 projects from 268 units were completed, with industry users comprising approximately 9.5% of the total.
Two rounds of proposal calls each year.
User proposal VS. Proposal proved
User publications
Notes: CSNS has built a bilingual Chinese and English user official website for proposal application and management. Up to now, we have more than 10,000 registered users. A total of over 2,500 research projects from 268 institutions worldwide have been completed, among which industrial users account for about 9.5%. We launch two rounds of project proposals every year. The statistical chart clearly shows the annual number of user proposals and approved projects since 2018.

## Slide 8
Research Areas
Chart: 
| Energy & Battery | Magnetism&Multiferroic | Metal&Alloy | Oxides Film | Spintronics | Polymer | Nano Composite | Biology | Superconductivity | Engineering | others
Sales | 64 | 27 | 32 | 15 | 11 | 17 | 15 | 3 | 7 | 12 | 11
University：～45%
Research institution：～49%
Enterprise：～6%
Notes: The user projects cover many research areas. The largest proportion is accounted for by new energy and batteries.

## Slide 9
White neutron source
~300 MeV neutron
Associated Proton beam Experiment Platform 80 MeV proton
Proton test beam
1.6 GeV proton
muon source
CSNS Beam Expansions Application
Linac
Ion source
Synchrotron
Notes: The main research at CSNS (China Spallation Neutron Source) is focused on thermal neutron scattering measurements, corresponding to condensed matter physics and materials science. However, for such a large facility, we have also designed several platforms for extended applications around the accelerator. We have designed and built four beam application platforms, two of which have already been completed. The other two will be constructed within the next six years as part of CSNS-II.

## Slide 10
伴生质子束平台
Associated Proton beam Experiment Platform

## Slide 11
White neutron source
~300 MeV neutron
Associated Proton beam Experiment Platform 80 MeV proton
Proton test beam
1.6 GeV proton
muon source
CSNS Beam Expansions Application
Linac
Ion source
Synchrotron
Notes: APEP is located at the end of the linear accelerator and is primarily used for proton irradiation experiments.

## Slide 12: Generation of associated protons
e
e
e
Dipole magnet
DUMP
APEP
RCS
By using a dipole magnet to separate the three components, the H- ions are injected into the ring accelerator, H0 is directed towards the dump, and the protons are extracted to APEP.
During the acceleration process of negative hydrogen ions, due to collisions with gas molecules in the vacuum pipeline, the outer electrons can be stripped off, resulting in a certain proportion of hydrogen atoms (H0) and protons.
Notes: During the acceleration process of negative hydrogen ions, due to collisions with gas molecules in the vacuum pipeline, the outer electrons can be stripped off, resulting in a certain proportion of hydrogen atoms (H0) and protons. By using a dipole magnet to separate the three components, the H- ions are injected into the ring accelerator, H0 is directed towards the dump, and the protons are extracted to APEP.

## Slide 13: CSNS Associated Proton beam Experiment Platform
Vacuum valve
CT Monitor
degrader
COL1
COL2
COl3
Faraday cup
DUMP
Vacuum pump
the beamline is 14 meters.
Proton
Parameters of APEP
Energy：10-80 MeV (FWHM)<8.65% @>30MeV
Spot： 10 x 10 mm2 – 50 x 50 mm2（Continuously adjustable, uniformity > 95%）
Flux：105-1010 p/cm2/s
Monitor：1. CT, Faraday cup and activation foil
Vacuum terminal：vacuum<10-3 Pa, 50cm×Ø0.8m, Five test position；
Atmospheric terminal ：Remote-controlled sample holder
Background：<1.4E-4(n)和<3.4E-5(gamma) @20 x 20 mm2
When negative hydrogen ion beams are accelerated and transmitted in the LINAC, they interact with the residual gases in the vacuum tube. A small portion of the negative hydrogen ions are stripped into protons and transmitted to the end of the linear accelerator. This is the world's first experimental terminal utilizing accompanying proton beams.
Vacuum terminal
Atmospheric terminal
Notes: A degrader is used to reduce the energy of particles.

## Slide 14: User experiment
Detector radiation tests
Si material radiation damage
ASIC SEE for ATLAS
ASIC SEE for LHCb detector
Radiation-induced mutation breeding
Communication devices radiation
Detector calibration
Radionuclide activity measurements
Space photoelectric device radiation
*Chips radiation damage; *Material radiation research ; *Detector radiation and calibration ;
*Space Electronics radiation damage; *Radiation-induced mutation breeding;
APEP began trial operation at the end of 2021.
Each year, it completes over 100 experiments, covering various fields.

## Slide 15: Scintillator irradiation
NIMB 548 (2024) 165247
NIMB 561 (2025) 165628

## Slide 16: 反角白光中子实验装置
Back-n

## Slide 17
White neutron source
~300 MeV neutron
Associated Proton beam Experiment Platform 80 MeV proton
Proton test beam
1.6 GeV proton
muon source
CSNS Beam Expansions Application
Linac
Ion source
Synchrotron
Notes: Before the protons hit the target, a dipole magnet here deflects the protons by 15°. Since there are no obstructions in the path of the protons to the target, the energy of the white neutrons is also very high. Unlike thermal neutron tunnels, which all face the moderator, the white neutron tunnel directly faces the neutron target.

## Slide 18
White neutron source
target
TOF
Gamma flash
neutron
The name "white neutron" is derived from "white light," which indicates a broad spectrum of wavelengths. Unlike monoenergetic neutron sources, a white neutron source has a very wide energy spectrum.
Notes: It typically involves a pulsed accelerator that accelerates electrons or protons to strike a target. At the moment of impact, we obtain the initial flight time of the neutrons. Neutrons of different energies are produced through spallation reactions or photonuclear interactions, and the neutron energies are then distinguished by their flight times.

## Slide 19: Back-n
2017 JINST 12 P07022
Eur. Phys. J. A (2019) 55: 115
Layout of the Back-n
proton

## Slide 20: Back-n Tunnel and shielding
Neutron and γ background measurements of the experimental halls at the CSNS back-streaming white neutron source，NIMA Volume 980, 11 November 2020, 164506

## Slide 21: Back-n neutron energy spectrum measurement
Eur. Phys. J. A (2019) 55: 115
Chen, Y., Qiu, Y., Li, Q. et al. Eur. Phys. J. A 60, 63 (2024).
Energy range | flux (neutrons/cm2/s)
0.1-1 eV | 4.08×103
1-10 eV | 1.79×104
10-100 eV | 3.01×104
0.1-1 keV | 5.01×104
1-10 keV | 1.23×105
10-100 keV | 4.30×105
0.1-1 MeV | 2.98×106
1-10 MeV | 2.77×106
10-200 MeV | 6.21×105
Total | 7.03×106
We used different reference cross-sections to measure the energy spectrum, including: (n, p), 6Li(n, t), 235U(n, f), 238U(n, f)
Measurement of the neutron flux of CSNS Back-n ES#1 under small collimators from 0.5 eV to 300 MeV

## Slide 22
https://user.csns.ihep.ac.cn/backn-publications-standalone/

## Slide 23: Gamma Total Absorption Facility（GTAF）
Courtesy of Guangyuan Luan ( CIAE)
· By using Cd absorption sheets, the background caused by long-lived nuclides in the environment can be evaluated.
· By measuring the empty target, the background unrelated to the samples can be assessed.
· By measuring the C sample, the background of scattered neutrons caused by the sample can be evaluated.
Core component:
15-cm-thick BaF₂ crystal, composed of 40 independent detection units
Neutron shielding:
Boron-containing polyethylene absorber
High measurement efficiency:
~90% for gamma rays up to 10 MeV; ~100% for neutron capture events
Notes: Sodium Cobalt Niobium

## Slide 24: Q-value selection
Q-value of 139La(n,γ)： 5161.0keV
Q-value of 138La(n,γ)： 8780.3keV

## Slide 25: MTPC探测器系统
Anode board
High voltage
Gas pressure control system
DAQ
Pre-amp
Power supplier
Gas mixture system
NIMA 1039 (2022) 167157
Z. Chen et al 2022 JINST 17 P05032
NIMA1058(2024)168912
NIMA 1060 (2024) 169045
Back-n multipurpose TPC

## Slide 26: Experiment Setup
Assembled Module (PAM, ACM, PCMM)
DCM
TCM
Electronics:
Sampling frequency: 40 MHz
Sampling time window: 25.6 μs
Total channels: 1521
Courtesy of Han Yi (CSNS)

## Slide 27: 235U(n, f) cross section measurement
The distributions of the vertexes of (a) decay α particles from the 235U sample. (b) fission fragments from the 235U(n, f) reaction.
Han Yi et al 2026 Chinese Phys. C 50 044004

## Slide 28: Nuclide identification radiography (NIR)
sample：
Au、Ag、W、Ta、In
Transmission image
Indium
Tungsten
NIMA 1048, 2023, 167892

## Slide 29: Resonance Image system

## Slide 30: Image results
铜镜成像
铁钱成像
空速管成像
preliminary
preliminary

## Slide 31: 缪子源
Melody

## Slide 32
White neutron source
~300 MeV neutron
Proton test beam
1.6 GeV proton
muon source
CSNS Beam Expansions Application
Linac
Ion source
Synchrotron
Associated Proton beam Experiment Platform 80 MeV proton

## Slide 33: Muon Facilities Worldwide
MELODY@CSNS (constructing) HIAF/CiADS/SHINE/SULF (planning)
RAON(planning)
RCNP
Major established user facilities
TRIUMF, ISIS, PSI, J-PARC, RCNP
New facilities emerging in Asia
MELODY at CSNS — under construction, project acceptance targeted for 2029/10 with CSNS-II.
Other projects under study
*MELODY: Muon station for sciEnce, technoLOgy and inDustrY

## Slide 34: Generation of muons
Notes: When high-energy protons collide with a target, usually made of materials such as carbon or beryllium, a large number of pions are produced. Pions decay into muons and muon neutrinos. Pions have a spin of 0, so the spins of neutrinos and muons are opposite. Since the spin direction of neutrinos is always opposite to their motion direction, when we observe muons, their spin direction must be in another direction, in other words, they are polarized. Therefore, the corresponding muons can be used as magnetic probes to measure the properties of the local magnetic field of the material.

## Slide 35: From CSNS-II Proton Pulses to MELODY Muon Beams
LINAC: 300 MeV
RCS
1.6 GeV
500 kW
25 Hz
Neutron Spallation Target
MELODY
1.6 GeV
20 kW
1 Hz
1 out of 25 RCS pulses extracted by a fast kicker
Dedicated 20-kW proton beam on a thick Cu target
Surface (105~107/s), negative (104~106 /s) under construction.
Independent and beamlines support parallel operation. Decay (~106 /s) channel reserved

## Slide 36: Experimental Opportunities at MELODY
From user instruments to beam R&D and future physics
3 beamlines, 5 experimental terminals areas in full layout
SMBT1 for
Magnetic, superconducting, energy materials
SMBT2 for R&D
Muon moderation
Laser wakefield acceleration
Detector testing
beam diagnostics
MIXE/elemental analysis
Muonic-atom spectroscopy
nuclear capture
Irradiation/SEE
Deep-penetration
Deep-probing MIXE
Muography
Irradiation/SEE
Surface : 2 terminals (under construction)
Negative : 1 terminal (under construction)
Decay : 2 terminals (reserved)

## Slide 37: Pulsed Muon Beams: Opportunities and Detector Challenges
Physics opportunities
Well-defined t0 for time-resolved measurements
Timing-cuts for uncorrelated background suppression
Delayed-process studies: decay, capture, relaxation dynamics
Detector Challenges
High instantaneous rate
Pile-up and dead time
Prompt flash
Fast recovery and multi-hit readout
Continuous beam
Pulsed beam
High particle density within a short beam pulse
These requirements motivate highly segmented detector systems.

## Slide 38: µSR Spectrometer
Detector Arrays: 3024 detection units
  Large solid angle coverage: θ1 (10° ~ 40°)
  Plastic scintillator + PMT/SiPM
θ0
Detection units:
  8.8×8.8×40 mm3 plastic scintillator
  6×6 mm2 Sensl SiPM
Layout of µSR Spectrometer
Detector arrays
Detector arrays

## Slide 39: Future Physics Opportunities at MELODY
Physics priorities will evolve with commissioning, experimental R&D and user proposals.
Muon-capture
nuclear physics
Planned at terminal
Rare muon processes
Planned at surface terminal 2
True muonium
production and detection
Extension required
Capture and de-excitation
μ⁺
e⁺
μ⁻
Purely leptonic bound state
Nuclear structure and data
Muon capture and de-excitation process
Spectroscopy & PID needed
New physics beyond the standard model: charged lepton flavor violation
Fast and highly segmented tracking detector needed. Low-energy positron tagging
Exotic QED bound state, not observed yet
QED precision tests
Tracking and vertexing needed
7

## Slide 40: MELODY: From Design to Construction
Proton Beam
Target
Negative Muon
Surface Muon
2024/7
Physics Review
2025/7
Engineering Review
2026/9
Civil Construction
Completed
2028/6
Beam Commissioning
2029/10 Project Acceptance
2027/11
System Integration
Experimental hall completed
Target station shielding completed
Core container under fabrication

## Slide 41: 高能质子测试束
HPES

## Slide 42
White neutron source
~300 MeV neutron
Proton test beam
1.6 GeV proton
muon source
CSNS Beam Expansions Application
Linac
Ion source
Synchrotron
Associated Proton beam Experiment Platform 80 MeV proton

## Slide 43: Motivation: Detector Complex in Collider
Detector complex in colliders are massive but precise.
Particle trajectory resolution ~ 15 to 20 μm.
Particle energy resolution < 3%.
Particle test beams are essential throughout the entire R&D life-cycle of detectors.
There are currently no such facilities in China.
1440 chip
Si-Pixel Detector
15148 chip
Si-Strip Detector
68524 unit
PbWO4 Crystal
~70k piece
Plastic Scintillator
CMS
Name of Facility | Institute | Beamline | Country | Particle Types | Kinetics
CERN SPS North Area | CERN | H2, H4, H6, H8 | Switzerland | protons, muons, electrons, pions | 400GeV/c
CERN SPS North Area | CERN | H2-VLE, H4-VLE | Switzerland | pions, kaons | 80 GeV/c
CERN PS East Area | CERN | T9, T10 | Switzerland | Secondary particles | <15 GeV/c
DESY II TBF | DESY | TB21/22/24 | Germany | electrons | 1.5~6 GeV
FTBF | FermiLAB | -- | USA | protons | 120 GeV
ESTB | SLAC | -- | USA | electrons | 2.5-15 GeV
PF-AR | J-PARC | electron TBL | Japan | electrons | <5.8 GeV

## Slide 44: Introduction to HPES
High-energy Proton-beam Experiment Station（HPES）
First 1.6 GeV proton test beam in China.
Under construction. Pilot run at 2029.
Protons are slow-extracted by a scattering foil.
Strong and Weak beam can be provided.
Parameters | Design Value
Energy | 0.8-1.6 GeV
Frequency | 25 Hz
Strong flux | 105-108 p/s
Weak flux | 103-106 p/s
Slow extraction of proton beam.
Proton Energy:

## Slide 45: DIT Development Progress
An EUDET-type proton telescope equipped in HPES.
6 MIMOSA-28, DUT resolution reach < 10 μm.
Telescope resolution is expected reach < 5 μm.
We are also developing a telescope based on Jadepix. Prototype is under test at CERN East Area.
TRACK
A TOF spectrometer developed to measure energy.
2 LGAD, 40 m distance, E res. ~1%@1.6 GeV.
LGAD pixels are bonded in parallel to reduce readout channels.
Timing resolution of each ~ 100 ps.
ENERGY
A trigger device designed to provide time gate reference.
Scintillator fiber coupled with PMT.
Trigger time spread < 1 ns.
Prototype have been tested at CERN North Area.
TIME
DOI:10.1007/s41365-024-01447-9

## Slide 46: Applications of HPES
Tracker Calibration
  Si Pixel/Si Strip/TPC/Drift Chamber
  High position resolution（~10μm）
  Telescope @ HPES would reach 2.7μm.
Calorimeter Calibration
  EM-CAL, H-CAL, Scintillator.
  High energy resolution（3~10%）
  Energy spread of proton: <1% @1.6 GeV.
System-level test to micro-nano chip
  Super computing, intelligent computing and control systems for aerospace applications require micro-nano chips.
  GeV proton beam is preferred to evaluate the radiation resistance by cosmic ray.

## Slide 47: Civil Progress of HPES
T1
T2
Experiment hall have been finished.
Terminals will be finished by JUN. 2027.
More Detailed information can be found in Dr Yuhang Guo’ talk.

## Slide 48: CERN beam extending applications

## Slide 49
White neutron source
~300 MeV neutron
Associated Proton beam Experiment Platform 80 MeV proton
Proton test beam
1.6 GeV proton
muon source
Beam parameters |  |  | 
Beamline | Particle | Energy | flux
Back-n | Neutron | thermal-300 MeV | 1E7 n/cm-2/s
APEP | Proton | 80 MeV | 1E9 p/s
POEM | Proton | 1.6 GeV | 1E3 – 1E8 p/s
MELODY | Muon | 4 MeV | 1E5 muon/pulse
CSNS Beam Expansions Application
Linac
Ion source
Synchrotron

## Slide 50: BEAG Team
CHEN Y.H.
JING H.T.
BAO Y.
FAN R.R.
WU C.
TAN Z.X.
JIANG W.
LI Q.
YI H.
LYU Y.
GUO Y.H.
DU H.Y.
DENG Y.F.
FENG M.C.
CHEN C.
YANG Y.Q.
ZHANG M.F.
ZHU K.F.
14 staff, 6 post doc., 2 assistant, 24 students.
Deputy Director
Group Head
Research Fellow
Research Fellow
Special Research Fellow
Senior Engineer
Associate Research Fellow
Associate Research Fellow
Associate Research Fellow
Assistant Research Fellow
Assistant Research Fellow
Assistant Research Fellow
Post Doctor
Post Doctor
Post Doctor
Post Doctor
Post Doctor
Post Doctor
Nikolaos Vassilopoulos
Associate Research Fellow
LI. Y
Associate Research Fellow

## Slide 51: Summary
The China Spallation Neutron Source (CSNS) currently operates at 185 kW, providing over 5,000 h/y, with plans to upgrade to 500 kW before 2030.
Beam extension applications at CSNS include medium- and high-energy protons, white neutron beams, and muons—rare beam resources both in China and world—making it an ideal platform for detector calibration and testing.
Future physics experiments and beam measurements under these extended beam will require a large number of advanced detectors and electronic systems. CSNS is an best place for applying various new technologies:
  Higher detection efficiency
  Faster response times
  Finer granularity……
We sincerely welcome everyone in CSNS!

## Slide 52: 礼
Thanks
礼
Thanks