## Slide 1
Simulation update for HNS0
Jiangpeng Zhou, Aiqiang Guo
CCNU
2026.04.07

## Slide 2
Lambda不变质量谱修正
束流能量4.25 GeV模拟

## Slide 3: Procedure of reconstruction
Select the event, in which there are track on both the proton and pion arm
Assume the track on proton arm is proton, and pion on another arm
Determine the momentum according to the measured velocity by LGAD
Calcaulate the invariant mass of the found two particles

## Slide 4
MAPS Resolution: 5um
LGAD Resolution: 50ps
在USTC-MAPS后和LGAD前各设置了2.2mm的FR4材料
为扩大接受度，将系统沿Z轴旋转10次
产生子：Jam2
Detector Set
Geant4 Geometry
Layer | 1 | 2 | 3 | 4 | 5 | 6
Detectors | MIC6 | MIC6 | MIC6 | MIC6 | USTC-MPAS | LAGD
Material Budget | 200 um Silicon | 200 um Silicon | 200 um Silicon | 200 um Silicon | 300 um Silicon | \
Size [mm] | 30*12 | 30*12 | 30*12 | 30*12 | 21*12 | 6.5*6.5*12
LGAD

## Slide 5
Reconstruct from Hits
要求 至少 1 Hit on LGAD & 2 Hits on MAPS
遍历所有Hit组合，基于最小二乘拟合径迹
基于LGAD测量时间计算速度
假定径迹来自Proton、Pion，计算不变质量

## Slide 6
Cuts:
Decay Length > 0.5cm
DCA p-π < 0.5cm
DCA p-prim > 0.1cm
DCA π-prim > 0.3cm
Angle < 0.3 rad
Invariant Mass From Hits Reconstruction
Around 860 Lambda
820M Events From Jam2
Beam: | 1X108 (pps)
Target: | 1% C target
Cross section ratio σ(Λ)/σ(tot): | ~ 0.1 %
接受度扩大了十倍
~800 Lambda in 820M O+C Events(2.6GeV)
~合计 0.2 M Lambda in 10M Events
Efficiency ~ 5 * 10-6
据此估计，10000Lambda~23Days

## Slide 7
Reconstruct Momentum vs Truth Momentum
Truth with smearing
Truth without smearing
Pion
Proton
Lambda
距离偏小，动量偏小，导致不变质量偏小
重建动量 vs 真实动量
proton
pion

## Slide 8
Correction for Invariant Mass
x2
x0
Pion
Proton
Lambda
x1
Define:
Lambda decay time : (Unknown)
LGAD on proton arm :
LGAD on pion arm :
①
②
③
Conservation of energy and momentum:
Totally 7 equations for 4 variables: , , ,
For true event, all equations hold
Select 4 of them（①~④）and solve
④
⑤~⑦
Get

## Slide 9
Correction for Invariant Mass
This equation admits a unique solution.
Solve it numerically using Brent's method (ROOT)
When is too small for ROOT to solve, set
When the equation has no solution, also set

## Slide 10
Correction for Invariant Mass
Before correction
After correction
Total 739 Lambda
significance: 16.5
significance: 16.1
峰值得到了修正
重建效率基本一致

## Slide 11
束流能量4.25 GeV模拟

## Slide 12
 | 2.6 GeV | 4.25 GeV
Proton | 7.3 ° | 6 °
Pion | 16.6 ° | 12 °
Open Angle | 19.3 ° | 17 °
4.25GeV/u simulation
按模拟结果，4.25GeV时：
将Proton Arm放在6°
将Pion Arm放在17-6 = 11°
考虑到Lambda DecayLenth增大，以及避让束流线，将第一层Layer后移至15cm处
Layer 1~6：15, 20, 30, 40, 45, 50 [cm]

## Slide 13
4.25GeV/u simulation：Cuts
Total 238.4M 4.25GeV/u O+C from Jam2

## Slide 14
4.25GeV/u simulation：Cuts
Cuts:
Decay Length > 0.5cm
DCA p-π < 0.25cm
DCA p-prim > 0.05cm
DCA π-prim > 0.2cm
Angle < 0.25 rad
238.4M Events From Jam2
~340 Lambda in 238.4 M O+C Events(2.6GeV)
接受度扩大了十倍
~合计 0.3 M Lambda in 10M Events
Efficiency ~ 4.8 * 10-6
Jam2模型中，Lambda 产额增大了~50%
如果据此产额估计，10000 Lambda ~ 16 Days
Beam: | 1X108 (pps)
Target: | 1% C target
Cross section ratio σ(Λ)/σ(tot): | ~ 0.15 % ？
significance: 13.24

## Slide 15
Summary
模拟了HNS0原理样机重新Lambda的性能，基于现有设计可以重建出Lambda信号。
2.6 GeV/u束流能量下，HNS0张角设置为7° + 12°，10000个Lambda信号需要约3周束流时间。
4.25 GeV/u束流能量下，HNS0张角设置为6° + 11°，10000个Lambda信号需要约2周束流时间。
模拟中，4.25GeV/u下 Lambda产额相较2.6GeV/u 提高约50%。真实产额需要计算截面。
基于顶点拟合+数值求解尝试修正Lambda不变质量谱峰位置。

## Slide 16
Back Up

## Slide 17
LGAD covered by PCB
模拟了LGAD被前端的电子学板遮挡导致的影响
在第五层MAPS后和LGAD前各设置了2.2mm的FR4材料
加入FR4板材后的几何
FR4 材料参数

## Slide 18
LGAD covered by PCB
From Hits
= 22.48
From Hits
= 23.38
无FR4遮挡
有FR4遮挡
重建信号数损失约10%
显著度略降低
认为该影响有限，可以接受

## Slide 19
Different Open Angle Set

## Slide 20
Different Open Angle Set
7° Proton Arm + 12° Pion Arm is the best geometry set

## Slide 21
LGAD Time Resolution: 50~70ps
模拟了LGAD不同时间分辨率&距离靶位置下的Lambda重建情况
Time Resolution: 50, 60, 70 ps
Distance of LGAD: 50, 60, 70 cm
不同LGAD时间分辨率/位置下的重建信号数
不同LGAD时间分辨率/位置下的重建显著度

## Slide 22
Time Resolution
50 ps
60 ps
70 ps
LGAD Distance
50cm
60cm
70cm

## Slide 23
Difference between Λ / Non-Λ Events（MCTrack）
Pion
Proton
MCTrack信息（StartXYZ）中的DCA差别

## Slide 24
Difference between Λ / Non-Λ Events（MCTrack）
基于Smear后的MCTrack信息计算的拓扑量差别

## Slide 25
Different Open Angle Set
8+13
7+12

## Slide 26
Different Open Angle Set
10+15
9+14

## Slide 27
Different Open Angle Set
11+16
12+17