## Slide 1: ACTS-based 4D Tracking and a design of timing pixel chip
Hongzhang Xie, Yanqi Wang on behalf of all the contributors
on July, 2026
Notes: Hello, everyone. Today I am very glad to give the presentation presenting the progress of ACTS-based 4D Tracking and pixel digital chip design.

## Slide 2: Introduction Chance of future 4D tracking for ATLAS ITk
No time information
Add time information
Zoom in space
Separation by time
Pictures from: ATL-PHYS-PUB-2023-023: Investigating the impact of 4D Tracking in ATLAS Beyond Run 4
Motivation – LHC upgraded to HL-LHC
  Luminosity up to , pile-ups up to 200
Longitudinal view of a simulated event with <μ>= 200 in ATLAS ITk
Notes: First, it’s the reason why we study 4D tracking. LHC will be upgraded to HL-LHC after RUN 3. The luminosity will reach up to 7.5 times nominal value, which corresponds to up to 200 pile-ups. Higher luminosity can provide more dataset, but, as well as more challenges.
The four plots show the longitudinal view of a simulated event with 200 pile-ups in ATLAS Inner Tracker. The first plot is tracking without time information. Lines are the tracks and dots are the vertexes. The second plot is an illustration of adding time information to the track, with different colors representing different time. If we add a time cut of 30 ps, the hard-scatter vertex will be able to be separated from other vertexes by time information.
i.e. time information has the ability to improve the performance of tracking, a step forward, the performance of physics measurement
First, it’s the reason why we study 4D tracking. LHC will be upgraded to HL-LHC after RUN 3. The luminosity will reach up to 7.5 times nominal value, which corresponds to up to 200 pile-ups. Higher luminosity can provide more dataset, but, as well as more challenge.
The four plots show the longitudinal view of a simulated 𝑡𝑡 ̅ event with 200 pile-ups in ITk. The first plot is tracking without time information. Lines are the tracks and dots are the vertexes. The second plot is that we add time information to the track, with different colors representing different time. If we add a time cut, the hard-scatter vertex will be able to be separated from other vertexes by time information.

## Slide 3: Introduction Chance of future 4D tracking for ATLAS ITk
The two innermost layers of the ATLAS ITk Pixel﻿ is designed for a maximum luminosity of 2000 fb−1.
Chance to implement 4D tracking for ATLAS in the middle of HL-LHC operation:
  Efforts in hardware and software
  Need to understand the physics potential
  This talk reports the progress of low-level 4D tracking and a design of timing pixel chip
﻿The total ionizing dose distributions for the ITk Pixel Detector.
<5 MGy in 4000 fb-1 for unreplaceable part
up to 10 MGy for 2000 fb-1 for Layer 0
ATLAS-TDR-030 Inner Tracker Pixel Detector
Notes: The two innermost layers of the ATLAS ITk Pixel﻿ is designed for a maximum luminosity of 2000 , which needs to be replaced during the operation of LHC. The right plot shows the simulation of the total ionizing dose distributions for the ITk Pixel Detector.
So, it’s an opportunity to implement 4D tracking during the pixel replacement.
And (possible) implementing 4D tracking needs efforts from both hardware and software, to understand the physics potential of using time information.
This talk will report the progress of low-level 4D tracking and a design of pixel digital chip
Grey
The two innermost layers of the ATLAS ITk Pixel﻿ is designed for a maximum luminosity of 2000 𝑓𝑏^(−1), which needs to be replaced during the operation of LHC. You could see in the right plot that.
So, it’s an opportunity to implement 4D tracking. And implementing 4D tracking needs efforts from both hardware and software, to understand the physics potential of 4D tracking.
This talk will report the progress of low-level 4D tracking and a design of pixel digital chip
Grey

## Slide 4: 4D tracking with ACTS

## Slide 5: Introduction to Software
ACTS (A Common Tracking Software) is an experiment-independent toolkit for (charged) particle track reconstruction in (high energy) physics experiments
track parameters in ACTS
Smear truth hit information in the ITk innermost 2-layer pixel region with gauss distribution
a rough estimation of hardware
ACTS GitHub: https://github.com/acts-project/acts
ACTS docs : https://acts.readthedocs.io/en/latest/index.html
Notes: ACTS is an experiment-independent toolkit for (charged) particle track reconstruction in (high energy) physics experiments, which will also be used in ATLAS Run 4 ITk reconstruction.
ACTS has 6 parameters in its track parameters, which includes time information. And this would benefit the studies on 4D tracking.
The results we show later will use the ITk geometry, and smear truth hit information in the ITk innermost 2-layer pixel region with gauss distribution using 50 ps time resolution, to provide time measurements. This number is a rough estimation from the hardware.

## Slide 6: Full chain workflow in ACTS
Fatras / Geant4
simulation
digitization & clustering
seeding
use smeared hit information
vertexing
time information
with time algorithm
propagate time information, not used in algorithms
track finding& fitting (CKF)
Notes: This is the full chain tracking workflow in ACTS. First is Fatras/Geant4 simulation, simulating a particle going through the detector. (Fatras is a fast simulation implemented in ACTS. 这句可以略掉) Followed is digitization, simulating the detector electronic response. And clustering, organizing several cells and producing spacepoints. Seeding will combine the spacepoints to form initial tracks. Then is track finding and fitting, which extends the initial tracks. Finally it’s vertexing, to find where an interaction or a decay occurred.

## Slide 7: Full chain workflow in ACTS
Fatras / Geant4
simulation
digitization & clustering
seeding
track finding& fitting (CKF)
use smeared hit information
vertexing
with time algorithm
time information
studying in Athena
studied in ACTS
propagate time information, not used in algorithms
Notes: ACTS tracking algorithms could prograte time information from truth simulation information to track and vertex.
From the start of the tracking workflow, now we are doing some studies of digitization and clustering in Athena framework(, in collaboration with CERN group). There are already some studies on 4D vertexing in ACTS with ODD geometry, which shows that timing could improve the performance of vertexing. This presentation will show the algorithms and performance of 4D seeding, as well as the performance of 4D tracking.
oblique line

## Slide 8: 4D seeding algorithm
Variable for spacepoint
A gauss filter for doublets & a chi-square filter for triplets
truth-matched
Doublet - Normalized distribution of
Triplet - Normalized distribution of
Chi-square distribution with dof =2 for truth-matched
Notes: In the 4D seeding algorithms, an additional variable is introduced for spacepoint, which is defined as the time of arrival substracted by the time of flight. It describes the original time of the particle/track.
Since a traditional seeding algorithm would combine three spacepoints into one seed. A gauss filter for seed doublets and a chi-square filter for seed triplets are introduced to filter truth-matched seeds with time information.
From left plot, we could see that, the gauss discriminator of doublets from truth-matched seeds follows gaussian distribution with a resolution of square root 2 times the resolution of a time measurement. While doublets from fake seeds have a flatter component contributing from pile-up time distribution.
In the right plot, with the chi-square discriminator, truth–matched triplets follow the distribution of chi-square with 2 degrees of freedom. While fake triplets have more components n the tail.
With those discriminators, truth-matched seeds could be separated from fake seeds, in time dimension.
In the 4D seeding algorithms, an additional variable 𝑡_0 is introduced for spacepoint, which is defined as the time of arrival substracted by the time of flight. It describes the original time of the particle/track.
Since a traditional seeding algorithm would combine three spacepoints into one seed. A gauss filter for seed doublets and a chi-square filter for seed triplets are introduced to filter truth-matched seeds with time information.
From left plot, we could see that, the gauss discriminator of doublets from truth-matched seeds follows gaussian distribution with a resolution of square root 2 times the resolution of a time measurement. While doublets from fake seeds have a flatter component contributing from pile-up time distribution.
In the right plot, with the chi-square discriminator, truth–matched triplets follow the distribution of chi-square with 2 degrees of freedom. While fake triplets have more components n the tail.
With those discriminators, truth-matched seeds could be separated from fake seeds, in time dimension.

## Slide 9: 4D seeding performance
Only apply triplet cut
No time cut
（base line）
p-value: corresponds to the probability of excluding a truth-matched seed by cut
higher efficiency and lower fake rate with time cut
Using pixel (5 layers) spacepoint seeding
Adding time for innermost 2 layers
Notes: Here we see the final 4D seeding performance. Remember that we are using 5 pixel layers to do seeding, and adding time measurements to the innermost 2 pixel layers.
In the left plot, the color shows the p-value corresponding to the probability of excluding a truth-matched seed by time-cut.
With different configurations of time-cut, compared with no time-cut configuration (red dot) , we could achieve better seeding purity (x-axis) and seeding efficiency (y-axis) at the same time.

## Slide 10: 4D tracking performance
RED (4D tracking): CKF initial track parameters and measurements have time information
BLUE (3D tracking): no time information for CKF initial track parameters and measurements
Tracking efficiency
93.72% (no timing) to 94.87%↑ (50 ps timing)
93.71% (only “measured” time for initial track parameters)
93.63%↓ (only time for measurements)
Event generation: events =200 with Pythia 8
Fatras simulation & Truth-Smeared seeding
Improvements from adding time for both initial track parameters and measurements to innermost 2-layer pixel
Combinatorial Kalman Filter
Notes: Following the seeding, it’s track finding and fitting. ACTS track finding and fitting uses Combinatorial Kalman Filter, and involves time in its track parameter, so it could process time information automatically within Kalman formation.
The simulated events are ttbar events with 200 pile-ups.
Here we used fast simulation, and didn’t use any 4D seeding algorithms (even without any seeding algorithms), instead, we use truth-smeared particle information to form initial track parameters.
And finally, we could see improvement on tracking efficiency if we add time in both initial track parameters and measurements.

## Slide 11: A design of Timing Pixel chip

## Slide 12: Overview
Modules for the Readout ASIC:
  Pixel: Amplifier, Discriminator, Time-to-digital converter, 200 μm×200 μm
  Cores Array: 1 core includes 88 pixels, same as ITKPix. 8 pixels are in one region.
  Periphery: End of Column, Chip Bottom.
Overview
Core Array
Periphery
Pixel circuit
Notes: This is the overview of the structure of the readout chip. The chip has core array and periphery circuit.
In the core array, every core has 8 x 8 pixels. 8 pixels are in one region.
Every pixel could achieve amplification, discrimination, and time measurement.
In the periphery (/pəˈrɪfəri/)(per-ri-fer-ri), it needs to do the data readout and concentration. It consists of some EOCs and a Bottom.

## Slide 13: Pixel: Analog Front-end
Amplifier
Discriminator
Precisions of Amp. + Discr.
（130nm）
Two-stage Amplifier:
  Charge sensitive amplifier: folded cascode + Voltage Amp.
Two-stage Discriminator：
  Differential driver: positive feedback
  Common source driver: saving power
3D sensor@3fC
Notes: First, it is the Analog Front-end in the pixel. It includes a two-stage amplifier and a discriminator.
We use two-stage structure to amplify the weak signal from the sensor. The first is a CSA with a folded cascode. It uses MOS reset feedback. And the second one is a voltage amplifier.
The discriminator is also a two-stage one. And the figure on the right shows the precision simulation of the front-end in different input charges.
Amp. Power ~ 40 μA
Disc. Power ~（16~21） μA

## Slide 14: Pixel: Time to Digital Converter
Designs for Time to Digital Converter
Delay line + Loop counter:
  Edge detector
  SR latch
  ToA & ToT measurement ( bin size ~ (90~120) ps )
Designs for Time to Digital Converter
ToA measurement:
  Line’s cycle + Line’s phase
ToT measurement
  Only line’s cycle
Notes: The next part is the TDC. We used the delay line combining a loop counter. It can reduce the area greatly.
Hit would enter the loop and TDC would latch the state when the clk arrives.
ToA and ToT measurement would shared the same loop.

## Slide 15: Core
The cluster size
Shared map
Shared memory structure:
  Reduce the storage space due to the sparse hits
Factors:
  All pixels shared are need to be independent.
  The cluster size effect is universal in the detector.
Eliminating the cluster effect:
  Using a specific map to share the pixels
Storage space
Notes: To hold the TDC data and the hit rate, we use a shared memory structure. The hits are often sparse, that give us a thinking. Some pixels could shared the storage space to avoid being the idle.
We did a simulation to verify the idea, as the figure shows on the right. As the shared pixels increase, the storage space could be used more fully, the storage units per pixel decline.
This structure need a condition, the hit data of these pixels needs to be independent. So we need to eliminate (/ɪˈlɪmɪneɪt/) the cluster effect.
We use a specific shared map, as the figure in the middle shows, the same color pixels are shared, to Eliminating the cluster effect.

## Slide 16: Core
Core degin:
  8 × 8 pixels, core is same as others and they are connected as a chain
  Receiving and buffering data from TDC
  completed the trigger matching
Shared memory structure:
  8 pixels shared in one region
  One core consists of 8 regions
Readout:
  Priority readout
  Core column readout to the End of column
Core array
Core design
Core Column
Notes: In the digital core, its function is receiving and buffering data from TDC, and completed the trigger matching.
We design a shared memory structure to reduce memory. Each core consists of several regions. All pixels in the same region shared a same memory.
In the core column, the region data would be readout in priority to the End of column.

## Slide 17: Region
Shared memory structure (eg. 1 region)
Processing the trigger matching
Managing the pixel order
Functions:
  Storing the time stamp (BCID) and TDC data, doing the trigger matching.
Two priority arbiters for Leading Edges and Trailing Edges:
  Manage the address of memory.
Every cell in shared memory needs a FSM to process trigger matching.
Notes: Based on the shared memory structure, we design the region circuits.
In the region, we design the priority (/praɪˈɒrəti/) arbiters (/ˈɑːbɪtə(r)/) , data selectors, memory address manager to control the storage of the shared memory.
In the memory, each cell stores one hit per pixel and it needs a state machine to process the trigger matching.

## Slide 18: Simulation
The performance of shared memory (eg.8-pixel)
The power comparison for the layout
The area comparison for the layout
Lost rate lower than the red line (1%)
The simulation results (in 130 nm)
  Holding the corresponding data rate (~75 kHz/pixel)
  Lower power, Lower density.
  Shared memory could reduce power and area obviously.
Notes: According to the design of the core and region mentioned above, we simulate the power and area to verify our shared memory scheme. We completed the core layout.
On the left, it shows that, the circuits can handle the hit rate. 8 pixels are shared, and when we hold the most of hit data, we need 15 units in the memory. And the figure shows the frequency of each unit being used when it works.
And the figure on the right shows that, our circuit really consumes a lower power compared to a rd53b-like structure, // which is used in the ATLAS ITK (?)

## Slide 19: Periphery
Overview
Core Array
Periphery
Data flow
EOC design
Modules for the Periphery:
  End of Column: packaging and encoding and compressing the data.
  Bottom: concentrating the chip data and control the trigger.
Notes: This is the overview of the structure of the chip data flow
In the periphery (per-ri-fer-ri), it needs to do the data readout and concentration. It consists of several EOCs and one chip bottom.
In the end of column, we add encoding and packaging module to compress the hit data.

## Slide 20: End of Column
End of Column:
controlling the readout of core column, and packaging the hit data
Shared memory:
Disrupt the order of reading data from the core.
Breaking up the concentration of clusters. Making data more dispersed which is not conducive to data compression
Packaging area:
8 pixels
EOC design
Remap module:
Reorganizing the hit as the packaging area.
The packaging area use the cluster effect to concentrate the data.
Remap data to make it more concentrated
phi
eta
:
Notes: Packaging by the physical position and the cluster size can reduce the data bits.
But the shared memory disrupt the order of reading data.
So, we use a remap module to reorganize the hit as the packaging area.
The orange box in the figure show how we reorganize the hits.

## Slide 21: End of Column
Packaging data: coarse address + hit map + hit data
Encoder:
Based on the frequency distribution of hit-map in simulation data, use Huffman encoding to compress the hit-map
hit data
coarse address
hit map
Encoding of hit map |  | Entropy
Bitmask |  | 8
Binary-tree |  | 7.79
Independent address |  | 11.20
Multi-stages Hoffman | 4-6-14 | 7.17
 | 3-6-14 | 7.84
 | 6-14 | 6.34
EOC design
Hoffman coding to compress
A data packet
Encoding schemes
Encoding schemes:
Comparing several compression schemes to get the best
Compression efficiency:
packaging + Huffman  ~73% (27% reduced)
Notes: After the packaging, we get the data packet on the bottom. The hit map part could be compressed further.
We compared some encoding schemes, and finally, we use the Huffman encoding.
Based on the frequency distribution of hit-map of the hit data, we encode it by Multiply stages.

## Slide 22: Bottom
Trigger Table logic
Functions for the Bottom:
  Trigger table: manage the trigger and generate the trigger ID to control the readout.
  Data concentration: concentrating the chip data.
Notes: Finally, it’s the bottom circuits. Bottom need to manage the trigger and generate the trigger ID to control the data readout from the pixel array (core array).
And it also need to concentrating the chip data.

## Slide 23: Summary
4D tracking
  ACTS simulation & tracking workflow is powerful for 4D tracking study
  Investigating and implementing 4D seeding & track finding/fitting algorithms with ACTS
  – possibilities of improvement
  Studying 4D tracking workflow in ATLAS Software Framework
  Outlook: physics case using the 4D tracking + 4D vertexing + 4D flavor tagging
Timing Pixel design
  the overview of the chip design scheme: Pixel, Core array, Periphery.
  Pixel: Amplifier, Discriminator (precision sim. < 80ps), Time-to-digital converter
  Core array: the shared memory structure, Eliminating the cluster effect
  Periphery:
    End of column: remap, package, encode the hit data to compress data bits
    Chip Bottom: concentrating the chip data
Thanks!

## Slide 24: Back-ups

## Slide 25: Timing pixel digitization in Athena
Digitization
  simulate detector response from hit simulation information
  HIT (Geant4 simulation) -> RDO (Raw data output)
  (position, charge…) -> (identifier/position of cells, ToT, ToA)
Geant4 hit time
fast time digitization
more realistic digitization
(the same method with HGTD)
smeared time
(add random gaussian distribution)
simulate pulse and calculate ToA
based on parameterized pulse waveform
digitized time
stored in RDO
1.732 ns
1.851 ns
00011010…
example
Graphs from ACTS docs

## Slide 26: Purity and track-only impact parameter resolution
No significant change on the resolution of impact parameters

## Slide 29
Vertex distribution / ps | 5000 | 500 | 200 | 100
/ mm |  | 21.67 | 21.68 | 21.56
/ mm |  | 215.8 | 108 | 81.14
fake / mm |  | 21.41 | 21.62 | 21.57
fake / mm |  | 226.9 | 114.2 | 87.49
fake / ps |  | 757 | 381 | 292
/ps |  | 711 | 292 | 158
Vertex distribution / ps | 5000 | 500 | 200 | 100
 |  | 21.67 | 21.68 | 21.56
 |  | 215.8 | 108 | 81.14
 |  | 21.41 | 21.62 | 21.57
 |  | 226.9 | 114.2 | 87.49
 |  | 757 | 381 | 292
 |  | 711 | 292 | 158
21.199 mm

## Slide 30: ITk spacepoint distribution

## Slide 31: 4D seeding performance with ITk

## Slide 32: Huffman coding
Sort | Hit-map (bitmask) | Frequency | “6-14” mode bits
1 | 10101010 | 6.966% | 6
2 | 01010101 | 6.418% | 6
3 | 01000000 | 6.183% | 6
4 | 00000010 | 5.784% | 6
5 | 00000011 | 5.175% | 6
6 | 11000000 | 4.533% | 6
7 | 00000001 | 3.960% | 6
… | … | … | 
64 | 11101010 | 0.173% | 6+8
65 | 11110100 | 0.173% | 6+8
66 | 00110101 | 0.150% | 6+8
… | … | … | 
Encoding of hit map |  | Entropy
Bitmask |  | 8
Binary-tree |  | 7.79
Independent address |  | 11.20
Multi-stages Hoffman | 4-6-14 | 7.17
 | 3-6-14 | 7.84
 | 6-14 | 6.34
Encoding schemes
Huffman Encoding schemes (eg. 6-14 mode):
For the first 63 high-frequency hit-maps: use 6 bits to encode.
Since 6 bits correspond to 64 combinations, the last combination will be used as the header for other 193 hit-maps.
For the other 193 hit-maps: 6 bits header + the original bitmask hit-map (8 bits)
Bitmask: 1 bit for 1 pixel,
1 for hit and 0 for not