## Slide 1
STCF BTOF Simulation, Digitization and Reconstruction
Speaker : Teng Ma

## Slide 2: OutLine
Introduction
Optimization
Full-Chain Analysis
--- Simulation
--- Digitization
--- Reconstruction
Summary

## Slide 3
Introduction

## Slide 4: STCF Introduction
STCF Future Performance :
Center of Mass Energy :
Peak Luminosity :
Cross Angle :

## Slide 5: BTOF Introduction
(R~885mm)
High time precision acquired with MCP-PMT
Dispersion effect need to be reduced (Add wavelength filter)
Consistent with electronics of DTOF detector

## Slide 6
Optimization

## Slide 7: Pixels Optimization
Polar Angle / deg (p=2GeV) | 37 | 55 | 65 | 85
16*1 Division / (/K) | 3.89 | 3.70 | 3.78 | 4.15
4*4 Division / (/K) | 3.96 | 4.04 | 3.97 | 4.3
Polar Angle / deg (p=2GeV) | 37 | 55 | 65 | 85
 | 3.89 | 3.70 | 3.78 | 4.15
 | 3.96 | 4.04 | 3.97 | 4.3

## Slide 8: Geometry Optimization
In each sector, two silicon quartzs are connected with grease instead of absorbing coat on inner side.
Performance when large polar angle is hoped to be improved.
Polar Angle / deg (p=2GeV) | 37 | 55 | 65 | 85
Before Coupling / (/K) | 3.96 | 4.04 | 3.97 | 4.3
After Coupling / (/K) | 4.00 | 4.09 | 3.98 | 4.6
Polar Angle / deg (p=2GeV) | 37 | 55 | 65 | 85
 | 3.96 | 4.04 | 3.97 | 4.3
 | 4.00 | 4.09 | 3.98 | 4.6
Much improved!
Comparison (85 polar angle)

## Slide 9: Geometry change
To reduce the material and ensure eough number of photon electron, the thickness of quartz plate is reduced to 15mm, and the wavelength cut is chosen to be 320nm.
The PID performance and the with thickness of quartz plate equal to 15mm, and the blue line represents the level of the original version (20mm && 375nm)

## Slide 10: Geometry Optimization
An extra optical expansion is added on the outer side of the quartz plate
Performance at high momentum will be obviously improved.
Θ=65°
Φ=90°
15mm
25mm

## Slide 11: Full-Chain Analysis
Geometry
Manager
Simulation
RunAction
EventAction
TrackingAction
SteppingAction
BarHit
PDHit
Digitization
Bkg mix
Electronic
Time-walk effect
Dead time
Digi Parameter
PD information after Digi
Reconstruction
Uncertainty

## Slide 12
Simulation

## Slide 13: BTOF Geometry
12 sectors, each corresponds with azimuthal angle and has two silicon quartzs covered by an AHP shield.
Two bearby quartz plates connected and MCP-PMTs ( pixels) on outer side of quartz.
Extra optical expansion added to suit existing size of PMT.
Electronic module added in OSCAR Geometry
1515mm
15mm
450mm
80mm
80mm

## Slide 14: Simulation Result
The 2D time vs ChannelID distribution and the distribution with p=2GeV, θ=65°and Φ=90°

## Slide 15: Distribution
distribution of pion

## Slide 16
Digitization

## Slide 17: BTOF Digitilization
Digitilization processes:
Simulate the performance of photon electron in MCP-PMT.
Add Time-Amplitude Wandering Effect, uncertainty and dead time (5ns).
Output channelID, TOA, TOT as input of reconstruction algorithm.
Digitilization parameters:
TOT = TOTDis->GetRandom() (3 Gauss)
TTS = TTSDis->GetRandom() (2 Gauss)
TOTtru = TOT + Gaus(0, 10ps)
TOTMEAN = 780ps TOT_CALIPAR = 0.35
TOA = time + TTS + (TOTtru - TOTMEAN) * TOTCALIPAR
TOA-Timetru : TOT
TOA-Timetru : TOT
(after correction)

## Slide 18
Reconstruction

## Slide 19: Timing Method
XOZ Plane
Photon direction in XOZ(, )
Reconstruction Principle
For each k, we calculate and
The photon path with minimum is selected
( not )
(TIR1)
(TIR2)

## Slide 20: Timing Method
recTOF () distribution can be described with 3 Gauss model :
Gaus1 is the main peak, Gaus2 represents the effect caused by TTS, Gaus3 represents the impact caused by multi-scattering.

## Slide 21: Imaging Method
Create a 2D time-channel PDF for each track to calculate likelihood conveniently.
Wavelength(), particle track in the radiator and are divided into many intervals.
For each bin we can calculate the reaching channel and time of the Cherenkov photon, and fill the PDF.
Propagation efficiency is also taken into consideration.
The red dots and COLZ PDF represent simulation data and calculated PDF
Good agreement between calculated pattern and simulation

## Slide 22
PID Performance

## Slide 23
Performance between
Separation between
(under 1bkg)
Efficiency of (misID=2%)
(under 1bkg)

## Slide 24
Performance between
Separation between
(under 1bkg)
Efficiency of (misID=2%)
(under 1bkg)

## Slide 25: Summary
BTOF simulation, digitization and reconstruction have been completed.
The separation performance between have reached to 4σ around 2GeV, which can meet the STCF PID requirement.
Optimization of geometry change finished can improve PID performance.

## Slide 26
Back Up

## Slide 27: Simulation Parameter
Cherenkov photon with wavelength less than 320nm is neglected to reduce dispersion