## Slide 1: Electromagnetic Calorimeter Software for Super Tau-Charm Facility
Bo Wang
University of Science and Technology of China
State Key Laboratory of Particle Detection and Electronics
(On behalf of the STCF ECAL working group)
超级陶粲装置研讨会
2026年7月2日，西安

## Slide 2: Super Tau-Charm Facility
Electron-positron collider experiment
High luminosity：beyond @ 4GeV
Wide energy region：center-of-mass energy range of 2~7 GeV
Multi-Linac
Total 550 m
Positron Damping Ring 150 m
Collider Ring
860 m
New generation Spectrometer
Center-of-Mass energy coverage : 2-7 GeV;
Peak Luminosity > 0.51035 cm-2 s-1 @ 4GeV
Potential to increase lumi. & realize beam polarization

## Slide 3: Requirements for ECAL
Fast response
  Challenge of high Luminosity
    High count rate
    Extremely high background
High precision
  Energy resolution
    Better than 2.5% @1GeV
  Position resolution
    Approximately 5mm @1GeV
  Time resolution
    Better than 300ps @1GeV
Energy distribution for photons

## Slide 4: ECAL Geometry Optimization
Total absorption calorimeter
  Barrel:
  Endcap:
  11% volume reduction

## Slide 5: ECAL Full Chain
Simulation
ECAL Hit Slide
Digitization
ECAL Digi
event
Reconstruction
ECAL Shower
Simulation
  Geant4 based
  Vertical Layered Crystal Data Structure
Digitization
  Waveform shaping
  Waveform fitting
    Peaking finding method
    Template fit method
    Pipeline fit method
Reconstruction
  Classical cluster reconstruction method
  4D Cluster reconstruction

## Slide 6: Simulation Algorithm
Based on Geant4 Simulation
  Process the information for each Geant4 step
Data Model (layer as a unit)
  Thickness 2cm as a layer unit
  Each unit with a energy-time distribution:
  points with (E,T)
  Bin width 500ps for energy-time distribution
  Save storage space
  Minimal loss of information
  Facilitate the Digitization
28cm
2cm

## Slide 7: Digitization Algorithm
Waveform shaping
Points (E-T) in each layer unit
Light output nonuniformity
Fluorescence transfer parameterized simulation
Geant4 optical simulation for each layer unit (standalone)
Sampling
Scintillation process
convolution
Electronics response function
Electronic noise
ADC (12.5ns)
Output waveform
Strategy 0

## Slide 8: Digitization Algorithm
Waveform shaping
Points (E-T) in each layer unit
Fluorescence transfer parameterized simulation
Sampling
Scintillation process
convolution
Electronics response function
ADC (12.5ns)
Points (E-T) in each layer unit
Fluorescence transfer parameterized simulation
Scintillation process
Electronics response function
ADC (12.5ns)
convolution
Strategy 1
Time: 15ss per event
Strategy 2
Time: Comparable

## Slide 9: Challenges of high background
Luminosity-related Background
  Radiative BhaBha Scattering (RBB)
  Two Photon Process
  Variation of the background counting rate with polar angle
  Counting rate reaches the order of MHz
Single-beam related Background
  Thouschek Effect
  Coulomb Scattering
  Bremsstrahlung
  Momentum distribution of background particles
  Most background particles concentrate in the low momentum region

## Slide 10
Pile-up is superimposed on the signal waveform
  Inaccurate fit results of amplitude and time
  Larger resolution of energy and time
The amplitude of signal is distorted
Pipeline fitting method
Multi-template fit
  Has been used to study the capability for pile-up recovery
Digitization Algorithm
Pile-up recovery
2025 Beam
Accuracy unsatisfactory!

## Slide 11
Pipeline fit
Interpolation fitting
  Real-time online processing
  Template fit once for each fitting
    Each fitting begin with different ADC point
    Add one more fitting between two ADC points
  Fit successful
    :
  Cache and compared with next fit
  Remove template
  Ongoing processing
Digitization Algorithm

## Slide 12
Pipeline fit
A-T correction
  Real-time online processing
  Template fit once for each fitting
  Fit successful
  Correction with control sample
Digitization Algorithm
After Correction
Before Correction

## Slide 13: Reconstruction Algorithm
A complete reconstruction algorithm of ECAL is developed
ECALRecAlg
Cluster search
Seed search
Clusters split into Showers
Calculation and correction of shower energy and position
Cluster (two photons)
Seed
Energy distribution of 1GeV with background
Fitted by Crystal Ball function
Energy resolution defined by

## Slide 14: Reconstruction Algorithm
No Time information
DigiHit
  The Digi with max energy will be chosen as the Hit to reconstruct the shower
HitCluster
  The connected ignited crystals will be treated as a Cluster
Background
  Affects signal resolution
  A large number of fake photons
  Affects mass resolution
w/o bkg
w bkg

## Slide 15: Reconstruction Algorithm
4D Reconstruction
  Seed finding in 3D space with timing information
  Add time selection while reconstructing Cluster
w bkg
w/o bkg

## Slide 16
@ 1 GeV
@ 0.1 GeV
With background
Meet the requirement
Good energy linearity in the energy range of 100 MeV ~ 3.5 GeV
Reconstruction Performance
Energy Reconstruction

## Slide 17
ps @ 1 GeV
Fitted with Gaussian function
With background
Meet the requirement
Reconstruction Performance
Time Reconstruction
1 GeV

## Slide 18
Splitting algorithms (used by BESIII and Panda)
Barycenter method
  Where
Reconstruction Performance
Position Reconstruction
mm @ 1 GeV
With background
Meet the requirement

## Slide 19
Reconstruction Performance
Reconstruction
~1 GeV
with the minimum
sample
MeV/ @ 1 GeV
With background
Truth matched

## Slide 20: Summary
The software of ECAL has been established based on OSCAR
The simulated performance of ECAL meets requirements with the background concerned
  Energy measurement with 2.03% @ 1 GeV
  Time measurement with 130 ps @ 1 GeV
  Position measurement with 5.3 mm @ 1 GeV
  mass measurement with 5.6 MeV/ @ ~1GeV
Prospect:
  Verify and update digitization to align with beam test data
  dE/dx for simulation to describe hardon waveform
Thanks for your listening!

## Slide 21: Back up

## Slide 22: ECAL Design
Total absorption calorimeter
  Barrel:
  Endcap:
  Crystal Size:
Sensitive Unit
  Pure CsI (pCsI) crystal
    Fast decay time (~30ns)
    Good radiation hardness
    Low light yield
  Avalanche photodiode (APD)
    Short wavelength type
    Large area ()

## Slide 23: ECAL Design —— Sensitive Unit
Pure CsI crystal + APD photo-device
  Pure CsI (pCsI) crystal
    Fast decay time
    Good radiation hardness
    Low light yield
  Crystal Size:
      Total radiation length
      15 (28 cm)
    End face size
  front end: ~
  back end: ~
  Avalanche photodiode (APD)
    Short wavelength type
    Large area ()
APD
pCsI
ECAL pCsI crystal unit

## Slide 24: ECAL Setup
“Dead Material”
  150-µm Teflon reflective film
  75-µm polyethylene insulating film
  75-µm Al electrostatic shielding film
  No supporting material
Light Yield: p.e./MeV
Light Collection Non-uniformity
  collection efficiency:
MeV
MeV
Secondary Particles Hit APD
2.5cm

## Slide 25: ECAL Electronics
Charge sensitive amplifier and pole-zero cancellation with shaping time 100 ns
High and Low Gain (300 MeV/3000MeV)
16-bit ADC (~16000 channels) with 80 MHz sampling rate

## Slide 26: Digitization Algorithm
Waveform check
100 ns
30 ns
< 1.0 MeV
L.Y. > 100 p.e./MeV
100 ns
30 ns + 85ns
< 0.4 MeV
L.Y. > 300 p.e./MeV

## Slide 27: Digitization Algorithm
Waveform fitting
Template fit to extract Amplitude and Time
  Find the points around amplitude peak to do the template fitting
  Template shape function:
  Apply
  Where and are from readout waveform; the electronics foundation in digitization is ; and are the amplitude and time from fitting result; is the noise covariance matrix.
Pipeline fit for pile-up recovery

## Slide 28
Sizes of thickness and time bin width have been optimized
  No large difference of time distribution for different thickness
    Consider the non-uniformity may vary in the future : 2cm
  Different time bin width with different time resolution and central value
    Difference in central value approximately equivalent to a shift of the template
    Consider the resolution and the similarity to the template: 500ps
Simulation Algorithm
Data Model

## Slide 29
Energy distribution and comparison with template
Simulation Algorithm
Data Model

## Slide 30
Before Correction
After Correction
E Correction
T Correction
A-T Correction

## Slide 31: Template Fitting
  Template shape function：
  Apply :

## Slide 32: Nonnegative Least Square (NNLS)

## Slide 33
Fit all the potential waveforms with template
Isolate signals by time
The fit minimizes the defined as:
  Where:
  N is the number of templates;
  vector comprise the readout samples;
  vector is the waveform template;
  are the amplitudes, which are obtained by the fit;
  is the noise covariance matrix.
Pile-up Recovery
Multi-template fit

## Slide 34: 4D Reconstruction Algorithm

## Slide 35: Electron PID Algorithm
E/P ratio
  E: Energy of ECAL Shower
  P: Momentum from Track
  ;
  Poor performance in low-momentum
BDT Method
  Input variables: charge, , , E/P, , , , , , , second moment, lateral moment, moment, moment
  Distinguishing electrons from other charged hadrons (or muon)
  BDT Method used

## Slide 36: BDT Input

## Slide 37: BDT Output
e
K
p

## Slide 38
桶部角分布相同
  共53圈（左右各加一圈）
端盖重新排列
  最外层与桶部最外层平行
  间距4cm
  散焦点10cm
  尺寸变小
  共89圈
端盖边界1640mm
体积 6.47
节约 11%
MDC
PIDE (RICH/ASHIPH)