## Slide 1: Performance of the LHCb muon detector in Run 3
汇报人：马博 胡涌泉 聂雨

## Slide 2: upgrade
The LHCb Experiment and Run 3 Upgrade
LHCb is a dedicated heavy flavor physics experiment at the LHC, covering the rapidity range 2<η<5, mainly studying particles containing c and b quarks.
Run 2 (2015–2018): Instant brightness L = 4 × 10^32 cm⁻² s⁻¹
Run 3 (2022–2026): The instantaneous luminosity increases 5 times, reaching L = 2 × 10^33 cm⁻² s⁻¹.

## Slide 3: upgrade
The μ detector is located at the very end of the spectrometer
and consists of four rectangular stations, M2–M5, with 80 cm thick iron absorbers between the stations.
Main function: muon identification,
providing triggering and offline selection
for physics analyses
with a large number of muon final states.

## Slide 4: upgrade
MWPC
1、Particle traversal
2、Gas ionization
3、Electron drift
4、Avalanche multiplication
5、Signal generation

## Slide 5: upgrade
Horizontal strip: Sections from the cathodic pads
Vertical strip: Groups from the anode wires
x
y
A front view of a detector station

## Slide 6: upgrade
goal：Maintain or even improve the μ particle identification performance of Run 2：
  muon efficiency >90%
  Hadron misidentification rate <1%
The R2/R3/R4 of M2 and R4 of M5 removed the logic merge layer, which increased granularity and reduced dead time.
Aging Assessment

## Slide 7: Calibration (Time & Space)
Time calibration
指标 | 校准前 | 校准后
信号峰与 BXID 窗口中心偏差 | 可达 ±10 ns 以上 | < 1 ns
单站 hit 效率 | 可能低于 90% | > 99%
误归束团的比例 | 不可接受 | 可忽略

## Slide 8: Calibration (Time & Space)
Time distribution of the nODE channel .
The blue vertical line marks the center of the target BXID (25 ns window).
There's a tail near the signal peak.
Delay settings for all 32 channels on the node

## Slide 9: Calibration (Time & Space)
Space calibration
由于维护后探测器站的实际位置会偏离设计值，需要精确测量每个 μ 子站的偏移量
虚线框：μ 子站标称位置
实线框：μ 子站真实位置（带偏移）
：Expected hitting point
： Actual hit point

## Slide 10: Calibration (Time & Space)
空间分辨率= Pad尺寸/
​Pad尺寸：这是指探测器读出单元（物理Pad）的宽度。当粒子击中一个Pad时，我们只能知道它落在了这个Pad的范围内，而不知道具体在里面的哪个精确位置。
红/蓝点（空间分辨率）：这是探测器本身的“硬件限制”。它主要由读出条的宽度（即pad尺寸）决定，R1区域最精细，R4最粗糙，所以分辨率从内到外逐渐变差。
洋红线（多次散射）：这是物理过程带来的“原理性限制”。μ子穿越物质时会发生微小偏转，导致其实际到达位置与直线外推的位置有偏差。这限制了探测器能“看清”的极限。

## Slide 11: Testing (Performance Measurement)
Side view diagram of four stations
Standard Methods for Measuring Efficiency

## Slide 12: Testing (Performance Measurement)
The four areas (R1-R4) of each station (M2-M5) are all operating at nearly 100% efficiency.
All areas have an efficiency of over 99%, meeting the design goal.

## Slide 13: Testing (Performance Measurement)
μ：J/ψ→μ+μ−
k
p：Λ
The fitting results are used to calculate the sPlot weight for each event, so that the background can be subtracted in later analysis.

## Slide 14: Testing (Performance Measurement)
单击此处编辑母版文本样式
第二级
第三级
第四级
第五级
Use the sPlot technique on each sample to remove the combined background and get the pure signal distribution.
μ 集中在低值区，说明其 hit 与径迹预测匹配。
π/K 有更长的尾部，但低值区的小峰来自衰变-in-flight。
p 分布最靠右，误判率最低

## Slide 15: Testing (Performance Measurement)
ROC 曲线（μ 效率 vs. 强子误判率）
在 μ 效率 90% 处：
π 误判率 ≈ 0.4%（千分之四）
K 误判率 ≈ 0.6%（千分之六）
p 误判率 ≈ 0.05%（万分之五）
Performance is comparable to Run 2, meeting the Upgrade I target.

## Slide 16: Testing (Performance Measurement)
单击此处编辑母版文本样式
第二级
第三级
第四级
第五级
The dependence of muon efficiency and hadron misidentification rate on track momentum.
低动量 (p < 20 GeV/c)：
误判率较高（π ~2%）。
原因：多次散射严重。
高动量 (p > 50 GeV/c)：误判率降至 ‰ 级别。
μ 效率稳定在 >90%。
μ 效率在所有动量下均平稳（~90–95%）。

## Slide 17: Testing (Performance Measurement)
Test the effect of event pile-up (number of tracks per event) on μ identification performance at high brightness.
随着堆积增加（nLongTracks 从 0 到 >200），μ 效率几乎不变。
质子误判率有所上升（组合误判增加），但仍处于可接受水平。
证明了算法在高亮度环境下的稳定性。

## Slide 18: Testing (Performance Measurement)
Calculate the false alarm rate separately by region (R1–R4) and quadrant (Q1–Q4).
R1（最内层，靠近束流）：误判率最高（~1.5%）。
R2 显著下降，R3/R4 接近 0%。
没有明显的上‑下或左‑右不对称（四个象限一致）。

## Slide 19: Thank you