## Slide 1
CEPC AHCAL Energy Resolution
2025.6.26
李想
Notes: Today, I will present my work on improving the ECAL energy resolution using machine learning.

## Slide 2
AHCAL：
AHCAL Standalone Geometry Model:
Total Layers: 40 sampling layers.
Layer Components: Absorber, plastic scintillator tiles, and PCB.
Sensitive Area:720 × 720 mm² (populated by 324 scintillator tiles, each 40 × 40 × 3 mm³).
Absorber:20-mm-thick iron plate.
PCB:2-mm-thick G4_KAPTON.
Note: The absorber and PCB have the exact same area as the sensitive region.
Depth of the prototype ：5 λ
Notes: Let's briefly review the geometry of our AHCAL prototype. The system consists of 40 sampling layers. Each of these layers contains a 20-millimeter thick iron absorber plate, plastic scintillator tiles, and a 2-millimeter thick PCB. In total, the prototype reaches a depth of 5 lambda

## Slide 3
motivation：
Attempt to improve the HCAL
e- energy resolution using ML
Sim-to-Real Gap
strategy:
Hit level data: Train a CNN+LSTM
Using Transfer Learning
Option One for Data with position selecting
  Good match with MC_digi but small data volume
Option two for Data without position selecting
  Poor match with MC_digi but large data volume
Data with position selecting
Data without position selecting
cite Hong Bin's work
Notes: Our primary motivation is to improve the electron energy resolution of the HCAL using Machine Learning, specifically by bridging the 'Sim-to-Real' gap. We use hit-level data, trained CNN+LSTM. We explored two transfer learning options: Option One uses position-selected data, which matches the Monte Carlo simulation well but has a small data volume. Option Two uses data without position selecting, which has a poorer match but offers a much larger volume.The top plot shows Option One: Data with position selecting . The red experimental data points match the black 'MC digi' simulation curve quite well. However,the data volume is incredibly small. Compare that to the bottom plot, which shows Option Two: Data without position selecting . Here, the vertical axis jumps into the tens of thousands , giving us a massive data volume to work with. But the trade-off is obvious—the red data curve and the black simulation curve are significantly shifted and have a very poor match. These two figure was cited by Hong Bin's work.The difference caused by position selecting primarily comes from the saturation effects in the high and low gain channels.

## Slide 4
Cell different
Observation
Large data–MC_digi discrepancies are found in the central cells of the first 20 layers for energies above 30 GeV.
This region contains the highest information density of electromagnetic showers.
Impact
Models trained only on MC_digi learn an imperfect representation of the detector response.
This domain mismatch is a major factor limiting the energy-resolution improvement on real data.
100 GeV | Layer 7 | 18×18 cells
Notes: Our primary motivation is to improve the electron energy resolution of the HCAL using Machine Learning, specifically by bridging the 'Sim-to-Real' gap. We use hit-level data, trained CNN+LSTM. We explored two transfer learning options: Option One uses position-selected data, which matches the Monte Carlo simulation well but has a small data volume. Option Two uses data without position selecting, which has a poorer match but offers a much larger volume.The top plot shows Option One: Data with position selecting . The red experimental data points match the black 'MC digi' simulation curve quite well. However,the data volume is incredibly small. Compare that to the bottom plot, which shows Option Two: Data without position selecting . Here, the vertical axis jumps into the tens of thousands , giving us a massive data volume to work with. But the trade-off is obvious—the red data curve and the black simulation curve are significantly shifted and have a very poor match. These two figure was cited by Hong Bin's work.The difference caused by position selecting primarily comes from the saturation effects in the high and low gain channels.

## Slide 5
Transfer Learning Option One
MC (After digilization) : 1-120GeV e-(20000000) Continuous
Data without position selecting: from SPS [ 50.0, 60.0, 70.0, 80.0, 100.0, 120]GeV Uniformly mixed
Low-energy events produce fewer hits per event.
More events are therefore needed for effective training.
Additional MC_digi samples are allocated to the low-energy region.
As a result, the MC_digi dataset follows a trapezoidal event distribution.
Samples:
Not done
Notes: Here is a look at our Transfer Learning pipeline. We start by pretraining our models—the MLP, CNN-LSTM, and CNN-Transformer—on a massive dataset of 20 million continuous Monte Carlo events from 1 to 120 GeV After digilization without position selecting. In Stage 1, we freeze the backbone of the networks and train the attention and fully connected layers using selected-position MC data via Teacher Distillation. Finally, in Stage 2, we perform full fine-tuning using discrete experimental data.

## Slide 6
CNN+LSTM Trian (12000)
Input(hit level data):
HIt_ENERGY
Output:
  Predicted Energy
Samples: MC_truth
lr =1e-4
batch_size =256
epochs =150
weight_decay =1e-4
optimizer ="adamw"
Input and Output（rellative error <2%）
Samples:
MC_truth: 1-120GeV (2000000) Continuous e-
Data split
train_frac = 0.7
val_frac = 0.15
test_frac = 0.15
CNN (Convolutional Neural Network)
LSTM (Long Short-Term Memory)
Read the hit image of the super layer
Learn the development of shower at different levels
Notes: We used a CNN+LSTM architecture. The CNN Read the hit image of the super layer, and the LSTM learns development of shower at different levels.
.

## Slide 7
CNN+LSTM Result_Energy Resolution
Samples: MC_truth
Samples: MC_digi
Notes: These slide show the CNN+LSTM Result_Energy Resolution
The the top graph plots Energy Resolution. The blue line with circles is our MC_digi —this is our digitized . The green line with triangles is test beam data. Calculated by SUM E. The red line with squares represents digi_predict, which is the model's prediction on the simulated data. The orange line with diamonds is the data_predict, representing our model's prediction on thetest beam data after transfer learning. The bottom graph plots the resolution residual, or the relative difference, against the energy.The red line shows the relative difference between the predicted simulation and the baseline simulation.The orange line plots the relative improvement of our predicted data against the raw data. In summary,After applying transfer learning, the CNN+LSTM model improved the energy resolution of the test beam data by approximately 30%.

## Slide 8
Learn data mode
Inverse function to correct electronic non-linearity
Spline Plugin
Apply electronic non-linearity
Apply Spline Plugin
Frozen CNN+LSTM :Cell Calibration Fine-tuning
Notes: These slide show the CNN+LSTM Result_Energy Resolution
The the top graph plots Energy Resolution. The blue line with circles is our MC_digi —this is our digitized . The green line with triangles is test beam data. Calculated by SUM E. The red line with squares represents digi_predict, which is the model's prediction on the simulated data. The orange line with diamonds is the data_predict, representing our model's prediction on thetest beam data after transfer learning. The bottom graph plots the resolution residual, or the relative difference, against the energy.The red line shows the relative difference between the predicted simulation and the baseline simulation.The orange line plots the relative improvement of our predicted data against the raw data. In summary,After applying transfer learning, the CNN+LSTM model improved the energy resolution of the test beam data by approximately 30%.

## Slide 9
Learn data mode
Data without position selecting: from SPS [ 50.0, 60.0, 70.0, 80.0, 100.0, 120]GeV Uniformly mixed
Every Energy point: 100000 sample
Dep_Energy_error: steadily decreasing
Model learns to compensate for cell-by-cell discrepancies between data and MC_digi:
Notes: These slide show the CNN+LSTM Result_Energy Resolution
The the top graph plots Energy Resolution. The blue line with circles is our MC_digi —this is our digitized . The green line with triangles is test beam data. Calculated by SUM E. The red line with squares represents digi_predict, which is the model's prediction on the simulated data. The orange line with diamonds is the data_predict, representing our model's prediction on thetest beam data after transfer learning. The bottom graph plots the resolution residual, or the relative difference, against the energy.The red line shows the relative difference between the predicted simulation and the baseline simulation.The orange line plots the relative improvement of our predicted data against the raw data. In summary,After applying transfer learning, the CNN+LSTM model improved the energy resolution of the test beam data by approximately 30%.

## Slide 10
Summary
Biggest issue: Sim-to-Real Gap
Without transfer learning : the model successfully improves the energy resolution on simulations, but we see no improvement on the test beam data.
Without transfer learning : the model might over-optimize on a few specific discrete energy points, which destroys the continuity of the model's predictions across the entire energy spectrum.
Next step
Update CNN+LSTM and Transfer learning.