## Slide 1: Touschek lifetime optimization at Super C-Tau factory in Novosibirsk
A. Bogomyagkov
BINP, Russia
The 2024 International Workshop on Future Tau Charm Facilities (FTCF2024)
University of Science and Technology of China (USTC), Hefei, China
14 – 18 January, 2024

## Slide 2: Facility overview
1.5 – 3.5 GeV e-e+

## Slide 3: Crab waist (P.Raimondi 2006)
z
e
x
Li
+
e
-
2x
2z
 ∙x

Luminosity
Large Piwinski angle:
Transverse beam separation in parasitic IPs
  distance between bunches is not limited by beam-beam
Interaction area length
  no hour-glass
CRAB waist (CRAB sextupoles) suppresses betatron and synchro-betatron resonances
Notes: mux=3pi*2, muy=2.5pi*2

## Slide 4: Design parameters for
E(MeV) | 1500 | 2000 | 2500 | 3000 | 3500
(m) | 935.874 |  |  |  | 
(MHz) | 350 |  |  |  | 
(mrad) | 60 |  |  |  | 
(mm) | 100/1 |  |  |  | 
(%) | 0.5 |  |  |  | 
I(A) / | 2.9 / 941 | 2.7 / 983 | 2.5 / 983 | 2.7 / 983 | 2.9 / 974
 | 6 | 5.3 | 5 | 5.3 | 5.8
(keV) | 91 | 288 | 504 | 820 | 1266
(kV) | 1500 | 2000 | 3000 | 3900 | 5000
 | 0.0153 | 0.0152 | 0.0166 | 0.0172 | 0.018
(%) | 1.98 | 1.83 | 1.97 | 1.97 | 1.98
(SR/IBS+WG) | 0.27/1.1 | 0.36/1.2 | 0.5/1.2 | 0.5/1.2 | 0.6/1.3
(mm) (SR/IBS+WG) | 3.6/14 | 4.7/15 | 6/14 | 7/14 | 8/14
(nm) (SR/IBS+WG) | 2.0/6.4 | 3.5/3.8 | 5.5/3.2 | 7.9/4.1 | 11/5.7
 | 1 | 1 | 1 | 1 | 1
 | 0.005/0.12 | 0.003/0.1 | 0.002/0.08 | 0.002/0.065 | 0.002/0.05
(s) | 125 | 208 | 302 | 560 | 1100
(s) | 3500 | 3200 | 3000 | 3200 | 3500
E(MeV) | 1500 | 2000 | 2500 | 3000 | 3500
 | 935.874 |  |  |  | 
 | 350 |  |  |  | 
 | 60 |  |  |  | 
 | 100/1 |  |  |  | 
 | 0.5 |  |  |  | 
 | 2.9 / 941 | 2.7 / 983 | 2.5 / 983 | 2.7 / 983 | 2.9 / 974
 | 6 | 5.3 | 5 | 5.3 | 5.8
 | 91 | 288 | 504 | 820 | 1266
 | 1500 | 2000 | 3000 | 3900 | 5000
 | 0.0153 | 0.0152 | 0.0166 | 0.0172 | 0.018
 | 1.98 | 1.83 | 1.97 | 1.97 | 1.98
 | 0.27/1.1 | 0.36/1.2 | 0.5/1.2 | 0.5/1.2 | 0.6/1.3
 | 3.6/14 | 4.7/15 | 6/14 | 7/14 | 8/14
 | 2.0/6.4 | 3.5/3.8 | 5.5/3.2 | 7.9/4.1 | 11/5.7
 | 1 | 1 | 1 | 1 | 1
 | 0.005/0.12 | 0.003/0.1 | 0.002/0.08 | 0.002/0.065 | 0.002/0.05
 | 125 | 208 | 302 | 560 | 1100
 | 3500 | 3200 | 3000 | 3200 | 3500
SuperKEKB 2020
PEPII: I(e+)=3.2 A PEPII
DAFNE : I(e-)=2.45A
SuperKEKB:
Notes: 68_1, q=1093, I(e+)=3.2 A PEPII, I(e-)=2.45A DAFNE, L=2.1e34 KEKB

## Slide 5: Straight and Arc sections
Straight
Arc: FODO 90 cells
Notes: Arcs: 24 x and 24 y pairs of interleaved pairs of sextupoles

## Slide 6: Siberian Snake
The goal is to provide longitudinal polarization at IP
To decouple , 7 quadrupoles needed
Solenoid spin rotation angle is , at ,
IP
SS1
SS3
SS2
120
120
120
Notes: The total length is 33 m, adding 100 m to circumference.

## Slide 7: Interaction region 1
CRAB:
K.Oide FCC-ee
Notes: 54-1: crab at mux=3pi*2, muy=2.5pi*2, taux=0.3 s ->(wiggler) ->0.049 s

## Slide 8: CRAB sextupole influence on 6d DA, E=1.5 ГэВ
GeV | CRAB=100% | CRAB=0% | CRAB=25% | CRAB=50% | CRAB=100%
(s) | 34 | 265 | 255 | 240 | 230
 | CRAB=100% | CRAB=0% | CRAB=25% | CRAB=50% | CRAB=100%
 | 34 | 265 | 255 | 240 | 230
Notes: 54_1, 2021.06.17-13.08.03_sextupole_chrom-14.str

## Slide 9: CRAB sextupole influence: 5d-DA
4d, on momentum
5d, , CRAB ON
5d, , CRAB OFF
Why do CRAB sextupoles reduce 5d DA?!
Notes: 49-5: 2020.10.11-22.59.05_sextupole_chrom-5.str

## Slide 10: CRAB sextupole influence: detuning
 | CRAB ON | CRAB OFF
 | CRAB ON | CRAB OFF
CRAB sextupoles introduces humongous chromatic detuning!
Notes: 49_5, call,file="../2020.10.11-22.59.05_sextupole_chrom-5.str";

## Slide 11: 4d-DA study
4d DA is limited by CRAB sextupole and fringe fields and their interference
Notes: 49_6 (49_5), k2_lcrab = 24.2061222750197

## Slide 12: Optimization of the final doublet
Lattice | 49_5 | 54_1 | 55_1
L(Q0,d1,Q1) | 0.2, 0.3, 0.3 | 0.5, 0.44, 0.5 | 0.5, 0.45, 0.5
 | 20,20 |  | 
/(mm) | 100 / 1 |  | 
(m) |  |  | 
FRINGE OFF |  |  | 
FRINGE ON |  |  | 
Lattice | 49_5 | 54_1 | 55_1
L(Q0,d1,Q1) | 0.2, 0.3, 0.3 | 0.5, 0.44, 0.5 | 0.5, 0.45, 0.5
 | 20,20 |  | 
 | 100 / 1 |  | 
FRINGE OFF |  |  | 
FRINGE ON |  |  | 
L*
Q0
d1
Q1
IP
For the first final focus quadrupole, with , ,
Notes: call,file="../2020.10.11-22.59.05_sextupole_chrom-5.str";

## Slide 13: 4d-DA: optimization
49_5
54_1
55_1
Notes: 49_6, k2_lcrab = 24.2061222750197; 54_1, k2_lcrab = 19.7885218159168; 55_1, k2_lcrab = 15.6466891406201

## Slide 14: Which quad fringe is the strongest?
Starting from IP (two quadrupoles, four edges)
The second and the third
First edge
from IP
Second edge from IP
L*
Q0
d1
Q1
IP
Notes: 54_1, the whole input

## Slide 15: 6d DA, no damping
CRAB=100%
Notes: 54_1, 2021.09.16-20.22.30_1.0crab_sextupole_chrom-15.str

## Slide 16: Conclusion Interaction region 1
On momentum dynamic aperture is sufficient for injection and beam-beam effects
Off momentum dynamic aperture with CRAB ON is insufficient at 1.5-2.5 GeV to provide necessary Touschek lifetime
Optimization of final quadrupoles is possible

## Slide 17: Interaction region 2 (CCY, CCX, CRAB)
CRAB:
Notes: 57-2

## Slide 18: CRAB sextupole influence: 6d-DA
Observation 1:
addition of CCSX increased
energy aperture from
[-0.8;+1.1] to [-1.2;+1.6]
Observation 2: linear map between CRAB sextupoles
changes with ;
therefore, CRAB sextupoles reduce 6d DA
For aberration cancelation
,
Notes: 57-2: 2021.11.02-05.22.48_1.0crab_sextupole_chrom-4.str

## Slide 19: Conclusion Interaction region 2
Energy aperture is slightly larger
Large transport matrix (and) variation with respect to  between CRAB sextupoles
Is it possible to minimize transport map variation between crab sextupoles?
  What if we let at crab sextupoles vary with identically, and try to keep phase advance the same?

## Slide 20: Interaction region 3
CRAB:
Notes: 60

## Slide 21: Map between CRAB sextupoles comarision
IR 2
IR 3
Significantly smaller variation of r11, r22, r12, r21 with !
Notes: 60, 2021.12.21-08.21.09_1.0crab_sextupole_chrom-3.str. 57-2: 2021.11.02-05.22.48_1.0crab_sextupole_chrom-4.str

## Slide 22: Twiss functions between CRAB sextupoles
varies with  identically at left and right CRAB sextupoles
changes with  by and
Notes: 60, 2021.12.21-08.21.09_1.0crab_sextupole_chrom-3.str

## Slide 23: 6d DA for Interaction region 3
GeV | CRAB=100% | CRAB=60% | CRAB=0%
(s) | 63 | 126 | 280
 | CRAB=100% | CRAB=60% | CRAB=0%
 | 63 | 126 | 280
Energy aperture
Interaction region 1: , s
Interaction region 2:
Interaction region 3: , s
Why do CRAB sextupoles reduce 6d DA?!
Notes: 60, 2021.12.21-08.21.09_1.0crab_sextupole_chrom-3.str

## Slide 24: Local momentum aperture (CRAB is ON)
Notes: 60, 2021.12.21-08.21.09_1.0crab_sextupole_chrom-3.str

## Slide 25: Local momentum aperture (CRAB is OFF)
Why do CRAB sextupoles reduce 6d DA?!
Notes: 60, 2021.12.21-08.21.09_1.0crab_sextupole_chrom-3.str

## Slide 26: 6d scans of XY dynamic aperture
CRAB is ON
CRAB is OFF
Notes: 60: 2021.12.14-09.34.53_1.0crab_sextupole_chrom-4.str

## Slide 27: 6d scans: close-up XY aperture with
Theory of distortion functions (new invariant action as a function of the old action) prediction agrees with tracking for
DA:
Does not agree for . It means that at DA is limited not by the 1st order sextupoles.
Off momentum distortion functions are created by CRAB sextupoles, and are 20 times larger than the rest of sextupoles
Notes: 60, 2021.12.14-09.34.53_1.0crab_sextupole_chrom-4.str

## Slide 28: Touschek lifetime with CRAB ON and OFF at 2 GeV
GeV | CRAB OFF | CRAB ON
 | CRAB OFF | CRAB ON
GeV | CRAB OFF | CRAB ON
 | CRAB OFF | CRAB ON

## Slide 29: Conclusion Interaction region 3
Placing CRAB sextupoles close to IP gave the largest energy aperture
  Interaction region 1: , s at 1.5 GeV
  Interaction region 2:
  Interaction region 3: , s at 1.5 GeV, the smallest variation of transport map (and ) with 
But still not sufficient for Touschek lifetime at 1.5, 2 GeV with CRAB sextupole 100%, sufficient with CRAB sextupole OFF
Optimization of FF quadrupoles decreased fringe field effects
Strong 6d DA degradation with CRAB sextupole strength is explained by transport map variation with 

## Slide 30: Interaction region 4
CRAB:
Additional sextupoles in –I pairs
Four 90 cells
Notes: v. 68

## Slide 31: Lattice and layout

## Slide 32: 6d DA for Interaction region 4
GeV | CRAB=100% | CRAB=60% | CRAB=0%
(s) | 125 | 104 | 118
 | CRAB=100% | CRAB=60% | CRAB=0%
 | 125 | 104 | 118
Energy aperture
Interaction region 1: , s
Interaction region 2:
Interaction region 3: , s
Interaction region 4: , s
Sextupoles:
IR: 5(Y) + 8(X)
ARCS: 24(Y)+24(X)
Octupoles:
IR: 2(Y)+2(X)
Notes: 68, 2022.10.08-19.03.53_1.0crab_sextupole_chrom-13.str

## Slide 33: Design parameters for
E(MeV) | 1500 | 2000 | 2500 | 3000 | 3500
(m) | 935.874 |  |  |  | 
(MHz) | 350 |  |  |  | 
(mrad) | 60 |  |  |  | 
(mm) | 100/1 |  |  |  | 
(%) | 10 | 0.5 | 0.5 | 0.5 | 0.5
I(A) | 2.9 | 1.64 | 2.5 | 2.7 | 2.9
 | 6 | 3.25 | 5 | 5.3 | 5.8
/ q | 941/1093 | 983/1093 | 983/1093 | 983/1093 | 974/1093
(keV) / (kV) | 91 / 750 | 288 / 2000 | 504 / 3000 | 820 / 3900 | 1266 / 5000
 | 0.0108 | 0.0152 | 0.0166 | 0.0172 | 0.018
(%) | 1.3 | 1.83 | 1.97 | 1.97 | 1.98
(SR/IBS+WG) | 0.27/0.9 | 0.36/1.1 | 0.5/1.2 | 0.5/1.2 | 0.6/1.3
(mm) (SR/IBS+WG) | 3.6/17 | 4.7/15 | 6/14 | 7/14 | 8/14
(nm) (SR/IBS+WG) | 2.0/2.9 | 3.5/3.5 | 5.5/3.2 | 7.9/4.1 | 11/5.7
 | 0.29 | 0.4 | 1 | 1 | 1
 | 0.003/0.03 | 0.002/0.06 | 0.002/0.08 | 0.002/0.065 | 0.002/0.05
(s) | 304 | 304 | 302 | 560 | 1100
(s) | 12000 | 5000 | 3000 | 3200 | 3500
E(MeV) | 1500 | 2000 | 2500 | 3000 | 3500
 | 935.874 |  |  |  | 
 | 350 |  |  |  | 
 | 60 |  |  |  | 
 | 100/1 |  |  |  | 
 | 10 | 0.5 | 0.5 | 0.5 | 0.5
I(A) | 2.9 | 1.64 | 2.5 | 2.7 | 2.9
 | 6 | 3.25 | 5 | 5.3 | 5.8
 | 941/1093 | 983/1093 | 983/1093 | 983/1093 | 974/1093
 | 91 / 750 | 288 / 2000 | 504 / 3000 | 820 / 3900 | 1266 / 5000
 | 0.0108 | 0.0152 | 0.0166 | 0.0172 | 0.018
 | 1.3 | 1.83 | 1.97 | 1.97 | 1.98
 | 0.27/0.9 | 0.36/1.1 | 0.5/1.2 | 0.5/1.2 | 0.6/1.3
 | 3.6/17 | 4.7/15 | 6/14 | 7/14 | 8/14
 | 2.0/2.9 | 3.5/3.5 | 5.5/3.2 | 7.9/4.1 | 11/5.7
 | 0.29 | 0.4 | 1 | 1 | 1
 | 0.003/0.03 | 0.002/0.06 | 0.002/0.08 | 0.002/0.065 | 0.002/0.05
 | 304 | 304 | 302 | 560 | 1100
 | 12000 | 5000 | 3000 | 3200 | 3500
Notes: 68_1, q=1093, I(e+)=3.2 A PEPII, I(e-)=2.45A DAFNE, L=2.1e34 KEKB

## Slide 34: Conclusion
Interaction region 4 gives the highest Touschek life time
  GeV, s, ,
  GeV, s, ,
Optimization of FF quadrupoles worked
Minimization of -invariant worked
Minimization of transport map variation between CRAB sextupoles worked