## Slide 1: Trigger System R&D in Super Tau-Charm Facility
Zhujun Fang
State Key Laboratory of Particle Detection and Electronics
University of Science and Technology of China
On behalf of STCF Trigger Working Group
17/1/2024

## Slide 2: Outline
STCF overview and requirement for trigger system
STCF trigger system preliminary design
L1-level trigger algorithm R&D
L1-level FPGA-based hardware platform R&D
Summary

## Slide 3: Outline
STCF overview and requirement for trigger system
STCF trigger system preliminary design
L1-level trigger algorithm R&D
L1-level FPGA-based hardware platform R&D
Summary

## Slide 4: STCF overview
400 m linear accelerator
800 m storage ring
100 m damping ring
Detector spectrometer
Super Tau-Charm Facility:
A new generation of high-luminosity electron-positron collider
Center-of-mass energy: 2-7 GeV
Peak luminosity: >0.5×1035 cm-2s-1 at 4 GeV
Collision data: more than 1 ab-1/y
With potential to further increase luminosity and beam polarization

## Slide 5: Requirements for trigger system
High luminosity in STCF synchronous generates:
High physics event rate: over 400 kHz
Large data size: over 200 GB/s raw data
High background: ~ 400 kHz/channel in MDC
~ 1 MHz/channel in ECAL
Trigger system:
Identifying physics events from massive background
Reducing the pressure in data acquisition and transmission
Maintain the long-term stable operation of experiment
Requirements for trigger system in STCF
Very high physics event trigger efficiency (>99%)
Good background suppression capability
Low latency
High trigger rate (~ 1 MHz)
Distinguish of multi-physics events in 1 trigger window

## Slide 6: Outline
STCF overview and requirement for trigger system
STCF trigger system preliminary design
L1-level trigger algorithm R&D
L1-level FPGA-based hardware platform R&D
Summary

## Slide 7: STCF trigger system preliminary design
Two-stage trigger system:
L1-level Trigger:
Identifying physics events window
Based on FPGA platform
Latency ~ 5 μs
High Level Trigger (HLT):
Suppressing backgrounds in each time window
Based on server cluster

## Slide 8: Preliminary design of L1-level trigger
ITK: high background
MDC: key tracking detector
RICH: complex Cherenkov ring reconstruction
DTOF: auxiliary in Endcap
ECAL: key calorimeter, fast response
MUON: auxiliary for μ/π/n/KL

## Slide 9: Outline
STCF overview and requirement for trigger system
STCF trigger system preliminary design
L1-level trigger algorithm R&D
L1-level FPGA-based hardware platform R&D
Summary

## Slide 10: STCF MDC design
Baseline design:
48 layers of small cell
8 superlayers
1,4,7,8 superlayers are axial layers
33.4 deg
20 deg
Region division:
Barrel: 33.4 deg – 90 deg
Endcap: 20 deg – 33.4 deg

## Slide 11: MDC sub-trigger R&D
XY 2D tracking and reconstruction
Track segment (TS) pattern configuration
3 types of TS module
Un-identification of high-pt track in Endcap
3 hits tracking as a complement to 4 hits tracking
Further optimization is needed
Short track tagging
Un-reconstructed short track will be sent to GTL with related TS information
Suppressing long track background
Distinguish of cross tracks

## Slide 12: MDC sub-trigger R&D
3D reconstruction
Multi-layer fully connected neural network (MLP)
Input: Track segment numbers and TDC timing for 8 superlayers
Output: Reconstructed Z-position in various pt regions

## Slide 13: MDC sub-trigger performance
Relationship between track pt and σZ
Chart: Track pt (GeV/c)
| 0.22500000000000001 | 0.27500000000000002 | 0.32500000000000001 | 0.4 | 0.52500000000000002 | 0.8 | 1.25 | 2
 | 2.0377 | 2.0747 | 2.0943 | 2.0469 | 1.8387 | 1.332 | 0.96643 | 0.76253
MDC tracking efficiency to typical charged physics processes
Trigger: Ntracking ≥ 2，Nrec ≥ 1
mm
mm
Typical good reconstructed and puzzle events

## Slide 14: STCF ECAL design
Baseline design:
Barrel: 51 circles of pCsI crystal
Endcap (each): 10 circles of pCsI crystal
Trigger Cell (TC) setting:
Barrel (4×4 or 3×4):
51 circles × 132 crystal
429 TC in total
Each Endcap (3×5 or 4×5):
10 circles
  3 circles × 85 crystal => 3×5 divided
  3 circles × 105 crystal => 3×5 divided
  4 circles × 130 crystal => 4×5 divided
64 TC in total

## Slide 15: ECAL sub-trigger R&D
Time (ns)
Ratio
Time V.S. energy collection ratio
Single particle ECAL response:
Deposit energy V.S. momentum
Background level simulation:
1 μs time window for trigger
1 MeV TC signal threshold
ECAL background TC response distribution

## Slide 16: ECAL sub-trigger R&D
Time window
Signal mixed with background
Pure signal
Signal cluster
Rec. cluster
Cluster reconstruction:
Limit time window by T-Q map
Find the rec. cluster in TC map
Background energy distribution in each 12.5 ns bin
Counts
Bkg energy in ECAL (GeV)
Sig/bkg distinguish threshold
Basic parameters setting:
T-Q map bin width: 12.5 ns
S/B threshold: 210 MeV
Cluster energy threshold: 35 MeV

## Slide 17: ECAL sub-trigger performance
Polar angle = 90 deg
p= 400 MeV/c
Single particle trigger efficiency
ECAL trigger efficiency to typical charged physics reaction
Reaction | J/ψ->ee | J/ψ->mumu | charm_meson physics | Hyperon physics | τ-pair
Filter | N≥2 | N≥2 | N≥3 | N≥3 | N≥2
Efficiency | 99.40% | 98.20% | 98.70% | 95.60% | 98.50%
Counts
Counts
Time (ns)
Time (ns)
MC truth: 200 ns
MC truth: 100 ns
Distinguish of multi-physics events in 1 trigger window

## Slide 18: L1-level GTL R&D
GTL logic framework design
GTL algorithm realization & optimization
Trigger table design
L1-level trigger performance evaluation

## Slide 19: Preliminary trigger table
Trigger table
Cover 7 types of physics events of interest and typical background (RBB…)
Having 20 trigger parameters and 13 trigger channel
Trigger channel merge is planed in next step
Key parameters
MDC: Track No./(pt)
EMC: Eth1,2,3/Cluster No./Balance
Match: back-to-back/Track No.
Un-match: TS & TC

## Slide 20: L1-level trigger performance
Physics reaction | No. of charged track | No. of MC charged track in spec. | Signal mixed with background |  |  | 
反应类型 | 带电末态数 | 进入谱仪带电径迹 | No. of MDC track | No. of ECAL cluster | No. of MDC-EMC match | Trigger eff.
e+e- -> π+π-Jpsi Jpsi -> e+e- | 4 | 3.67 | 3.41 | 3.47 | 2.32 | 99.6%
e+e- -> π+π-Jpsi Jpsi -> μ+μ- | 4 | 3.65 | 3.39 | 3.33 | 2.40 | 98.7%
e+e- -> π+π-Jpsi Jpsi -> Λ Jpsi -> Ξ | 6, 8 | 4.10 | 4.12 | 6.43 | 3.28 | 99.3%
e+e- -> D0 e+e- -> D+ D- e+e- -> Ds+ Ds- | 2, 4, 6, (8) | 6.35 | 5.04 | 4.96 | 2.54 | 99.8%
e+e- -> τ+ τ- | 2 | 1.90 | 1.96 | 2.31 | 1.70 | 96.8%
V2 background | / | / | ~1.2 | 1.52 | 0.81 | 11.1%
Physics reaction | No. of charged track | No. of MC charged track in spec. | Signal mixed with background |  |  | 
反应类型 | 带电末态数 | 进入谱仪带电径迹 | No. of MDC track | No. of ECAL cluster | No. of MDC-EMC match | Trigger eff.
e+e- -> π+π-Jpsi Jpsi -> e+e- | 4 | 3.67 | 3.41 | 3.47 | 2.32 | 99.6%
e+e- -> π+π-Jpsi Jpsi -> μ+μ- | 4 | 3.65 | 3.39 | 3.33 | 2.40 | 98.7%
 | 6, 8 | 4.10 | 4.12 | 6.43 | 3.28 | 99.3%
 | 2, 4, 6, (8) | 6.35 | 5.04 | 4.96 | 2.54 | 99.8%
e+e- -> τ+ τ- | 2 | 1.90 | 1.96 | 2.31 | 1.70 | 96.8%
V2 background | / | / | ~1.2 | 1.52 | 0.81 | 11.1%
L1-level trigger efficiency to typical charged physics reaction
Key points
High background pass rate
MDC-Endcap efficiency improving
GTL-neutral particle identifying and utilization
Processing of 2-particle final state reactions

## Slide 21: Outline
STCF overview and requirement for trigger system
STCF trigger system preliminary design
L1-level trigger algorithm R&D
L1-level FPGA-based hardware platform R&D
Summary

## Slide 22: FPGA-based evaluation board test
Evaluation board equipped with an XCKU060-FFVA 1156-2 FPGA
Track segment trigger efficiency in FPGA evaluation board
Latency measured in FPGA evaluation board
The MDC sub-trigger 2D algorithm is tested on a FPGA-based evaluation board.

## Slide 23: L1-level trigger prototype design
Simulation data generator: 1 server & 12 PCIe
MDC sub-trigger: 3×CROB-ST，1×CROB-LTU
ECAL sub-trigger: 1×CROB-ST，1×CROB-LTU
GTL: 1×CROB-GTU，1×Fan-out

## Slide 24: FPGA-based hardware platform R&D
ATCA 6U chassis
CROB-LTU board
CROB-LTU board test
Function module design of CROB-LTU board
Notes: 确定FPGA、DDR4、FMC+选型设计
研制第一版CROB-LTU板卡
CROB-LTU板卡测试

## Slide 25: Outline
STCF overview and requirement for trigger system
STCF trigger system preliminary design
L1-level trigger algorithm R&D
L1-level FPGA-based hardware platform R&D
Summary

## Slide 26: Summary
The preliminary design of STCF trigger system is illustrated:
Trigger logic & framework
MDC sub-trigger algorithm
ECAL sub-trigger algorithm
Key performance parameters simulation & test:
Trigger efficiency to typical charged physics channel: 99% (2-particle final state reactions 96%)
Background trigger rate: 11.1% (~ 110 kHz)
MDC 2D algorithm latency: 350 ns
Future work:
Background suppression
Algorithm & trigger table optimization
HLT R&D
GTL design and algorithm
Trigger prototype design
CROB-LTU board design

## Slide 27: Thanks for your attention!

## Slide 28: Back up
MDC background distribution in 1 sampling window
ECAL background distribution in 1 sampling window
Count
Count
MDC and ECAL background

## Slide 29: Back up
Time V.S. deposit energy in whole EMC
Time V.S. deposit energy in whole EMC
σt = 5 ns
σt = 20 ns
ECAL online time resolution contributions

## Slide 30: Back up
GeV
GeV
Signal distribution
Signal and background distribution
Time V.S. deposit energy in whole EMC
ECAL response to low energy deposition event

## Slide 31: Back up
Transverse momentum of final state particle in hyperon physics

## Slide 32: Back up
Detected final state particle distribution in tau-pair physics events

## Slide 33
MDC
ECAL
MUON
Other detectors
Pipeline memory
Global Trigger
Logic
(Hardware)
Track
Shower: energy and multiplicity
Sub-trigger:
position, t
Sub-trigger: position, t, E
RU/
CROB-PXI
Pipeline memory
Pipeline memory
Pipeline memory
L1 accept
Software trigger
CROB-PCIe
ROS/EB
Data recording
HLT accept
400 kHz
RU/
CROB-PXI
RU/
CROB-PXI
RU/
CROB-PXI
CROB-PCIe
CROB-PCIe
CROB-PCIe

## Slide 34
MDC
ECAL
MUON
Other detectors
Pipeline memory
Global Trigger
Logic
(Hardware)
Track
Shower: energy and multiplicity
Sub-trigger:
position, t
Sub-trigger: position, t, E
RU/
CROB-PXI
Pipeline memory
Pipeline memory
Pipeline memory
L1 accept
Software trigger
CROB-PCIe
ROS/EB
Data recording
HLT accept
400 kHz
RU/
CROB-PXI
RU/
CROB-PXI
RU/
CROB-PXI
CROB-PCIe
CROB-PCIe
CROB-PCIe
DTOF
Pipeline memory
RU/
CROB-PXI
CROB-PCIe

## Slide 35
MDC Sub-trigger
ECAL Sub-trigger
DTOF Sub-trigger
MUON Sub-trigger
XY 2D tracking and reconstruction
3D reconstruction
Time reconstruction
Cluster reconstruction
and pattern analysis
Energy and balance analysis
Event time reconstruction
Trigger & time reconstruction
Long track reconstruction
Neutral hadron identification
L1-level GTL

## Slide 36
MDC data extract
MDC parameter solve
GTL_MDC_parameters
ECAL data extract
ECAL parameter solve
GTL_ECAL_parameters
MDC back-to-back
ECAL back-to-back
MDC-ECAL match
GTL_BackToBack Desicion
ECAL balance
GTL_ECAL_Balance
GTL_Decision
Trigger channels definition
Trigger efficiency evaluation
MC simulation data
Event filter
GTL_Match_parameters