## Slide 1: RICH Simulation and Reconstruction Algorithm
Binlong Wang Huibin Zhang Qian Liu
Qingyuan Huang Shiping Chen Wenqian Huang
University of Chinese Academy of Sciences
FTCF2024，Hefei

## Slide 2
Contents
Introduction
DLL Algorithm
StandAlone Simulation
Work in OSCAR
Conclusion

## Slide 3
PIDB, 12 modules
located between MDC and EMC
RICH in STCF

## Slide 4
Wide range of momentum distribution
  being up to 7 GeV , PID up to 2GeV
  Low momentum region (< 0.6 GeV/c) covered by dE/dx measurement
  Cherenkov-based technology
Compact (< 20 cm) and limited material budget (< 0.3 )
  difficult to find optical focusing method
Large solenoid angle coverage
PID Requirements

## Slide 5
~10 photonelectron
Cherenkov distribution
Deformed distribution in different kinematic regions
Cherenkov Ring with seperated branches in some cases
Hit on anode
θ=90°
2GeV/c
θ=45°
2GeV/c
liquid Radiator
Anode
Anode
Cherenkov dist.
Quartz

## Slide 6
Delta-Log-Likelihood Algorithm
For each partical hypothesis h , log-likelihood defined as
do seperation by figure out delta-log-likelihood
and generated offline
To speed up the program , only pixels with included in calculation
:photoelectron number received by anode pixel i
:photoelectron number expected to received by anode pixel i for particle hypothesis h
:background photonelectron number expected to received by anode pixel i

## Slide 7
In geant4
GeV/c , deg,
Background level: 10-3 hit / (pixel · time window)
mis-ID rate < 1% , PID efficiency > 98% mostly
Deformed Cherenkov distribution makes PID performance worse
Standalone Simulation
θ=45°
2GeV/c
θ=60°

## Slide 8
  Normal anode readout:
    Granularity: mm2
      43200 pixels 12 modules
      too many channels, expensive
    Granularity: mm2
      Low PID efficiency @ 2GeV/c
  Encoding anode readout:
    Granularity remains mm2
    Specific pixels share same electronic channels,
      decode the fired pattern to locate hit position
    ~20% Front end electronics less cost
    PID efficiency remain 98％ mostly @ 10-3 background level
  Encoding Readout in Standalone Simulation
θ=
Notes: 做下图为与束流夹角为70度情况下模拟给出π、k、p中π鉴别成功的概率；含1.35^-3的本底。

## Slide 9
Migration to OSCAR
Standalone simulation:
  Generate Cherenkov distribution in geant4
  Cherenkov distribution in part of kinematic region
  98% separation
OSCAR:
  Generate Cherenkov distribution database by numerical calculation
    faster than geant4 simulation
    same result
  Database: ~7M Cherenkov distribution image for different particles
  > 96％ separation
    use RecExtTrack to improve PID performance
    translate or interpolate Cherenkov distribution

## Slide 10
Convolutional Neural Networks
CNN used
  Pro
  PID efficiency ~ similar level of likelihood method.
  Highly accelerate the execution time to 1evt/2ms (1 2080Ti).
  Con
  Only take fixed-size images , lack of track information
Disadvantages of DLL algorithm
  Slow calculation:
  Frequently database access
  Too many Poisson likelihood calculated
  Data-MC agreement is highly required
Kaon hit
Pion hit

## Slide 11
Graph Neural Networks
> 95％ when the training sample size > 4000

## Slide 12
Conclusion
RICH satisfy STCF PID requirement: 98％ separation @ 2GeV/c
Algorithm | Expected PID efficiency | Note
DLL (standalone) | >98% | Need Cherenkov distribution as database Uniform distribution background
DLL (OSCAR) | >96% | Attempt to use RecExtTrack to improve PID performance
CNN | ～99% | Large memory consumption Unable to use track information
GNN |  | Start a trail
Future Plan:
optimize DLL algorithm
More simulation under OSCAR framework
Continue to work on neural network algorithm

## Slide 13
Backup
θ=90°
θ=60°

## Slide 14
Backup
PID efficience decrease with the Cherenkov Ring deformed
θ=40°
θ=50°